THEMIS-ARTEMIS

Administrator’s Guide

thm_soc_122

May 4, 2012

# Document Revision Record

| Rev. | Date | Description of Change | Approved By |
| --- | --- | --- | --- |
| - | 3/7/2007 | Draft | - |
|  | 3/7/2011 | v6.0 changes |  |
|  | 3/7/2012 | V7.0 changes |  |

# Distribution List

| Name | Email |
| --- | --- |
| Jim Lewis, U.C. Berkeley | jwl@ssl.berkeley.edu |
| Dr. Jim McTiernan, U.C. Berkeley | jimm@ssl.berkeley.edu |
| Pat Cruce, UCLA | pcruce@igpp.ucla.edu |
| Dr. Vassilis Angelopoulos, U.C. Berkeley | vassilis@ssl.berkeley.edu |
| David King, U.C. Berkeley | dking@ssl.berkeley.edu |
| Aaron Flores, UCLA | floresaa@igpp.ucla.edu |
| Lydia Philpott, UCLA | lphilpott@igpp.ucla.edu |
| Ben Sadeghi, U.C. Berkeley | bsadeghi@ssl.berkeley.edu |

# TBD List

| Identifier | Description |
| --- | --- |

Table of Contents

Document Revision Record	2

Distribution List	2

TBD List	2

1.	Introduction	16

1.1	Purpose	16

1.2	Applicable Documents.	16

2.	Data Processing Overview	17

2.1	Overview	17

3.	Probe Data Processing Activities	21

3.1	Virtual Channel (VC) File Recovery	21

3.1.1	Description	21

3.1.2	Main Scripts/Programs	21

3.1.3	Products and Storage	21

3.1.4	Process Logs	21

3.1.5	Database Information	21

3.1.6	Web Information	21

3.2	Level 0 (L0) and Level 1 (L1) File Creation	22

3.2.1	Description	22

3.2.2	Main Scripts/Programs	22

3.2.3	Products and Storage	22

3.2.4	Process Logs	23

3.2.5	Database Information	23

3.2.6	Web Information	23

3.3	Level 1 (L1) Eclipse Spin Corrections	23

3.3.1	Description	23

3.3.2	Main Scripts/Programs	24

3.3.3	Products and Storage	24

3.3.4	Process Logs	25

3.4	Level 2 (L2) CDF File Production	26

3.4.1	Description	26

3.4.2	Main Scripts/Programs	26

3.4.3	Products and Storage	27

3.4.4	Process Logs	27

3.4.5	Database Information	27

3.4.6	Web Information	28

3.4.7	Calibration Files	28

3.5	BFDS Ephemeris Data Product Archive and Probe State File Production – Version 0	28

3.5.1	Description	28

3.5.2	Main Scripts/Programs	28

3.5.3	Products and Storage	29

3.5.4	Process Logs	29

3.5.5	Database Information	29

3.5.6	Web Information	30

3.6	BFDS Ephemeris Data Product Archive Check	31

3.6.1	Description	31

3.6.2	Main Scripts/Programs	31

3.6.3	Products and Storage	31

3.6.4	Process Logs	31

3.6.5	Database Information	31

3.6.6	Web Information	31

3.7	Probe State File Production – Version 1	32

3.7.1	Description	32

3.7.2	Main Scripts/Programs	32

3.7.3	Products and Storage	32

3.7.4	Process Logs	32

3.7.5	Database Information	32

3.7.6	Web Information	32

3.8	Probe State File Production – Version 2	33

3.8.1	Description	33

3.8.2	Main Scripts/Programs	33

3.8.3	Products and Storage	34

3.8.4	Process Logs	34

3.8.5	Database Information	34

3.8.6	Web Information	34

3.9	Summary and Tohban Plot Production	35

3.9.1	Description	35

3.9.2	Main Scripts/Programs	35

3.9.3	Products and Storage	35

3.9.4	Process Logs	35

3.9.5	Database Information	35

3.9.6	Web Information	35

3.10	Archival of Raw Probe Telemetry Files	36

3.10.1	Description	36

3.10.2	Main Scripts/Programs	36

3.10.3	Products and Storage	36

3.10.4	Process Logs	37

3.10.5	Database Information	37

3.10.6	Web Information	37

3.11	VC1 Dump Verification and Validation	38

3.11.1	Description	38

3.11.2	Main Scripts/Programs	38

3.11.3	Products and Storage	38

3.11.4	Process Logs	38

3.11.5	Database Information	38

3.11.6	Web Information	38

3.12	VC3 Dump Verification and Validation	39

3.12.1	Description	39

3.12.2	Main Scripts/Programs	39

3.12.3	Products and Storage	39

3.12.4	Process Logs	39

3.12.5	Database Information	39

3.12.6	Web Information	39

3.13	L0 Data File Inventory	40

3.13.1	Description	40

3.13.2	Main Scripts/Programs	40

3.13.3	Products and Storage	40

3.13.4	Process Logs	40

3.13.5	Database Information	40

3.13.6	Web Information	40

3.14	L1 Data File Inventory	41

3.14.1	Description	41

3.14.2	Main Scripts/Programs	41

3.14.3	Products and Storage	41

3.14.4	Process Logs	41

3.14.5	Database Information	41

3.14.6	Web Information	41

3.15	L2 Data File Inventory	42

3.15.1	Description	42

3.15.2	Main Scripts/Programs	42

3.15.3	Products and Storage	42

3.15.4	Process Logs	42

3.15.5	Database Information	42

3.15.6	Web Information	42

3.16	State Data File Inventory	43

3.16.1	Description	43

3.16.2	Main Scripts/Programs	43

3.16.3	Products and Storage	43

3.16.4	Process Logs	43

3.16.5	Database Information	43

3.16.6	Web Information	43

4.	Ground Data Processing Activities	44

4.1	UCLA Ground Magnetometer (GMAG) Data Collection – THEMIS GBO	45

4.1.1	Description	45

4.1.2	Main Scripts/Programs	45

4.1.3	Products and Storage	46

4.1.4	Process Logs	46

4.1.5	Database Information	46

4.1.6	Web Information	46

4.2	Ground Magnetometer (GMAG) Data Collection – THEMIS EPO	47

4.2.1	Description	47

4.2.2	Main Scripts/Programs	47

4.2.3	Products and Storage	47

4.2.4	Process Logs	48

4.2.5	Database Information	48

4.2.6	Web Information	48

4.3	Ground Magnetometer (GMAG) Data Collection – CARISMA	49

4.3.1	Description	49

4.3.2	Main Scripts/Programs	49

4.3.3	Products and Storage	50

4.3.4	Process Logs	50

4.3.5	Database Information	50

4.3.6	Web Information	50

4.4	Ground Magnetometer (GMAG) Data Collection – GIMA	51

4.4.1	Description	51

4.4.2	Main Scripts/Programs	51

4.4.3	Products and Storage	52

4.4.4	Process Logs	52

4.4.5	Database Information	52

4.4.6	Web Information	52

4.5	Ground Magnetometer (GMAG) Data Collection – MACCS	53

4.5.1	Description	53

4.5.2	Main Scripts/Programs	53

4.5.3	Products and Storage	54

4.5.4	Process Logs	54

4.5.5	Database Information	54

4.5.6	Web Information	54

4.6	Cleanup after GMAG data download	55

4.6.1	Description	55

4.6.2	Main Scripts/programs	55

4.6.3	Products and Storage	55

4.6.4	Process logs	55

4.6.5	Database Information	55

4.6.6	Web Information	55

4.7	Ground Magnetometer (GMAG) Data Collection – Athabasca	56

4.7.1	Description	56

4.7.2	Main Scripts/Programs	56

4.7.3	Products and Storage	56

4.7.4	Process Logs	56

4.7.5	Database Information	57

4.7.6	Web Information	57

4.8	Ground Magnetometer (GMAG) Data Collection – Greenland/Denmark/Norway	58

4.8.1	Description	58

4.8.2	Main Scripts/Programs	59

4.8.3	Products and Storage	59

4.8.4	Process Logs	60

4.8.5	Database Information	60

4.8.6	Web Information	60

4.9	Ground Magnetometer (GMAG) Data Collection – INTERMAGNET	61

4.9.1	Description	61

4.9.2	Main Scripts/Programs	62

4.9.3	Products and Storage	62

4.9.4	Process Logs	63

4.9.5	Database Information	63

4.9.6	Web Information	63

4.10	Ground Magnetometer (GMAG) Data Collection – US Geological Survey	64

4.10.1	Description	64

4.10.2	Main Scripts/Programs	64

4.10.3	Products and Storage	65

4.10.4	Process Logs	65

4.10.5	Database Information	65

4.10.6	Web Information	65

4.11	Ground Magnetometer (GMAG) Data Collection – Antarctic sites (PENGUIN)	66

4.11.1	Description	66

4.11.2	Main Scripts/Programs	66

4.11.3	Products and Storage	67

4.11.4	Process Logs	67

4.11.5	Database Information	67

4.11.6	Web Information	67

4.12	Ground Magnetometer (GMAG) Data Collection – Leirvogur	68

4.12.1	Description	68

4.12.2	Main Scripts/Programs	68

4.12.3	Products and Storage	69

4.12.4	Process Logs	69

4.12.5	Database Information	69

4.12.6	Web Information	69

4.13	Ground Magnetometer (GMAG) Data Collection – AARI	70

4.13.1	Description	70

4.13.2	Main Scripts/Programs	70

4.13.3	Products and Storage	71

4.13.4	Process Logs	71

4.13.5	Database Information	71

4.13.6	Web Information	71

4.14	Ground Magnetometer (GMAG) Data Collection – Monitor	72

4.14.1	Description	72

4.14.2	Main Scripts/Programs	72

4.14.3	Products and Storage	72

4.14.4	Process Logs	72

4.14.5	Database Information	72

4.14.6	Web Information	72

4.15	Ground Magnetometer (GMAG) Data – Convert Raw GBO Data to Level 2 (L2) CDF Data Product	73

4.15.1	Description	73

4.15.2	Main Scripts/Programs	73

4.15.3	Products and Storage	75

4.15.4	Process Logs	76

4.15.5	Database Information	76

4.15.6	Web Information	76

4.16	Ground Magnetometer (GMAG) Data – Convert CARISMA ASCII to Level 2 Data Product	77

4.16.1	Description	77

4.16.2	Main Scripts/Programs	77

4.16.3	Products and Storage	78

4.16.4	Process Logs	78

4.16.5	Database Information	78

4.16.6	Web Information	78

4.17	Ground Magnetometer (GMAG) Data – Convert GIMA NetCDF to Level 2 Data Product	80

4.17.1	Description	80

4.17.2	Main Scripts/Programs	80

4.17.3	Products and Storage	81

4.17.4	Process Logs	81

4.17.5	Database Information	81

4.17.6	Web Information	81

4.18	Ground Magnetometer (GMAG) Data – Convert MACCS ASCII data to CDF	83

4.18.1	Description	83

4.18.2	Main Scripts/Programs	83

4.18.3	Products and Storage	84

4.18.4	Process Logs	85

4.18.5	Database Information	85

4.18.6	Web Information	85

4.19	Ground Magnetometer (GMAG) Data – Convert Greenland/Denmark/Norway ASCII data to CDF	86

4.19.1	Description	86

4.19.2	Main Scripts/Programs	86

4.19.3	Products and Storage	87

4.19.4	Process Logs	87

4.19.5	Database Information	87

4.19.6	Web Information	87

4.20	Ground Magnetometer (GMAG) Data – Convert INTERMAGNET ASCII data to CDF	88

4.20.1	Description	88

4.20.2	Main Scripts/Programs	88

4.20.3	Products and Storage	89

4.20.4	Process Logs	89

4.20.5	Database Information	89

4.20.6	Web Information	89

4.21	Ground Magnetometer (GMAG) Data – Convert US Geological Survey ASCII data to CDF	90

4.21.1	Description	90

4.21.2	Main Scripts/Programs	90

4.21.3	Products and Storage	91

4.21.4	Process Logs	91

4.21.5	Database Information	91

4.21.6	Web Information	91

4.22	Ground Magnetometer (GMAG) Data – Convert Antarctic CDF data to ASCII	92

4.22.1	Description	92

4.22.2	Main Scripts/Programs	92

4.22.3	Products and Storage	93

4.22.4	Process Logs	93

4.22.5	Database Information	93

4.22.6	Web Information	93

4.23	Ground Magnetometer (GMAG) Data – Convert Leirvogur ASCII data to CDF	94

4.23.1	Description	94

4.23.2	Main Scripts/Programs	94

4.23.3	Products and Storage	95

4.23.4	Process Logs	95

4.23.5	Database Information	95

4.23.6	Web Information	95

4.24	Ground Magnetometer (GMAG) Data – Convert AARI ASCII data to CDF	96

4.24.1	Description	96

4.24.2	Main Scripts/Programs	96

4.24.3	Products and Storage	97

4.24.4	Process Logs	97

4.24.5	Database Information	97

4.24.6	Web Information	97

4.25	Ground Magnetometer (GMAG) Data – Make Stack Plot	98

4.25.1	Description	98

4.25.2	Main Scripts/Programs	98

4.25.3	Products and Storage	99

4.25.4	Process Logs	99

4.25.5	Database Information	99

4.25.6	Web Information	99

4.26	AEIndex Generation	100

4.26.1	Description	100

4.26.2	Main Scripts/Programs	100

4.26.3	Products and Storage	100

4.26.4	Process Logs	101

4.26.5	Database Information	101

4.26.6	Web Information	101

4.27	Ground Magnetometer (GMAG) Data – Check for Missing CDFs	102

4.27.1	Description	102

4.27.2	Main Scripts/Programs	102

4.27.3	Products and Storage	102

4.27.4	Process Logs	102

4.27.5	Database Information	102

4.27.6	Web Information	102

4.28	Ground Magnetometer (GMAG) Data – Generate Missing CDFs	103

4.28.1	Description	103

4.28.2	Main Scripts/Programs	103

4.28.3	Products and Storage	104

4.28.4	Process Logs	104

4.28.5	Database Information	104

4.28.6	Web Information	104

4.29	Ground Magnetometer (GMAG) Data – EPO JPEG Processing	106

4.29.1	Description	106

4.29.2	Main Scripts/Programs	106

4.29.3	Products and Storage	107

4.29.4	Process Logs	107

4.29.5	Database Information	107

4.29.6	Web Information	108

4.30	Ground Magnetometer (GMAG) Data – EPO JPEG Monitor	109

4.30.1	Description	109

4.30.2	Main Scripts/Programs	109

4.30.3	Products and Storage	109

4.30.4	Process Logs	109

4.30.5	Database Information	109

4.30.6	Web Information	109

4.31	GMAG Raw Data File Inventory	110

4.31.1	Description	110

4.31.2	Main Scripts/Programs	110

4.31.3	Products and Storage	112

4.31.4	Process Logs	113

4.31.5	Database Information	113

4.31.6	Web Information	113

4.32	GMAG CDF Data File Inventory	114

4.32.1	Description	114

4.32.2	Main Scripts/Programs	114

4.32.3	Products and Storage	115

4.32.4	Process Logs	115

4.32.5	Database Information	115

4.32.6	Web Information	115

4.33	GMAG Stack Plot Data File Inventory	116

4.33.1	Description	116

4.33.2	Main Scripts/Programs	116

4.33.3	Products and Storage	116

4.33.4	Process Logs	116

4.33.5	Database Information	116

4.33.6	Web Information	116

4.34	GMAG EPO JPEG Plot File Inventory	117

4.34.1	Description	117

4.34.2	Main Scripts/Programs	117

4.34.3	Products and Storage	118

4.34.4	Process Logs	118

4.34.5	Database Information	118

4.34.6	Web Information	118

4.35	All Sky Imager (ASI) Low-Rate Data Collection – THEMIS GBO	119

4.35.1	Description	119

4.35.2	Main Scripts/Programs	119

4.35.3	Products and Storage	120

4.35.4	Process Logs	120

4.35.5	Database Information	120

4.35.6	Web Information	120

4.36	All Sky Imager (ASI) High-Rate Data Collection – THEMIS GBO	121

4.36.1	Description	121

4.36.2	Main Scripts/Programs	121

4.36.3	Products and Storage	121

4.36.4	Process Logs	121

4.36.5	Database Information	121

4.36.6	Web Information	122

4.37	All Sky Imager (ASI) Low-Rate Data File Inventory	123

4.37.1	Description	123

4.37.2	Main Scripts/Programs	123

4.37.3	Products and Storage	124

4.37.4	Process Logs	124

4.37.5	Database Information	124

4.37.6	Web Information	124

4.38	All Sky Imager (ASI) High-Rate Data File Inventory	125

4.38.1	Description	125

4.38.2	Main Scripts/Programs	125

4.38.3	Products and Storage	125

4.38.4	Process Logs	126

4.38.5	Database Information	126

4.38.6	Web Information	126

4.39	All Sky Imager (ASI) Level 1 (L1) CDF Data File Inventory	127

4.39.1	Description	127

4.39.2	Main Scripts/Programs	127

4.39.3	Products and Storage	129

4.39.4	Process Logs	129

4.39.5	Database Information	129

4.39.6	Web Information	129

4.40	All Sky Imager (ASI) Site Summaries	130

4.40.1	Description	130

4.40.2	Main Scripts/Programs	130

4.40.3	Products and Storage	132

4.40.4	Process Logs	132

4.40.5	Database Information	132

4.40.6	Web Information	132

4.41	All Sky Imager (ASI) Products	133

4.41.1	Description	133

4.41.2	Main Scripts/Programs	133

4.41.3	Products and Storage	134

4.41.4	Process Logs	134

4.41.5	Database Information	134

4.41.6	Web Information	134

4.42	All Sky Imager (ASI) Orbits	135

4.42.1	Description	135

4.42.2	Main Scripts/Programs	135

4.42.3	Products and Storage	135

4.42.4	Process Logs	136

4.42.5	Database Information	136

4.42.6	Web Information	136

4.43	All Sky Imager (ASI) Mosaic Image Production	137

4.43.1	Description	137

4.43.2	Main Scripts/Programs	137

4.43.3	Products and Storage	137

4.43.4	Process Logs	137

4.43.5	Database Information	137

4.43.6	Web Information	137

5.	Databases	138

5.1	Cron-Job Warning Notification Database	139

6.	Website Activities	139

6.1	Process Web Server Logs	139

6.1.1	Description	139

6.1.2	Main Scripts/Programs	139

6.1.3	Products and Storage	140

6.1.4	Process Logs	140

6.1.5	Database Information	140

6.1.6	Web Information	140

6.2	Website Maintenance	141

6.2.1	THEMIS – Critical Site Files	141

6.2.2	THEMIS – Beta Test Page	141

6.2.3	THEMIS – News Updates	141

6.2.4	THEMIS – GBO Station Updates	142

6.2.5	THEMIS – Publications	142

6.2.6	THEMIS – Nuggets	142

6.2.7	ARTEMIS – Critical Site Files	143

6.2.8	ARTEMIS – Beta Test Page	143

6.2.9	ARTEMIS – News Updates	143

6.2.10	ARTEMIS – Publications	144

6.2.11	ARTEMIS – Nuggets	144

7.	Software Distribution Administration	145

8.	Appendix	148

8.1	GBO/EPO Site Map	148

8.2	THEMIS Data Mirror Sites	148

8.3	Software Extensions for TDAS	150

8.4	IDL Technical Support	150

# Introduction

## Purpose

The purpose of this document is to describe all activities, procedures, and functions involved in the day to day data processing of THEMIS science data.  Also details of the maintenance of the THEMIS web site and the TDAS software distribution are included.

## Applicable Documents.

- THM_SYS_012_PDMP				THEMIS Project Data Management Plan

- THM-SOC-102					THEMIS Probe State File Definition

# Data Processing Overview

## Overview

The major data processing elements are displayed below in Figure 1.

Figure 1 Data Processing Overview

Data processing is driven mainly by scripts and programs called from unix cronjobs which reside on a variety of workstations. These workstations and the associated cronjob initiated scripts are listed in Table 1. The majority of data processing scripts and programs reside in the workspace /disks/socware/thmsoc_dp_current, which is currently a softlink to /disks/socware/thmsoc_production_test. The scripts and programs found here are developed under SVN control and are copied into the workspace. Additional scripts and software can be found in /home/thmsoc/software_dev.

A wrapper script, call_scripts.ksh, is used to call a particular script and serves to check if that script is already running. This is done in place of lock files. If a script is found to be running in excess of a set time limit, email notification is sent to personnel. The wrapper script also records workstation, and start/stop time of each script in a MySQL database table Process_Logs.process_list.

Table 1 Cron Job Overview

| Process | Script(s) | Workstation |
| --- | --- | --- |
| Server Write Check | cronwatch.ksh | ALL |
| EPO UCLA-GMAG Mirror | epo_ucla_rmd_mirror_batch.ksh | gaia2 |
| GBO UCLA-GMAG Mirror | gbo_uc_rmd_mirror_batch.ksh | gaia2 |
| GBO UAlberta-GMAG Mirror | gbo_ua_canmag_mirror_batch.ksh | gaia2 |
| GBO UAlaska-GMAG Mirror | gbo_ualaska_mirror_batch.ksh | gaia2 |
| GBO UAthabasca-GMAG Mirror | gbo_atha_rmd_mirror_batch.ksh | gaia2 |
| GBO Augsburg GMAG Mirror | call_wget_maccs_gmag.ksh | gaia2 |
| Download Greenland/Norway/Denmark gmag data from TGO. | call_wget_green_gmag.ksh | gaia2 |
| Download gmag data provided through INTERMAGNET | call_wget_intermagnet_gmag.ksh | gaia2 |
| Download gmag data provided from USGS | call_wget_usgs_gmag.ksh | gaia2 |
| Download Antarctic gmag data | call_wget_antarctic_gmag.ksh | gaia2 |
| Download gmag data from Leirvogur | call_wget_lrv_gmag.ksh | gaia2 |
| Download gmag data from AARI | call_aari_gmag_mirror.ksh | gaia2 |
| GBO Check for late GMAG (disabled Sep 09) | chk4late_gmag.ksh | gaia |
| Probe Make State V2 CDFs | make_state_v2.ksh | python2 |
| GBO ASI Low Res Mirror with Calgary | gbo_asi_rt_mirror_batch.ksh | gaia2 |
| GBO ASI Low Res Mirror Cleanup | rsync_gbo_cleanup.ksh | gaia2 |
| GBO ASI Low Res Collection Check (disabled Sep 09) | chk_lowrate_asi_files.ksh | gaia |
| Probe L0 Inventory List Generation | list_probe_l0.ksh | gaia2 |
| Probe L0 Inventory Display Generation | gen_probe_l0_list.ksh gen_probe_l0_lists.ksh | gaia2 |
| Probe L1 Inventory List Generation | list_probe_l1.ksh | gaia2 |
| Probe L1 Inventory Display Generation | gen_probe_l1_list.ksh gen_probe_l1_lists.ksh | gaia2 |
| Probe L2 Inventory List Generation | list_probe_l2.ksh | gaia2 |
| Probe L2 Inventory Display Generation | gen_probe_l2_list.ksh | gaia2 |
| Probe State Inventory List Generation | list_probe_state.ksh | gaia2 |
| Probe State Inventory Display Generation | gen_probe_state_list.ksh | gaia2 |
| Probe BFDS Archive and State V0 Generation | bfds_archive.ksh | python2 |
| Probe BFDS Archive Check | chk_bfds_archive.ksh | python2 |
| GBO UAlaska GMAG Conversion to L2 | call_gima_netcdf2all.ksh | astraea2 |
| GBO UAlberta GMAG Conversion to L2 | call_candat_ascii2all.ksh | astraea2 |
| GBO Greenland GMAG Conversion to L2 (no longer running) | call_green_ascii2all.ksh | astraea |
| Greenland/Denmark/Norway Conversion to L2 CDF | green_ascii2all_new.ksh | astraea2 |
| GBO MACCS GMAG Conversion to L2 | call_maccs_ascii2all.ksh maccs_ascii2all_cleanup.ksh | astraea2 |
| EPO GMAG JPG Collection and Processing | epo_jpg_check.ksh | astraea2 |
| EPO GMAG JPG List Generation | gen_gmag_jpg_list_new.ksh | astraea2 |
| GBO GMAG Stack Plot Generation | call_make_stack.ksh stacks_cleanup.ksh | astraea2 |
| GBO GMAG AEIndex generation | call_make_ae_index.ksh make_ae_index_cleanup.ksh | astraea2 |
| GBO GMAG Raw Data Inventory | make_gmag_raw_files.ksh | astraea2 |
| GBO GMAG L2 CDF Data Inventory | make_gmag_cdf_files.ksh | astraea2 |
| GBO GMAG Missing L2 CDFs | gen_gmag_missing_cdf_list.ksh | astraea2 |
| INTERMAGNET GMAG Conversion to L2 CDF | intermagnet_ascii2all.ksh | astraea2 |
| USGS GMAG Conversion to L2 CDF | usgs_ascii2all.ksh | astraea2 |
| Antarctic GMAG Conversion to L2 ASCII (CDF provided) | antarctic_cdf2ascii.ksh | astraea2 |
| Leirvogur GMAG Conversion to L2 CDF | lrv_ascii2all.ksh | astraea2 |
| AARI GMAG Conversion to L2 CDF | aari_ascii2all.ksh | astraea2 |
| GBO ASI Low Res Inventory and Display | list_lowrate_asi_files.ksh, gen_lowrate_asi_display.ksh, gen_lowrate_asi_display_summary.ksh | astraea2 |
| GBO ASI Hi Res Inventory and Display | make_hi_asi_file_list.ksh, gen_hirate_asi_display_daily.ksh | astraea2 |
| GBO ASI L1 CDF Lists | list_l1_ast_cdfs.ksh, gen_ast_l1_cdf_list.ksh, list_l1_asf_cdfs.ksh, gen_asf_inventory_display.ksh, list_l1_ask_cdfs.ksh, gen_ask_l1_cdf_list_display.ksh | astraea2 |
| GBO ASI Summary File Inventory and Display | list_asi_site_summaries.ksh, gen_asi_site_summary_display.ksh, list_asi_allsite_summaries.ksh, gen_asi_allsite_summary_display.ksh, gen_grand_asi_display.ksh | astraea2 |
| Probe L0/L1 File Generation | make_l0_and_l1.ksh cleanup_make_l0_and_l1.ksh | python2 |
| Probe L1 Eclipse Spin Corrections | ecl_spin_corrections_wrapper.bash | python2 |
| Probe Data Dump Checks | process_vc1dump_stats.ksh, process_vc3dump_stats.ksh | python2 |
| Probe L2 File generation | create_probe_l2cdf.ksh | python2 |
| Cleanup GBO WGET log files | wget_gbo_cleanup.ksh | gaia2 |
| Cleanup after GMAG download scripts | gmag_webdownloads_cleanup.ksh | gaia2 |
| Probe Summary Plot Generation | overplot.ksh, overplot2.ksh | gaia2 |
| Probe Summary Plot Inventory | list_summaryplots.ksh, gen_summaryplot_display | gaia2 |
| Web Server Log Processing | process_weblogs.ksh | danaid |
| GBO ASI Mosaic Generation | run_asi_mosaic.ksh | thailo |
| GBO/EPO UCLA GMAG Conversion to L2 | ucla_rmd2all.ksh ucla_rmd2all_missing.ksh | auxo |
| GBO ASI CDF Product Generation | make_asi_products.ksh reprocess_asi.ksh | auxo |
| Probe/GBO Orbit/Ground Plot Generation | make_asi_orbits.ksh | auxo |
| Probe VC File CD Archive | probeDataToCD.ksh | auxo |
| Generate EPO GMAG summary plots for EPO web interface. | make_epo_plots_daily.ksh epo_magfile_append.ksh | auxo |
| Cronjob Warning Notifications | thmsoc_dbnotify.php | astraea2 |

To check on the status of processing activities, go to the following website:

http://themis.ssl.berkeley.edu/status.shtml

# Probe Data Processing Activities

## Virtual Channel (VC) File Recovery

### Description

The VC files containing the raw instrument data have to be retrieved from a variety of locations, both remotely and locally.

### Main Scripts/Programs

There are 4 major programs making up the THEMIS VC File Recovery System:

- /home/thmsoc/software_dev/filetracker/sattrackscheduler/ScheduleReader.java

- /home/thmsoc/software_dev/filetracker/filegetter /FileGetter.java

- /home/thmsoc/software_dev/filetracker/filechecker/FileChecker.java

- /home/thmsoc/software_dev/filetracker/fileprocessor/FileProcessor.java

These programs run automatically on btaps-srvr1 and will restart themselves if errors occur. For each program there’s a cronjob running on rayon which restarts the program in an event of a catostrophic failure. The programs also terminate and restart periodically.

### Products and Storage

VC files are initially copied to:

/disks/themisdata/vc_drop/incoming

When the copy is complete, they are moved to the following directory for further processing:

/disks/themisdata/vc_drop/ready2process

### Process Logs

Log information is found in:

/disks/themisdata/process_logs/vc_files/schedulereader.txt

/disks/themisdata/process_logs/vc_files/filegetter.txt

/disks/themisdata/process_logs/vc_files/filechecker.txt

/disks/themisdata/process_logs/vc_files/fileprocessor.txt

### Database Information

The database file_tracker_themis is found on the MySQL database server on astraea2. It includes tables containing file and process statistics.

### Web Information

An interface to the database statistics can be found at:

http://themis.ssl.berkeley.edu/schedule_view/

## Level 0 (L0) and Level 1 (L1) File Creation

### Description

When the VC files are received they are initially converted into 2 data products: L0 files are raw counts for each packet/application ID, L1 files are raw counts stored in CDF format.

### Main Scripts/Programs

A cronjob on python launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/make_l0_and_l1.ksh

and calls the configuration files:

[1] /disks/socware/thmsoc_dp_current/src/config/make_l0_and_l1.config

[2] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[3] /home/thmsoc/jwls_stuff/tmtools_current/tmtools_setup.bourne

which define the following environment variables:

from [1]: LOGFILE=/disks/themisdata/process_logs/lzprocess/lz_process_log_$(date '+%y%m%d')

VCDROP=/disks/themisdata/vc_drop/ready2process

from [2]: THMSOC=/disks/socware/thmsoc

LOCAL=/mydisks/home/thmsoc

WEBSERVERLOGHOME=/var/log/httpd

VC1FILECHK=/disks/themisdata/workdir/VC0_Files_Received/VC1_Check

VC3FILESCH=/disks/themisdata/workdir/VC0_Files_Received/VC3_Check

KSH_SCRIPTS=/disks/socware/thmsoc/src/ksh

PHP_SCRIPTS=/disks/socware/thmsoc/src/php

SCRATCH=/disks/themisdata/scratch

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu 			lphilpott@igpp.ucla.edu"

from [3]: TMTOOLS_DATAROOT=/disks/themisdata

TMTOOLS_ROOT=/home/thmsoc/jwls_stuff/tmtools_6_30

This script checks /disks/themisdata/vc_drop/ready2process for VC files and if found, launches the following script to produce the L0 and L1 files:

/home/thmsoc/jwls_stuff/tmtools_current/bin/vc_wrapper

/home/thmsoc/jwls_stuff/tmtools_current/bin/lzp_wrapper

For each VC files processed, vc_wrapper produces a directory of log files containing numerous statistics on processing results. The following script is called to process this information into a MySQL database:

/disks/socware/thmsoc_dp_current/src/ksh/prc_vcwrap_results.ksh

### Products and Storage

vc_wrapper will produce L0 packet files for a specific probe and place the files at:

/disks/themisdata/th[a-e]/l0/yyyy/mm/dd/

lzp_wrapper will produce L1 CDF files for a specific probe at:

/disks/themisdata/th[a-e]/l1/yyyy/[type]/

### Process Logs

Process logs are available at:

make_l0_and_l1.ksh: /disks/themisdata/process_logs/lzprocess/lz_process_log_yymmdd

vc_wrapper: /tmp/vc_wrapper_dirlist.$$

lzp_wrapper: /disks/themisdata/th[a-e]/l1/tmpfiles/th[a-e]_yyyymmdd.log

prc_vcwrap_results.ksh: /tmp/vc_wrapper_dirlist.$$

### Database Information

The database probe_l0_process is found on the MySQL database server on astraea2. It includes tables containing file and process statistics.

### Web Information

Recent results of the L0 processing can be viewed at the following web address:

http://themis.ssl.berkeley.edu/vc_check/list_latest.php

Long term results can be accessed by probe/apid/date at:

http://themis.ssl.berkeley.edu/vc_check/

A useful tool for reviewing packet counts by probe/apid is found at:

http://themis.ssl.berkeley.edu/db_access/apidStat.html

A full inventory of the L0 and L1 files produced can be viewed at the following web addresses:

http://themis.ssl.berkeley.edu/data_inventory/space_data/probe_l0_availability.txt

http://themis.ssl.berkeley.edu/data_inventory/space_data/probe_l1_availability.txt

## Level 1 (L1) Eclipse Spin Corrections

### Description

Once the L1 State CDFs have been produced, the eclipse spin corrections can be applied. First, fake sunpulses are generated for the eclipse periods by fitting piece-wise quadratic functions to the eclipse boundaries.  The second round of corrections is done by estimating the FGM angle offset between the spin projections of the FGL and FGS science data. The L0->L1 process is then re-run to update eclipse period sunpulses, and to update the Spin and State CDFs with the FGM angle offsets.

### Main Scripts/Programs

A cronjob on python2 launches the spin corrections wrapper script:

/disks/socware/thmsoc_dp_current/src/tmtools/src/scripts/ecl_spin_corrections_wrapper.bash

and calls the configuration files:

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /home/thmsoc/jwls_stuff/tmtools_current/tmtools_setup.bourne

which define the following environment variables:

from [1]: THMSOC=/disks/socware/thmsoc

LOCAL=/mydisks/home/thmsoc

KSH_SCRIPTS=/disks/socware/thmsoc/src/ksh

PHP_SCRIPTS=/disks/socware/thmsoc/src/php

SCRATCH=/disks/themisdata/scratch

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu"

from [2]: TMTOOLS_DATAROOT=/disks/themisdata

TMTOOLS_ROOT=/home/thmsoc/jwls_stuff/tmtools_7_10

The ecl_spin_corrections_wrapper launches the following sequence of scripts:

/disks/socware/thmsoc_dp_current/src/tmtools/src/scripts/ecl_sunpulse_wrapper.bash

/home/thmsoc/jwls_stuff/tmtools_current/bin/lzp_wrapper

/disks/socware/thmsoc_dp_current/src/tmtools/src/scripts/ecl_fgm_corr_wrapper.bash

/home/thmsoc/jwls_stuff/tmtools_current/bin/lzp_wrapper

ecl_spin_corrections_wrapper can be used in automated mode with the “-auto” option (for cronjobs), where it identifies the last eclipse processed, and applies the spin corrections from that date to the present date.

For re-processing of spin corrections, ecl_spin_corrections_wrapper can be given the start, end dates  and probes at the command line as follows:

ecl_spin_corrections_wrapper 20110530 20120101 tha thb

For processing a new batch of spin corrected L1 State CDFs, the following commands can be used:

args=”20110530 20120101 tha thb” ; ephem_prelim_wrapper $args ; process_lzp_batch $args ;

ecl_spin_corrections_wrapper $args

### Products and Storage

ecl_sunpulse_wrapper will produce fitted, fake sunpulses and PNG images of the eclipses, and place the files at:

${TMTOOLS_DATAROOT}/${probe}/eclipse_model_sunpulse/${yyyy}/${mm}

ecl_fgm_corr_wrapper will produce FGM spinfit correction data and diagnostic plots, and place them at:

${TMTOOLS_DATAROOT}/${probe}/eclipse_model_sunpulse/${yyyy}/${mm}

### Process Logs

Process logs are available at:

ecl_sunpulse_wrapper.bash:

${TMTOOLS_DATAROOT}/eclipse/logs/${probe}/${probe}_sunpulse_available.txt

${TMTOOLS_DATAROOT}/eclipse/logs/${probe}/${probe}_last_ecl_fake_sunpulse.txt

${TMTOOLS_DATAROOT}/eclipse/logs/${probe}/${yyyy}/${mm}/${probe}_eclipse_${date}/installed_sunpulse_files.log

ecl_fgm_wrapper.bash:

${TMTOOLS_DATAROOT}/eclipse/logs/${probe}/${probe}_fgm_corr_available.txt

${TMTOOLS_DATAROOT}/eclipse/logs/${probe}/${probe}_last_ecl_fgm_correction.txt

${TMTOOLS_DATAROOT}/eclipse/logs/${probe}/${yyyy}/${mm}/${probe}_eclipse_${date}/installed_fgm_corr_files.log

## Level 2 (L2) CDF File Production

### Description

The L2 data files include data in calibrated, physical units.

### Main Scripts/Programs

A cronjob on python launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/create_probe_l2cdf.ksh

and calls the configuration files:

[1] /disks/socware/thmsoc_dp_current/src/config/overplot.bourne

[2] /disks/socware/thmsoc_dp_current/src/config/setup_idl6.3.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

thus defining the following environment variables:

from [1]: IDL_BASE_DIR=/disks/socware/thmsoc_dp_current/idl

IDL_PATH=+/disks/apollo/export/idl_6.3/lib:

+/disks/apollo/export/idl_6.3/examples:

+/disks/socware/thmsoc_dp_current/idl/thmsoc/temp:

+/disks/socware/thmsoc_dp_current/idl/themis:

+/disks/socware/thmsoc_dp_current/idl/ssl_general:

+/disks/socware/thmsoc_dp_current/idl/external:

+/disks/socware/thmsoc_dp_current/idl/thmsoc/summary_plots/

from [2]: IDL_DIR=/disks/apollo/export/idl_6.3

from [3]: LOCAL=/mydisks/home/thmsoc

The script calls an IDL routine which converts any L1 data files produced or modified in the last 36 hours into L2 data files in CDF format:

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/runoff_l2gen.bm (wrapper)

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_all_l1l2gen.pro

The IDL routine thm_all_l1l2gen.pro in turn executes instrument-specific L2 data generation IDL routines:

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_fgm.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_fbk.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_fit.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_esa.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_mom.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_sst.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_fft.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_scm.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_efi.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen/thm_l2gen_scmode.pro

In the instrument specific programs (i.e. thm_l2gen_esa.pro), the first step it to create calibrated data. Typically, one uses TDAS software to load and calibrate the L1 (of L0) data. All L2 data are the same as what one would get by loading and calibrating L1 data. The L2 data generated are contained in “TPLOT VARIABLES,” which are the main components of any TDAS based analysis. For information on tplot variables, please read the THEMIS_DATA_ANALYSIS_USERS_GUIDE.

When reprocessing of L2’s is required, use the following script:

/disks/socware/thmsoc_dp_current/src/ksh/create_probe_l2cdf_redux.ksh

The default L2 processing will reprocess any L2 files that require coordinate transforms (all but FFT and FBK) if new L1 STATE files are created. Occasionally, massive STATE file reprocessing will cause large amounts of un-necessary reprocessing (for example, if new state variables are added, but the state data used for coordinate transforms are not changed).  If  the new STATE files do not change coordinate transforms, then edit the crontab file on python, comment out the default command, and un-comment the line containing the command:

/disks/socware/thmsoc_dp_current/src/ksh/create_probe_l2cdf_nostate.ksh

In addition, there are a number of scripts for different types of reprocessing in the directory /home/thmsoc/l2_cronjobs, which can handle complex reprocessing tasks. These are typically .tcsh or .csh shell scripts which can be run from the command line.

Reprocessing can also be done by the thmsoc user from the IDL command line. First, cd into the directory /home/thmsoc/l2_cronjobs. Then source test_idl_setup, and start IDL. The IDL scripts that handle L2 processing are RUNOFF_L2GEN and THM_ALL_L1L2GEN. Please refer to the documentation headers in these files (located in the directory /disks/socware/thmsoc_dp_current/idl/thmsoc/l2gen) for instructions for use.

### Products and Storage

The L2 data files produced take the form:

th[a-e]_l2_[abc]_yyyymmdd_vnn.cdf

where:

abc=data type=fbk,fgm,esa,sst

nn=version number

The files are archived at:

/disks/themisdata/th[a-e]/l2/[abc]/yyyy

### Process Logs

Process logs are available on python at:

/mydisks/home/thmsoc/l2_proc/l2gen_idl_log.txt

### Database Information

The database probe_l2_processing is found on the MySQL database server on astraea2. It includes tables containing file and process statistics.

### Web Information

An inventory of the L2 files can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/space_data/probe_l2_availability.txt

### Calibration Files

Calibration files for all probe instruments are saved in the THEMIS SVN repository, and are distributed into the data directories. For each probe and instrument the files are located in the ‘0000’ directory for L1 data.  Most calibration files are stable and rarely require updating; FGM calibration files are frequently updated and are an exception to this rule.

Files are located in the sub-directory svn+ssh://thmsvn.ssl.berkeley.edu/calibration/cal_files. To update files, change the files in your local working copy, then commit to the SVN repository. This saves the new files in the repository, but not in the data directories. To update the files in the data directories, log into the thmsw account and run the script update_cal_files.sh:

/bin/sh /disks/socware/calibration/src/update_cal_files.sh

Note that this script currently updates all calibration files. Since FGM is updated more often, there is a special script that updates the FGM cal files (called update_fgm_cal_files.sh). Notes for each instrument follow:

FGM:

Calibration files for each probe are located in the sub-directory:

calibration/cal_files/spacecraft/fields/fgm

with filenames:

th?_fgmcal.txt

These files contain time dependent calibration parameters. Each row of each file contains a time followed by 13 values. The first 3 values are offsets, the next 9 are a 3 by 3 matrix of gain factors, followed by the nominal spin period.  For details on the calibration process, see the document:

ftp://apollo.ssl.berkeley.edu/pub/THEMIS/3%20Ground%20Systems/3.2%20Science%20Operations/Science%20Operations%20Documents/thm_soc_113_FGM_CALPROC_20061018.pdf.

Spin Harmonics: Calibration files to remove spin harmonics in the L2 fgm data are provided periodically by the German/Austrian FGM team.  These calibrations remove 1 Hz & 0.66 Hz harmonics in the spacecraft spin-plane and 0.66 Hz and 0.33 Hz harmonics along the spacecraft spin axis.   Our contacts for these files are Uli Auster(uli.auster at tu-bs.de) and David Fischer(David.Fischer at oeaw.ac.at)

Once provided the files should be copied into the appropriate probe directories fitting the pattern calibration/cal_files/spacecraft/ground/fgm/th?/l1/spin_cal.  The latest calibration file for each probe should also be copied to replace the th?_default_avgdist.txt file, so that preliminary calibrations will be available to TDAS for dates when definitive calibrations are not yet available.

EFI:

Calibration files for each probe are located in the sub-directory:

calibration/cal_files/spacecraft/fields/efi

with filenames:

th?_efi_calib_params.txt

These files contain the calibration factors for THEMIS EFI electric field data. Although the name of each file is different, the parameters used for each probe are the same, pending updates. The parameters, in order, are:

CAL_PAR_TIME    STRING    Array[1]

V_OFFSET        LONG      Array[6]

V_GAIN          FLOAT     Array[6]

V_UNIT          STRING    Array[1]

EDC_OFFSET      LONG      Array[3]

EDC_GAIN        FLOAT     Array[3]

EAC_OFFSET      LONG      Array[3]

EAC_GAIN        FLOAT     Array[3]

BOOM_LENGTH     FLOAT     Array[3]

BOOM_SHORTING_FACTOR

FLOAT     Array[3]

DSC_OFFSET      FLOAT     Array[3]

E_UNIT          STRING    Array[1]

SCM:

Calibration files for each probe are located in the sub-directory:

calibration/cal_files/spacecraft/fields/scm/cal (Note the difference from efi, fgm)

with filenames:

THEMIS_SCM?.cal

The files THEMIS_SCM1.cal, THEMIS_SCM2.cal, THEMIS_SCM3.cal, THEMIS_SCM4.cal, and THEMIS_SCM5.cal contain calibration data for THEMIS probes, A, B, C, D, and E. Each file contains the Gap angle (degrees) between the reference axis and the radiance diagram axis of the antenna. Following these parameters are the real and imaginary parts for the X, Y, and Z sensors for the full frequency range of each sensor. For details about the calibration process, see the

document:ftp://apollo.ssl.berkeley.edu/pub/THEMIS/3%20Ground%20Systems/3.2%20Science%20Operations/Science%20Operations%20Documents/thm_soc_129_scm_calibration.pdf

ESA:

ESA has one calibration file for all probes;

calibration/cal_files/spacecraft/particles/esa/tha_l1_esa_cal.txt

The file tha_l1_esa_cal.txt contains time-dependent gain factors for the ESA instrument. This file is used for calibration of all probe data, not only THEMIS A. The text file has each time followed by an array of 12 gain factors, 6 for electrons for each probe, plus probe 'f', the flatsat, and then six for ions. The relative gain factor for a given time is found via interpolation.

MOM:

Calibration files for each probe are located in the sub-directory:

calibration/cal_files/spacecraft/particles/mom

with filenames:

th?_l1_mom_cal_v03.txt         (Note v01, v02 and .sav files are obsolete)

The files th?_l1_mom_cal_v03.txt contain scaling factors for on-board moments and spacecraft potential, used in calibration of Level 1 MOM data. The first numbers are a 4, 13 array of scaling for the moments, transpose(caldata.mom_scale), then another 4, 13 array, transpose(caldata.mom_scale_sw1), used for solar wind mode, then a single number for scaling of SC potential. IDL save files and previous versions of each file are not used.

SST:

Calibration files for each probe are located in the sub-directory:

calibration/cal_files/spacecraft/particles/sst

with filenames:

th?_psif_calib_params.txt (ions)

th?_psef_calib_params.txt (electrons)

ASI:

ASI calibration files are located in the sub-directory:

calibration/cal_files/ground/asi/cal

And are copied to the data directory:

/disks/data/themis/thg/l2/asi/cal

Care should be taken to be sure that the files are updated correctly in both areas.

## BFDS Ephemeris Data Product Archive and Probe State File Production – Version 0

### Description

BFDS ephemeris products are archived and version 0 of the probe state files are produced on a daily basis.  Version 0 contains predictive information on all elements.

### Main Scripts/Programs

A cronjob on python launches the following script to archive the ephemeris products:

/disks/socware/thmsoc_dp_current/src/ksh/bfds_archive.ksh

which calls the following configuration files:

[1] /disks/socware/thmsoc_dp_current/src/config/bfds.config

[2] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[3] /disks/socware/thmsoc_dp_current/src/config/make_l0_and_l1.config

and the following environment variables are defined as:

from [1]: PROBES=”THEMIS_A THEMIS_B THEMIS_C THEMIS_D THEMIS_E”

BFDSEPHM=/home/bfds/THEMIS

BFDSARCH=/disks/themisdata/bfds

from [2]: SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu 			lphilpott@igpp.ucla.edu"

from [3]: TMTOOLS_ROOT=/home/thmsoc/jwls_stuff/tmtools_current

The following script is called to convert the newly archived ephemeris into version 0 of probe state files:

/home/thmsoc/jwls_stuff/tmtools_current/bin/ephem_prelim_wrapper

calling the configuration files:

[1] /home/thmsoc/jwls_stuff/tmtools_current/tmtools_setup.bourne

and thus defining the environment variables:

from [1]: TMTOOLS_DATAROOT=/disks/themisdata

TMTOOLS_TMPROOT=/mydisks/home/thmsoc

The script ephem_prelim_wrapper.bash calls a TMTOOLS batch routine to create probe state V00 CDF files from 1-day probe state ASCII files:

/home/thmsoc/jwls_stuff/tmtools_current/bin/process_prelim_ephem (bash)

which in turn calls the following routines:

/home/thmsoc/jwls_stuff/tmtools_current/bin/split_ephem_ascii_24h (bash)

/home/thmsoc/jwls_stuff/tmtools_current/bin/ephem2cdf (C)

/disks/socware/thmsoc_dp_current/idl/thmsoc/state/state_addcoords_batch.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/state/state_addcoords.pro

The ephem_prelim_wrapper.bash script can be run from the command line to reprocess state V00 CDFs, but not to re-archive the daily ephemeris files.  An additional script is available for archiving long time periods as well as processing data in the QA area:

/disks/socware/thmsoc_dp_current/src/ksh/make_state_from_archive.ksh

### Products and Storage

The ephemeris products are retrieved from /home/bfds/Products/THEMIS and are stored at:

/disks/themisdata/bfds

Version 0 of the probe state files follow the naming convention:

th[a-e]_l1_state_yyyymmdd_v00.cdf

These files are stored at:

/disks/themisdata/th[a-e]/l1/state/yyyy

### Process Logs

Process logs available:

make_probe_state_cdf: /disks/themisdata/process_logs/makestate/IDLOUT_MAKESTATE_yymmdd

### Database Information

None.

### Web Information

An inventory of version 0 state files can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/space_data/probe_state_availability.txt

## BFDS Ephemeris Data Product Archive Check

### Description

Check to see that the BFDS archive is up to date. If an archive is found missing, the procedure listed in section 3.4 will be run.

### Main Scripts/Programs

A cronjob on python launches the following script to archive the ephemeris products:

/disks/socware/thmsoc_dp_current/src/ksh/chk_bfds_archive.ksh

which calls the following configuration files:

/disks/socware/thmsoc_dp_current/src/config/bfds.config

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

### Products and Storage

The ephemeris products are retrieved from /home/bfds/Products/THEMIS and are stored at:

/disks/themisdata/bfds

Version 0 of the probe state files follow the naming convention:

th[a-e]_l1_state_yyyymmdd_v00.cdf

These files are stored at:

/disks/themisdata/th[a-e]/l1/state/yyyy

### Process Logs

None.

### Database Information

None.

### Web Information

An inventory of version 0 state files can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/space_data/probe_state_availability.txt

## Probe State File Production – Version 1

### Description

Version 1 state files shall contain predictive information on all elements except _spinper and _spinphase, which shall be definitive, produced from SUNPULSE telemetry processing..

### Main Scripts/Programs

Version 1 of the state file is produced as part of the L1 file creation – see section 3.2.

### Products and Storage

The filename format look like:

th[a-e]_l1_state_yyyymmdd_v01.cdf

These files are stored at:

/disks/themisdata/th[a-e]/l1/state/yyyy

### Process Logs

None.

### Database Information

None.

### Web Information

An inventory of version 1 state files can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/space_data/probe_state_availability.txt

## Probe State File Production – Version 2

### Description

When definitive ephemeris data becomes available, it is converted into CDF format and predictive information on attitude and principal inertial axis is added.

### Main Scripts/Programs

A cronjob on python launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/make_state_v2.ksh

which calls the following configuration files:

[1] /disks/socware/thmsoc_dp_current/src/config/make_l0_and_l1.config

[2] /disks/socware/thmsoc_dp_current/src/config/bfds.config

[3] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

and thus defining the environment variables:

from [1]:  LOGDIR=/disks/themisdata/process_logs/lzprocess

from [2]:	 BFDSEPHM=/home/bfds/THEMIS

BFDSARCH=/disks/themisdata/bfds

For the definitive ephemeris data processing, the script make_state_v2.ksh calls the wrapper and PHP routines:

/home/thmsoc/jwls_stuff/tmtools_current/src/scripts/ephem_definitive_wrapper.bash

/disks/socware/thmsoc_dp_current/src/php/inputEphem.php

/disks/socware/thmsoc_dp_current/src/php/inputASCII.php

/disks/socware/thmsoc_dp_current/src/php/inputCDF.php

The ephem_definitve_wrapper script initializes and calls the bash script:

/home/thmsoc/jwls_stuff/tmtools_current/src/scripts/process_definitive_ephem.bash

which in turn calls the following C binary, and IDL routines:

/home/thmsoc/jwls_stuff/tmtools_current/bin/ephem2cdf

/disks/socware/thmsoc_dp_current/idl/thmsoc/state/state_addcoords_batch.pro

/disks/socware/thmsoc_dp_current/idl/thmsoc/state/state_addcoords.pro

followed by the execution of the wrapper script:

/home/thmsoc/jwls_stuff/tmtools_current/src/scripts/statev2_wrapper

which sets up and calls the C binaries:

/home/thmsoc/jwls_stuff/tmtools_current/bin/process_statev2

/home/thmsoc/jwls_stuff/tmtools_current/bin/make_spinmodel

/home/thmsoc/jwls_stuff/tmtools_current/bin/spinmodel2cdf

/home/thmsoc/jwls_stuff/tmtools_current/bin/statecdf

/home/thmsoc/jwls_stuff/tmtools_current/bin/fix_l1_times

/home/thmsoc/jwls_stuff/tmtools_current/bin/link_highest_version

### Products and Storage

Similar to the version 0 production, C binaries and an IDL routine will convert ephemeris data into version 2 of the probe state file:

th[a-e]_l1_state_yyyymmdd_v02.cdf

These files are stored at:

/disks/themisdata/state15/CDF (no predictive attitude or inertial axis information yet)

/disks/themisdata/th[a-e]/l1/state/yyyy  (predictive attitude and inertial axis information added)

### Process Logs

make_state_v2.ksh: /disks/themisdata/process_logs/makestate/make_v2_yymmdd

ephem_definitive_wrapper: /tmp/make_state_v2.$$

process_definitive_ephem: /disks/themisdata/ephem/logs/th[a-e]

### Database Information

The database Probe_StateFile_Production is found on the MySQL database server on astraea2. It includes tables containing ASCII and CDF file and process statistics.

### Web Information

An inventory of version 2 state files can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/space_data/probe_state_availability.txt

## Summary and Tohban Plot Production

### Description

Summary and Tohban plots are created from L1 and L2 data products giving overviews of instrument operations and events, and are available for viewing on the THEMIS website

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/overplot.ksh

### Products and Storage

This script calls an IDL routine which downloads L1/L2 data files into IDL memory for conversion into the various plots. These plots are place in the following directory:

/disks/themisdata/overplots/yyyy/mm/dd

### Process Logs

Process logs are available at:

/disks/themisdata/process_logs/overplots/make_over_yymmdd

### Database Information

None.

### Web Information

The plots can be viewed on the website at:

http://themis.ssl.berkeley.edu/summary.php

## Archival of Raw Probe Telemetry Files

### Description

The raw probe telemetry (Virtual Channel – VC) files are archived at:

/disks/themisdata/th[a-e]/vc_archive/yyyy

In addition to the online archive, the VC files are backed up ob CD-R media

### Main Scripts/Programs

A cronjob on auxo launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/probeDataToCD.ksh

This script determines if enough new data has accumulated (650 Mbyte CD-R limit), and if so it assembles a CD-R directory of data in /disks/themisdata/scratch/CD_Production and converts the directory into a ISO CD-R image file which will be downloaded to the CD-R production system.

The CD production equipment is PC based and is found in SSL-Addition room 236 and is initiated by running the following script on moerae:

C:\Program Files\Padus\DiscJuggler\make_themis_images.BAT

### Products and Storage

The CD ISO file naming format is:

THEMIS_VC_ARCHIVE_n.iso

Where nnnn is a unique integer identifier starting at 1 for the first CD and incrementing through the mission.

Note: There is also a THEMIS_VC_ARCHIVE_n.job file made which contains ancillary data about the iso file and is used to drive to write process.

The files are stored at:

/disks/themisdata/scratch/CD_Production

Check output spindle on CD production system for finished THEMIS CDs. CDs are labeled using the following naming convention:

When (1) CD volume is found, delete the associated image and job files (THEMIS_VC_ARCHIVE_n.iso &THEMIS_VC_ARCHIVE_n.job) from /disks/themisdata/scratch/CD_Production.

### Process Logs

Process logs can be found at:

/disks/themisdata/process_logs/cd_production/CD_LogYYMMDD

### Database Information

CD production is database driven. Received VC files are archived in the MySQL table probe_l0_process.VC_Files_Processed. Each entry in this table has an “archive” field, a binary setting indicating whether the file needs to be archived (0) or not (1). The table CD_Production.CD_Inventory is used to catalog what files are on what CD. Both databases are accessed via the MySQL database server on astraea2.

### Web Information

None currently, but an interface allowing a user to specify probe/date/VC and retrieve volume information would be useful and easy to build.

## VC1 Dump Verification and Validation

### Description

Housekeeping telemetry is used to check for an indication that VC1 dump has occurred, and if so, verify the file was received and compare the frame dump count derived from housekeeping telemetry against the actual count derived from the file on the ground.  Any discrepancies encountered will lead to notification of the FOT.

### Main Scripts/Programs

A cronjob on python launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/process_vc1dump_stats.ksh

This high level script checks the following directory for VC0 files to check:

/home/thmsoc/software_dev/workdir/VC0_Files_Received/VC1_Check

Additional scripts:

/home/thmsoc/software_dev/ksh/ probe_vc1memchk.ksh – Gets SSR statistics from the BTAPS MySQL database; checks if a dump has occurred; compares telemetered dump count with ground dump count; updates DP MySQL database with dump statistics; notifies ops personnel if discrepancies are encountered (no VC1 file found, ground dump count < telemetered dump count).

### Products and Storage

None.

### Process Logs

None.

### Database Information

A table in the database probe_l0_process is used to store VC1 dump statistics which can be accessed from the web. The database is accessed via the MySQL database server on astraea2.

### Web Information

Dump statistics can be viewed at:

http://themis.ssl.berkeley.edu/data_processing_check/probe_data_processing/list_vc1_stats.php

## VC3 Dump Verification and Validation

### Description

Housekeeping telemetry is used to check for an indication that VC3 dump has occurred, and if so, verify the file was received and compare the frame dump count derived from housekeeping telemetry against the actual count derived from the file on the ground.  Any discrepancies encountered will lead to notification of the FOT.

### Main Scripts/Programs

A cronjob on danaid launches the following script:

/home/thmsoc/software_dev/ksh/process_vc3dump_stats.ksh

This high level script checks the following directory for VC0 files to check:

/home/thmsoc/software_dev/workdir/VC0_Files_Received/VC3_Check

Additional scripts:

/home/thmsoc/software_dev/ksh/ probe_vc1memchk.ksh – Gets SSR statistics from the BTAPS MySQL database; checks if a dump has occurred; compares telemetered dump count with ground dump count; updates DP MySQL database with dump statistics; notifies ops personnel if discrepancies are encountered (no VC3 file found, ground dump count < telemetered dump count).

### Products and Storage

None.

### Process Logs

None.

### Database Information

A table in the database probe_l0_process is used to store VC3 dump statistics which can be accessed from the web. The database is accessed via the MySQL database server on astraea2.

### Web Information

Dump statistics can be viewed at:

http://themis.ssl.berkeley.edu/data_processing_check/probe_data_processing/list_ssr_stats.php

## L0 Data File Inventory

### Description

Files are created and maintained which contain a list of files for each probe/apid. These files are then used to create a web display which gives quick access to the overall inventory of available L0 files.

### Main Scripts/Programs

A cronjob on gaia2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/list_probe_l0.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_probe_l0_list.ksh

### Products and Storage

list_probe_l0.ksh produces the following files:

th[a-e]_l0_list_nnn.txt

where nnn = apid number (hex)

Each file contains a listing of the L0 files that have been produced for that probe/apid. The files are stored at:

/disks/themisdata/workdir/filelists

gen_probe_l0_list.ksh produces the file:

probe_l0_availability.txt

This file contains an ascii formatted display of L0 availability and can be viewed on the web. It is also found locally at the directory listed above.

### Process Logs

None.

### Database Information

None.

### Web Information

The probe L0 availability display can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory_space_data/probe_l0_availability.txt

## L1 Data File Inventory

### Description

Files are created and maintained which contain a list of files for each probe/dtype. These files are then used to create a web display which gives quick access to the overall inventory of available L1 files.

### Main Scripts/Programs

A cronjob on gaia2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/list_probe_l1.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_probe_l1_list.ksh

### Products and Storage

list_probe_l1.ksh produces the following files:

th[a-e]_l1_list_[dtype].txt

where dtype = eff,efp,efw,esa,fbk,ffp_16,ffp_32,ffp_64,ffw_16,ffw_32,ffw_64,fgm,fit,hsk,mom,scf,scp,scw,spin,state,trg,vaf,vap,vaw,vbf,vbp,vbw

Each file contains a listing of the L1 files that have been produced for that probe/dtype. The files are stored at:

/disks/themisdata/workdir/filelists

gen_probe_l1_list.ksh produces the file:

probe_l1_availability.txt

This file contains an ascii formatted display of L1 availability and can be viewed on the web. It is also found locally at the directory listed above.

### Process Logs

None.

### Database Information

None.

### Web Information

The probe L1 availability display can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory_space_data/probe_l1_availability.txt

## L2 Data File Inventory

### Description

Files are created and maintained which contain a list of files for each probe/instrument. These files are then used to create a web display which gives quick access to the overall inventory of available L2 files.

### Main Scripts/Programs

A cronjob on gaia2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/list_probe_l2.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_probe_l2_list.ksh

### Products and Storage

list_probe_l2.ksh produces the following files:

th[a-e]_l1_list_[instr].txt

where instr = esa,fbk,fgm,scm,sst

Each file contains a listing of the L1 files that have been produced for that probe/instr. The files are stored at:

/disks/themisdata/workdir/filelists

gen_probe_l2_list.ksh produces the file:

probe_l2_availability.txt

This file contains an ascii formatted display of L1 availability and can be viewed on the web. It is also found locally at the directory listed above.

### Process Logs

None.

### Database Information

None.

### Web Information

The probe L2 availability display can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory_space_data/probe_l2_availability.txt

## State Data File Inventory

### Description

Files are created and maintained which contain a list of files for each probe/state-file-version. These files are then used to create a web display which gives quick access to the overall inventory of available state files.

### Main Scripts/Programs

A cronjob on gaia2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/list_probe_state.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_probe_state_list.ksh

### Products and Storage

list_probe_state.ksh produces the following files:

th[a-e]_state_list_v[nn].txt

where nn=00,01,02,03

Each file contains a listing of the state files that have been produced for that probe/version. The files are stored at:

/disks/themisdata/workdir/filelists

gen_probe_state_list.ksh produces the file:

probe_state_availability.txt

This file contains an ascii formatted display of state availability and can be viewed on the web. It is also found locally at the directory listed above.

### Process Logs

None.

### Database Information

None.

### Web Information

The probe state availability display can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory_space_data/probe_state_availability.txt

# Ground Data Processing Activities

Ground magnetometer data from both THEMIS ground based observatories and from external magnetometer networks is collected (downloaded) and processed to CDF using a number of automatic scripts. A brief overview of the process is given here, and details of each script can be found in the subsequent sections.

The magnetometer data available through TDAS can be divided up into a number of networks/groups based on where we retrieve the files from. These groups are:

THEMIS EPO (Education and Public Outreach) magnetometers, installed in US schools;

THEMIS GBO magnetometers;

University of Athabasca GBO (also known as AUTUMN: Athabasca University THEMIS UCLA Magnetometer Network);

University of Alberta GBO (also known as the CARISMA network);

Augsburg College (also known as MACCS network);

University of Alaska (GIMA network);

Greenland (actually Greenland, Denmark, Norway, data from the TGO and DTU networks);

INTERMAGNET (site ABK from SGU network and sites FCC and YKC from NRCan);

USGS (currently only site BRW);

Antarctic (also known as PENGUIN, Virginia Tech).

A list of all of the magnetometer sites available through TDAS can be found at gmag_desc.shtml and further information including longitude and latitude of stations can be found in the spreadsheet http://themis.ssl.berkeley.edu/images/ASI/THEMIS_GMAG_Station_List_Aug_2011.xlsx

For each of the networks an automated script downloads the magnetometer data to /disks/themisdata/thg/mirrors/mag from external servers at least once a day.  The format of the downloaded data depends on the network. Additional scripts process the downloaded files and produce ascii and cdf files, saved to /disks/themisdata/thg/ascii_data/mag/[SITE]/YYYY and /disks/themisdata/thg/l2/mag/[SITE]/YYYY respectively (and available on the THEMIS data website: http://themis.ssl.berkeley.edu/data/themis/).

Note:

- The script ucla_rmd2all.ksh processes THEMIS EPO, GBO, and AUTUMN rmd files to ascii and cdf, also producing intermediate flat files.

- Calibration files are used to produce flat files from rmd files. These calibration files live at /home/thmsoc/software_dev/c_prog/UCLA_Cal. The master calibration files can be found at http://www-ssc.igpp.ucla.edu/themis_data/calib_files/, and are kept up to date by the UCLA EPO team (contact: Kathyrn Rowe, Richard Hart, Max Chung). Changes to the master files need to be monitored so that the versions used by the scripts are kept up to date. Calibration files for AUTUMN are not included on the UCLA site.

Information about files that are downloaded and processed is written to databases on astraea2. The databases are in turn used to generate the status tables showing latest data availability (http://themis.ssl.berkeley.edu/status.shtml).  Scripts are also run to generate ascii tables showing all files available (same website as above). The ascii tables do not rely on database information.

Data from the THEMIS EPO magnetometers undergoes further processing to produce jpg plots for archiving (there is some overlap between sites considered to be THEMIS GBO and EPO). These plots are saved to /disks/horae/raid1/themis_epo/[SITE] and made available at http://sprg.ssl.berkeley.edu/themis/GEONS/SCHOOLS/. Information on the jpg plots produced is written to the EPOMAG database on Juneau. This database is queried by the webform http://sprg.ssl.berkeley.edu/themis/GEONS/ that gives the EPO schools access to the archived plots.

Note that ‘live’ plots are produced by the UCLA server, forwarded to Berkeley, and made available at http://ds9.ssl.berkeley.edu/themis/classroom_geons_data.html. There is no TDAS involvement in the production of the live plots.

Further notes:

- SPDF picks up gmag cdfs from THEMIS (along with all our other cdfs) from ftp://justice.ssl.berkeley.edu/thg/l2/mag.

- Many of the scripts listed here can also be used to reprocess data. Additional reprocessing scripts can be found in /disks/socware/thmsoc_dp_current/src/ksh. Manual reprocessing is best run on the same machine as the corresponding automated script.

- Notes relating to the display of GMAG information on the THEMIS website can be found in Section 6.2.

## UCLA Ground Magnetometer (GMAG) Data Collection – THEMIS GBO

### Description

Raw THEMIS GMAG data is collected from a data server at the University of Calgary.

Point of contact: Contact Harald Frey at (hfrey_at_ssl.berkeley.edu), who is in contact with the relevant people at Calgary.

Calgary status webpage: http://themis-rt.phys.ucalgary.ca:8080/dataflow/summary

Note: Data is occasionally retrieved from Calgary for the BERK magnetometer. This data comes from testing and trouble shooting at Berkeley. When this data is downloaded it may result in a warning message from the processing scripts as no calibration file is available. This data does not need to be processed to CDF so these warnings can be ignored.

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/gbo_uc_rmd_mirror_batch.ksh,

which simply calls

/disks/socware/thmsoc_dp_current/src/ksh/gbo_uc_rmd_mirror.ksh

for the current and previous month.  The script gbo_uc_rmd_mirror.ksh calls the following configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2]/disks/socware/thmsoc_dp_current/src/config/gbo_uc_rmd_mirror.config,

defining the environment variables

from [1] SOC_EMAIL=“jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu”

THEMISDATA="/disks/themisdata"

WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror

from [2] UCB_MIRROR_HOME=${THEMISDATA}/thg/mirrors/mag/ucalgary_rmd

LOGDIR=${THEMISDATA}/process_logs/gbo

LOGFILE=${LOGDIR}/GBO_UC_RMD_MIRROR_Log$(date '+%y%m%d')

WLOGFILE=${LOGDIR}/WGET_GBO_UC_RMD_MIRROR_Log$(date '+%y%m%d')	;

WEBSITE_NAME="http://aurora.phys.ucalgary.ca/data/themis/fluxgate/stream0"

gbo_uc_rmd_mirror.ksh uses wget to connect to the UCalgary server and download any new or updated files, writing a list of any downloaded files to

$GMAGMIRROR/GBO_RMDdirs,

and calling

/disks/socware/thmsoc_dp_current/src /php/gbo_uc_rmd_mirror.php

to update the record of the files collected in the database on the DP MySQL server.

NB: Files were previously retrieved using rsync, this was changed to wget in October 2011 as UCalgary moved their files to an http site. A record of the rsync exchange used to be kept in a database table gbo_ucla_rmd_rsync_stats, updated by the script

/disks/socware/thmsoc_dp_current/src /php/gbo_uc_rmd_mirror_stats.php.

This script is no longer run as it is harder to get download information from wget output.

### Products and Storage

The raw UCLA gmag data files take the form:

[site]YYMMDD_MAG_HH_MM.RMD

where [site] = {CHBG, GBAY, INUV, KAPU, KIAN, KUUJ, MCGR, SNAP, TPAS, WHIT} (and previously included {EKAT, YKNF}, and also PGEO – now an EPO site).

The files are stored locally at:

/disks/themisdata/thg/mirrors/mag/ucalgary_rmd/YYYY/MM/DD

### Process Logs

/disks/themisdata/process_logs/gbo/GBO_UC_RMD_MIRROR_LogYYMMDD

/disks/themisdata/process_logs/gbo/WGET_GBO_UC_RMD_MIRROR_LogYYMMDD_$$

### Database Information

The database gbo_uc_gmag_rmd_mirror is found on the DB MySQL server on astraea2. It contains tables for each GBO station (gbo_[site]_rmdfiles) listing the gmag files collected for each. There is also a table listing rsync statistics (gbo_ucla_rmd_rsync_stats) that was in use prior to October 2011 when the change from rsync to wget was made.

### Web Information

Status on the latest collected files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/gbo_ucla_gmag_table.php

A full inventory of collected files can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_raw_list.txt

## Ground Magnetometer (GMAG) Data Collection – THEMIS EPO

### Description

Raw THEMIS EPO GMAG data is initially collected by the University of California Los Angeles and stored on a data server. A rsync process at UCB pulls new and updated files from this server

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/epo_ucla_rmd_mirror_batch.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

defining the environment variable

CONFIGDIR=${THMSOC}/src/config.

ucla_rmd_mirror_batch.ksh calls

/disks/socware/thmsoc_dp_current/src/ksh/epo_ucla_rmd_mirror.ksh

for each of the present and previous month and for each school in

CONFIGDIR/lc_site_list_ucla_epo_fullname.txt.

epo_ucla_rmd_mirror.ksh loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2]/disks/socware/thmsoc_dp_current/src/config/epo_ucla_rmd_mirror.config

defining the environment variables

from [1]	WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror

from [2]	UCB_MIRROR_HOME=${THEMISDATA}/thg/mirrors/mag/ucla_rmd

UCLALOGDIR=$LOGDIR/gbo/ucla_gmag

LOGFILE=${UCLALOGDIR}/EPO_UCLA_RMD_MIRROR_Log$(date '+%y%m%d')

RSLOGFILE=${UCLALOGDIR}/RSYNC_EPO_UCLA_RMD_MIRROR_Log$(date '+%y%m%d')

RSYNC_OPTIONS_A="-az --log-format=\"%i|%n|%t|%l\" --stats"

REMOTE_SERVER_NAME="themisrsync@gmag-data.igpp.ucla.edu:/THEMIS/fluxgate/epo".

epo_ucla_rmd_mirror.ksh uses rsync to connect to the UCLA server and download any new or updated files, saving a list of any such files to

$GMAGMIRROR/EPO_RMDdirs*

for later processing. The script also calls

epo_ucla_rmd_mirror.php

to update the  record of the files collected in the database on the DP MySQL server, and

epo_ucla_rmd_mirror_stats.php

to  keep a record of the rsync exchange in a database on the DP MySQL server.

### Products and Storage

The raw UCLA gmag data files take the form:

[site]YYMMDD_MAG_HH_MM.RMD,

where [site] = {BMLS, CCNV, DRBY, FYTS, HOTS, LOYS, PGEO, PINE, PTRS, RMUS, SWNO, UKIA}.

The files are stored locally at:

/disks/themisdata/thg/mirrors/mag/ucla_rmd/[site]/YYYY/MM/DD

### Process Logs

/disks/themisdata/process_logs/gbo/ucla_gmag/EPO_UCLA_RMD_MIRROR_LogYYMMDD

/disks/themisdata/process_logs/gbo/ucla_gmag/RSYNC_EPO_UCLA_RMD_MIRROR_LogYYMMDD

NB: Rsync log files older than 10 days are removed by the script rsync_gbo_cleanup.

### Database Information

The database epo_ucla_gmag_rmd_mirror is found on the DB MySQL server on astraea2. It contains tables for each EPO station (epo_[site]_rmdfiles) listing the gmag files collected for each. There is also a table listing rsync statistics (epo_ucla_rmd_rsync_stats).

### Web Information

Status on the latest collected files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/epo_ucla_gmag_table.php

A full inventory of collected files can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_raw_list.txt

## Ground Magnetometer (GMAG) Data Collection – CARISMA

### Description

Some of the THEMIS GBO stations are co-located with a station that is part of an existing ground magnetometer network. Data from five stations of the Canadian Array for Realtime Investigations of Magnetic Activity (CARISMA) are pulled from the main data server at the University of Alberta. Note that data from the magnetometer ATHA and also from the NRCan site SNKQ is also retrieved from the University of Alberta although not part of the CARISMA network.

Additional sites from the CARISMA network are being made available to TDAS users to download directly - the data from the additional sites will not be mirrored, for further information see the IDL load routine thm_load_carisma_gmag.pro.

Points of contact at Alberta:

Ian Mann  ian.mann_at_ualberta.ca,

David Milling dmilling@ualberta.ca

Websites:

http://bluebird.phys.ualberta.ca/carisma/

https://cssdp.ca/ssdp/app/static/data_providers/cgsm/carisma.html

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/gbo_ua_canmag_mirror_batch,

which simply calls

/disks/socware/thmsoc_dp_current/src/ksh/gbo_ua_canmag_mirror,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/gbo_ua_canmag_mirror.config,

defining the environment variables

from [1]	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

GMAGMIRROR=${WORKDIR}/gmag_mirror

from [2] UCB_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ualberta_ascii

UALOGDIR=${LOGDIR}/gbo/carisma_gmag

LOGFILE=${UALOGDIR}/carisma_mirror_log_$(date '+%y%m%d')

RSLOGFILE=${UALOGDIR}/carisma_rsync_results_$(date '+%y%m%d')

REMOTE_SERVER_NAME="carisma_rt@bluebird.physics.ualberta.ca:/data/THEMIS"

RSYNC_OPTIONS="-az  --log-format=\"%i|%n|%t|%l\" --stats".

gbo_ua_canmag_mirror.ksh uses the program rsync to connect to the UAlberta server and download any new or updated files. A list of downloaded files is written to

$GMAGMIRROR/CAN_ASCfiles*

for downstream L2 product creation, the php script

/disks/socware/thmsoc_dp_current/src/php/gbo_ua_canmag_mirror.php

is called to update the record of files collected in the database on the MySQL database server, and the script

/disks/socware/thmsoc_dp_current/src/php/gbo_ua_canmag_mirror_stats.php

is called to keep a record of the rsync exchange in a database on the  MySQL database server.

### Products and Storage

The data recovered from UAlberta is in ASCII format. The file naming convention is:

YYYYMMDD[SITE].Fnn.gz

Where nn = version number, and [SITE]={FSIM, FSMI, GILL, PINA, RANK, SNKQ, ATHA}

The files are stored locally at:

/disks/themisdata/thg/mirrors/mag/ualberta_ascii/YYYY/MM/DD

### Process Logs

/disks/themisdata/process_logs/gbo/carisma_gmag/carisma_mirror_log_yymmdd

/disks/themisdata/process_logs/gbo/carisma_gmag/carisma_rsync_results_yymmdd_*

### Database Information

The database gbo_ua_canmag_mirror is found on the DB MySQL server on astraea2. It contains tables for each GBO station (gbo_[site]_canmagfiles) listing the gmag files collected for each. There is also a table listing rsync statistics (gbo_ua_canmag_rsync_stats).

### Web Information

Status on the latest collected files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/canmag_table.php

A full inventory of collected files can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_raw_list.txt

## Ground Magnetometer (GMAG) Data Collection – GIMA

### Description

Some of the THEMIS GBO stations are co-located with a station that is part of an existing ground magnetometer network. Data from all stations of the Geophysical Institute Magnetometer Array (GIMA) are pulled from the main data server at the University of Alaska.

Point of contact at GIMA:

Bill Hauer uso_at_asf.alaska.edu;

Don Hampton dhampton_at_gi.alaska.edu (PI for magnetometer array)

GIMA website: http://www.asf.alaska.edu/program/gdc/project/magnetometer

Note: Data from GIMA is provided in netcdf format. Considerable information about each station can be found in the netcdf metadata. A convenient IDL netcdf browser can be obtained from http://www.idlcoyote.com/fileio_tips/ncdf_browser.html.

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/gbo_ualaska_mirror_batch

loading the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

which defines the environment variable

CONFIGDIR=${THMSOC}/src/config.

This script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/gbo_ualaska_mirror.ksh

for the current (and possibly last) year, and for each site listed in

${CONFIGDIR}/gima_network.txt.

gbo_ualaska_mirror.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/gbo_ualaska_mirror.config,

which define the environment variables

from [1]	WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	UCB_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ualaska_netcdf

GIMALOGDIR=$LOGDIR/gbo/gima_gmag

LOGFILE=${GIMALOGDIR}/gima_mirror_log_$(date '+%y%m%d')

RSLOGFILE=${GIMALOGDIR}/gima_rsync_results_$(date '+%y%m%d')

RSYNC_OPTIONS_A="-az --log-format=\"%i|%n|%t|%l\" --stats"

REMOTE_SERVER_NAME=“gima@gwa.asf.alaska.edu:/sc2/magnet/sites”.

gbo_ualaska_mirror.ksh uses the program rsync to connect to the UAlaska server and download any new or updated files. A list of new or updated files is copied to

${GMAGMIRROR}/GIMA_NC2ALL*

for downstream L2 product creation, the php script

/disks/socware/thmsoc_dp_current/src /php/gbo_ualaska_mirror.php

is called to update the record of the files collected in the database on the  MySQL server, and the php script

/disks/socware/thmsoc_dp_current/src /php/gbo_ualaska_mirror_stats.php

is called to record the rsync exchange in a database on the MySQL server.

### Products and Storage

The data recovered from UAlaska is in netcdf format. The file naming convention is:

YYYY[SITE]DOY-HH.nc

where [SITE] = {Arctic, Bettles, CIGO, Eagle, FtYukon, Gakona, HLMS, Homer, Kartovik, Poker, Trapper}

The files are stored locally at:

/disks/themisdata/thg/mirrors/mag/ualaska_netcdf/[site]/YYYY

### Process Logs

/disks/themisdata/process_logs/gbo/gima_gmag/gima_mirror_log_YYMMDD

/disks/themisdata/process_logs/gbo/gima_gmag/gima_rsync_results_YYMMDD

Note: the gima_rsync_results* logfiles are currently used to write the record of the rsync exchange to the database, but are deleted upon completion of the process.

### Database Information

The database gbo_alaska_mirror is found on the DB MySQL server on astraea2. It contains tables for each GBO station (gbo_[site]_magfiles) listing the gmag files collected for each. There is also a table listing rsync statistics.

### Web Information

Status on the latest collected files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/alaska_table.php

A full inventory of collected files can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_raw_list.txt

## Ground Magnetometer (GMAG) Data Collection – MACCS

### Description

Magnetometer data from magnetometers in the MACCS (Magnetometer Array for Cusp and Cleft Studies) network is retrieved from Augsburg College

Point of contact at Augsburg:

Erik Steinmetz steinmee_at_augsburg.edu

MACCS website:

http://space.augsburg.edu/ (formerly yspace.augsburg.edu)

Note: MACCS data is provided in local geomagnetic coordinates.  Some data on the MACCS website is rotated from local coordinates to geographic coordinates, but the data we retrieve is all in local magnetic coordinates.  If any further back data is downloaded it should be checked carefully to ensure it is in local magnetic coordinates.

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/call_wget_maccs_gmag.ksh

loading the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

which defines the environment variable

CONFIGDIR=${THMSOC}/src/config.

This script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/wget_maccs_gmag.ksh

for the current (and possibly last) year, and for each site listed in

${CONFIGDIR}/maccs_site_list.txt.

wget_maccs_gmag.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/wget_maccs_gmag.config,

which define the environment variables

from [1]	LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror

PHP_SCRIPTS=${THMSOC}/src/php

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	WEBSITE="ftp://yspace.augsburg.edu/MACCS_DATA/IAGA2000/"

LOCALWEBMIRROR="${THEMISDATA}/thg/mirrors/mag/maccs_ascii"

in addition, the following variables are defined:

LOGFILE=${LOGDIR}/webdownloads/maccs_gmag_log_ $(date '+%y%m%d')_$$

WGETLOG=${LOGDIR}/webdownloads/wget_output_maccs_gmag_ $(date '+%y%m%d').

wget_maccs_gmag.ksh uses the program wget to connect to the Augsburg server and download files. Files are copied to

${GMAGMIRROR}/

for downstream L2 product creation, and the php script

/disks/socware/thmsoc_dp_current/src /php/wget_maccs_gmag.php

is called to update the record of the files collected in the database on the MySQL server.

### Products and Storage

The data recovered from Augsburg is in ASCII format according to IAGA2000 guidelines. The file naming convention is:

[SITE]YYYYMMDD_10_sec.sec

where [SITE] = {CDR, CRV, GJO, IGL, NAN, PGG, RBY}.

The files are stored locally at:

/disks/themisdata/thg/mirrors/mag/maccs_ascii/[site]/YYYY.

### Process Logs

/disks/themisdata/process_logs/webdownloads/maccs_gmag_log_YYMMDD

/disks/themisdata/process_logs/webdownloads/wget_output_maccs_gmag_YYMMDD

Note that these process logs are cleaned up by the script gmag_webdownloads_cleanup.ksh (see section below).

### Database Information

The database web_downloads is found on the DB MySQL server on astraea2. It contains a table augsburg_maccs_gmag, listing the gmag files collected from the network.

### Web Information

Status on the latest collected files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/maccs_table.php

A full inventory of collected files can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_raw_list.txt

## Cleanup after GMAG data download

### Description

Cleanup old log files associated with the collection of gmag files from web-based servers (namely MACCS data).

### Main Scripts/programs

A cronjob on gaia2 launches the following script

/disks/socware/thmsoc_dp_current/src/ksh/gmag_webdownloads_cleanup.ksh,

which calls the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variable

LOGDIR=${THEMISDATA}/process_logs.

The script deletes files found in

${LOGDIR}/webdownloads

that are older than 14 days.

### Products and Storage

None.

### Process logs

None.

### Database Information

None.

### Web Information

None.

## Ground Magnetometer (GMAG) Data Collection – Athabasca

### Description

Some of the THEMIS GBO stations are co-located with a station that is part of an existing ground magnetometer network.  Magnetometer data from magnetometers in the AUTUMN network is retrieved from U Athabasca. Note that the sites currently retrieved are LARG, LETH, REDR, and ROTH. The site located at Athabasca (ATHA) is not retrieved from Athabasca. It is instead downloaded from Alberta.

Website:

http://autumn.athabascau.ca/

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/gbo_atha_rmd_mirror_batch.ksh

loading the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config.

This script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/gbo_atha_rmd_mirror.ksh

for the current (and possibly last) month, and for each of the sites: LETH ROTH REDR LARG.

gbo_atha_rmd_mirror.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/gbo_atha_rmd_mirror.config,

which define the environment variables

from [1]	WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	ATHA_MIRROR_HOME=${THEMISDATA}/thg/mirrors/mag/uatha_rmd

LOGDIR=${THEMISDATA}/process_logs/gbo

LOGFILE=${LOGDIR}/GBO_ATHA_RMD_MIRROR_Log$(date '+%y%m%d')

RSLOGFILE=${LOGDIR}/RSYNC_GBO_ATHA_RMD_MIRROR_Log$(date '+%y%m%d')

REMOTE_SERVER_NAME="themis@131.232.13.43:/autumndp/L0/"

RSYNC_OPTIONS="-az --port=8873 --log-format=\"%i|%n|%t|%l\" --stats"

gbo_atha_rmd_mirror.ksh uses the program rsync to connect to the UAthabasca server and download new or updated files. A list of downloaded files is written to

${GMAGMIRROR}/ATH_RMDdirs$$

for downstream L2 product creation.

### Products and Storage

The data recovered from Athabasca is in RMD format. The file naming convention is:

[SITE]YYYYMMDD_MAG_HH_MM.RMD

where [SITE] = {LARG, LETH, ROTH, REDR}.

The files are stored locally at:

/disks/themisdata/thg/mirrors/mag/uatha_rmd/[site]/YYYY/MM/DD/.

### Process Logs

/disks/themisdata/process_logs/gbo/GBO_ATHA_RMD_MIRROR_LogYYMMDD

/disks/themisdata/process_logs/gbo/RSYNC_GBO_ATHA_RMD_MIRROR_LogYYMMDD

NB: rsync log files older than 10 days are removed by rsync_gbo_cleanup.ksh.

### Database Information

The database gbo_uatha_rmd_mirror is found on the DB MySQL server on astraea2. It contains tables for each station (gbo_[site]_rmdfiles) listing the gmag files collected for each. There is also a table listing rsync statistics. Note that this database was setup in September 2011 so earlier rsync statistics are not captured.

### Web Information

Status on the latest collected files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/autumn_ucla_gmag_table.php

## Ground Magnetometer (GMAG) Data Collection – Greenland/Denmark/Norway

### Description

Data from magnetometers in the DTU (Technical University of Denmark) and TGO (Tromsø Geophysical Observatory) networks is retrieved from TGO.

For information on these networks see:

TGO:

http://geo.phys.uit.no/

DTU:

Point of contact:

Claudia Stolle cst_at_space.dtu.dk

Website:

http://www.space.dtu.dk/English/Research/Scientific_data_and_models/Magnetic_Ground_Stations.aspx

Note:

- TGO data is available in 10 sec or 1 min resolution. DTU data is available only in 1 min resolution (if 10 sec data is requested, the resulting data is generated from the 1 min data).  The current script downloads 1 min data for both TGO and DTU as there have not been any specific requests for 10 sec TGO data. If the resolution downloaded is changed in the future, changes are needed in a number of places in download and processing to cdf as the file names are given suffix .min for min resolution.

- Uncalibrated 1 sec data from DTU is being made available gradually. See ftp://ftp.spacecenter.dk/data/Ground_magnetometers/Adjusted/ for this data. This data is in geographic coordinates.

- Data can be downloaded from the Tromsø website in DHZ, XYZ geographic, or XYZ sensor (also referred to as HEZ) coordinates.

- In DHZ D is the declination measured in minutes of arc (not degrees) from geographic north, H is the strength of the field in the horizontal plane measured in nT, Z is the field strength in the vertical direction.  The XY geographic values are effectively: X = H cos(D/60), Y = H sin(D/60) (arguments in degrees).

The sensor XYZ (or XYZ(2) on the webform) data is uncalibrated raw sensor output. The XYZ sensor values give the variation of the field in the X (local magnetic north), Y (local magnetic east), and Z (vertical) directions. The following information is from Claudia Stolle and Jürgen Matzka at DTU:

Sensor XYZ has the following disadvantages, which for many applications are not critical:
-The numbers represent only variations of the field determined from an arbitrary level
-The scale values are not always exactly nT but might deviate by typically 3 %.
-The direction of H and D can be wrong by several degrees.

If you want to achieve the optimum data quality, you should use from Tromsø or from our ftp site data in XYZ geographic and then rotate the XY by the local geomagnetic declination found from a field model.

Truls Hansen at TGO additionally points out that some of the TGO sites have DIF rather than DHZ sensor orientation. This could cause confusion.

The current script downloads data in XYZ GEOGRAPHIC coordinates (as of May 2012).  The data is rotated to local geomagnetic coordinates in the processing to CDF, using declination angles provided by Truls Hansen. The declination angles are stored in the mastercdf.

### Main Scripts/Programs

A cronjob on gaia2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/call_wget_green_gmag.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/wget_green_gmag.config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

from [2]	DAYSTOCHECK=10

DAYSOFLAG=1.

This script loops through days beginning DAYSTOCHECK+DAYSOFLAG days ago for DAYSTOCHECK number of days.

For each date the script loops through the sites listed in

/disks/socware/thmsoc_dp_current/src/config/green_site_list_new.txt

calling the script

/disks/socware/thmsoc_dp_current/src/ksh/wget_green_gmag.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2]/disks/socware/thmsoc_dp_current/src/config/wget_green_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

from [2]	WEBSITE="http://flux.phys.uit.no/cgi-bin/mkascii.cgi"

WEBOPTS="res=1min\&pwd=NewAsc56\&format=iagaUnix\&comps=DHZ\&getdata=+Get+Data+"

LOCALWEBMIRROR ="${THEMISDATA}/thg/mirrors/mag/greenland_ascii/flux.phys.uit.no"

GMAGWORKDIR="${WORKDIR}/greenMag2Do".

The script runs /usr/bin/wget to retrieve files from the TGO website. Retrieved files are renamed

green_SITE_YYYYMMDD_min.min,

and saved in

$LOCALWEBMIRROR/SITE/YYYY/MM,

and copied to

$GMAGWORKDIR

for downstream processing.

### Products and Storage

The files are retrieved from TGO as ‘unix’ format and named with file name convention

green_{SITE}_YYYYMMDD_min.min

(filenames almost conform to IAGA2002 standards, original name of file as downloaded is the last part of the web address for the file and thus not suitable).

NB: SITE here is a 5 character alphanumeric code that begins with the three letter station code (the short and long codes can be found in green_site_list_new.txt). The final two characters for each station can change, so if there is a failure to retrieve data from a site the code should be checked by manually retrieving data using the webform: http://flux.phys.uit.no/ascii/ (settings for this form are found in the WEBOPTS variable listed above).

The files contain ASCII IAGA2002 formatted data except where a query has failed, in which case the html file may display for example “Cannot open datafile ?? No data”.

These files are stored locally at

/disks/themisdata/thg/mirrors/mag/greenland_ascii/flux.phys.uit.no/SITE/YYYY/MM

### Process Logs

/disks/themisdata/process_logs/webdownloads/green_gmag_log_${processdate}

/disks/themisdata/process_logs/webdownloads/wget_output_green_gmag_${processdate}_${site}

NB: The webdownloads directory is periodically cleaned out by the script

/disks/socware/thmsoc_dp_current/src/ksh/gmag_webdownloads_cleanup.ksh

### Database Information

None.

NB: There is a table greenland_nrsq_gmag in the database web_downloads. This table was used when the site NRSQ/NAQ was retrieved via a different process. It is no longer in use.

### Web Information

None.

## Ground Magnetometer (GMAG) Data Collection – INTERMAGNET

### Description

Data from different magnetometer networks made available through INTERMAGNET is downloaded via ftp. The current sites retrieved from INTERMAGNET are:

ABK (Abisko, Sweden)

This site is run by the Geological Survey of Sweden. It is one of the sites used to generate the Kyoto AE indices.

The current data available is 1 min resolution, 1 sec resolution may become available in the future.

Website: http://www.sgu.se/sgu/eng/geol_kartering/geomagn_dok/index.html

Contact name: Gerhard Schwarz gerhard.schwarz@sgu.se

FCC (Fort Churchill, Canada), YKC (Yellowknife, Canada)

These two sites are run by NRCan (Natural Resources Canada/Geological Survey of Canada). They are also used in the generation of the Kyoto AE indices.

1 sec resolution data is available.

Website: http://gsc.nrcan.gc.ca/geomag/data/index_e.php

Contact names: David Calp david.calp@nrcan-rncan.gc.ca , Jennifer Parmelee Jennifer.parmelee@nrcan-rncan.gc.ca

David Calp is the first point of contact and is listed as the PI in the FCC and YKC cdfs. His full details are:

David Calp 
Physical Scientist, Geomagnetism 
 Natural Resources Canada 
 Canadian Hazards Information Service 
 Telephone: 613-837-1757 
 Fax: 613-824-9803 
 Email: David.Calp@nrcan.gc.ca

Any use of the FCC and YKC data should include the following acknowledgment:

The Canadian Magnetic Observatory Network (CANMON), maintained
 and operated by the Geological Survey of Canada, provided the
 data used in this study - http://www.geomag.nrcan.gc.ca.

The following rules of use apply:

Geomagnetic data are provided for your use and are not for sale
 or distribution by you to third parties, without the express
 written permission of the Geological Survey of Canada (GSC). Any
 report or publication that makes use of these data should
 acknowledge the Geological Survey of Canada as the source. One
 copy of each report or publication should be sent to the GSC.
 
 We ask that the data not be used for commercial purposes, nor in
any project in which you, your organization, or your collaborators are in a commercial agreement with any third party.  Commercial users may contact the Geological Survey of Canada at the address below:

Geomagnetic Laboratory                                           
 Geological Survey of Canada
 Natural Resources Canada
 7 Observatory Crescent
 Ottawa, ON
 Canada
 K1A 0Y3
 Phone: 613-837-4241
 Fax: 613-824-9803
 Website: http://www.geomag.nrcan.gc.ca.

Note:

- Permission must be obtained from the relevant institute before data from any other sites is mirrored from INTERMAGNET.

- There are multiple datatypes available through INTERMAGNET: variation, provisional, quasi-definitive, definitive. The scripts download variation data as there is a delay before definitive data is produced and shipped to INTERMAGNET. Definitive data was downloaded for 2009 and earlier. To download definitive (or other data) have a copy of the script call a modified version of intermagnet_site_list.txt.

- The contact for INTERMAGNET was Jennifer Parmelee (NRCan) above, now Charles Blais chblais_at_nrcan.gc.ca or Randy Shaughnessy rshaugn_at_nrcan.gc.ca.

- The current sites downloaded through INTERMAGNET provide data in geographic XYZ coordinates. The data is converted to HDZ in the processing to CDF (as of April 2012).

### Main Scripts/Programs

A cronjob on gaia2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/call_wget_intermagnet_gmag.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variable

CONFIGDIR=${THMSOC}/src/config.

The script reads the gmag site, datatype, and resolution to download from the file

/disks/socware/thmsoc_dp_current/src/config/intermagnet_site_list.txt,

and calls the script

/disks/socware/thmsoc_dp_current/src/ksh/wget_intermagnet_gmag.ksh

for each site and the current and previous month.

The script wget_intermagnet_gmag.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/wget_intermagnet_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

PHP_SCRIPTS=${THMSOC}/src/php

from [2] WEBSITE=ftp://ftp.intermagnet.org

LOCALWEBMIRROR="${THEMISDATA}/thg/mirrors/mag/intermagnet_ascii"

GMAGWORKDIR="${WORKDIR}/intermagnet2do".

wget_intermagnet_gmag.ksh calls /usr/bin/wget to download new or updated gmag files from the ftp site. Information on the downloaded files is written to the database on astraea2 by the script

/disks/socware/thmsoc_dp_current/src/php/wget_intermagnet_gmag.php.

A copy of the downloaded file is placed in the directory

/disks/themisdata/workdir/intermagnet2do

for downstream processing to CDF.

### Products and Storage

Downloaded data files are stored at

/disks/themisdata/thg/mirrors/mag/intermagnet_ascii/SITE/YYYY/MM

and follow file naming convention

SITEYYYYM MDDvRES.RES

where SITE is the three letter code for the site, RES is either sec or min e.g. abk20110101vmin.min.

NB: Some files are downloaded in gzipped form.

### Process Logs

/disks/themisdata/process_logs/webdownloads/intermagnet_gmag_log_YYMMDD

/disks/themisdata/process_logs/webdownloads/wget_output_intermagnet_gmag_YYMMDD_SITE_$$

### Database Information

Information on the downloaded files is stored in the table intermagnet_gmag in the database web_downloads on astraea2.

### Web Information

None as yet.

## Ground Magnetometer (GMAG) Data Collection – US Geological Survey

### Description

Data from USGS sites is downloaded using wget.

As of December 2011 the only USGS site we are retrieving is Barrow (BRW), as it is one of those used in to generate the Kyoto AE indices. The data downloaded is 1 second resolution raw (variation) data, in IAGA2002 format.

Website: http://geomag.usgs.gov/

Contact: Duff Stewart dcstewart_at_usgs.gov

Note:

- Data prior to October 2011 was made available in zipped monthly files at the ftp site ftp://hazards.cr.usgs.gov/Geomag/OneSecData/BRW1sec/

This data is in a slightly different format, either .raw or .Sec files. The components listed are H, E, Z, where H is the raw value in the local magnetic north direction, E is the value in the local magnetic east direction, and Z is the value in the vertical north direction. The .raw files are give data in units of 0.001nT, the .Sec files in units of 0.01nT. All data written to cdf is in units of nT.

- The IAGA2002 data is in HDZ coordinates. For variation data H and Z are again the values in local magnetic north and vertical directions. D is the raw declination in minutes calculated from E (value in east direction) using the approximate equation D = 3437.7468 E/H (~arctan(E/H)). (Data recorded in CDF is H E Z corresponding to the THEMIS HDZ system).

- Duff Stewart also supplied the following useful information:

  - Difference between the recorded "H" and the true Horizontal field:

Note that although the H sensor detects most of the horizontal field, the true total horizontal field is the vector sum of the H and E values: Htotal = SQRT( H^2 + E^2), the contribution of E is usually negligible for low-latitude observatories but can be significant for high latitudes like BRW.

  - Difference between the recorded "D" and the true declination: Because the H and E sensors are aligned to magnetic (rather than geographic) north/south and east/west, the recorded "D" represents the variation of declination angle rather than the total declination. The total declination is the recorded D plus a baseline: Dtotal = D + Dbaseline, where Dbaseline is the approximate geographic declination angle at the observatory's location.

### Main Scripts/Programs

A cronjob on gaia2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/call_wget_usgs_gmag.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variable

CONFIGDIR=${THMSOC}/src/config.

The script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/wget_usgs_gmag.ksh

for each site and the current and previous month.

The script wget_usgs_gmag.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/wget_usgs_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

PHP_SCRIPTS=${THMSOC}/src/php

from [2] WEBSITE= http://geomag.usgs.gov/data/magnetometer/

LOCALWEBMIRROR="${THEMISDATA}/thg/mirrors/mag/usgs_ascii"

GMAGWORKDIR="${WORKDIR}/usgs2do".

wget_usgs_gmag.ksh calls /usr/bin/wget to download new or updated gmag files from the ftp site. Information on the downloaded files is written to the database on astraea2 by the script

/disks/socware/thmsoc_dp_current/src/php/wget_usgs_gmag.php.

A copy of the downloaded file is placed in the directory

/disks/themisdata/workdir/usgs2do

for downstream processing to CDF.

### Products and Storage

Downloaded data files are stored at

/disks/themisdata/thg/mirrors/mag/usgs_ascii/SITE/YYYY/MM

and follow file naming convention

SITEYYYYM MDDvsec.sec

where SITE is the three letter code for the site, e.g. brw20110101vsec.sec

### Process Logs

/disks/themisdata/process_logs/webdownloads/usgs_gmag_log_YYMMDD

/disks/themisdata/process_logs/webdownloads/wget_output_usgs_gmag_YYMMDD_SITE_$$

### Database Information

Information on the downloaded files is stored in the table usgs_gmag in the database web_downloads on astraea2.

### Web Information

None as yet.

## Ground Magnetometer (GMAG) Data Collection – Antarctic sites (PENGUIN)

### Description

Data from the Antarctic magnetometers PG1 and PG2 is downloaded using wget.

At the request of the providers, data from the Antarctic gmags has been included in the THEMIS database for use with TDAS. The data is provided to us as CDFs that should be compliant with TDAS. The coordinate system matches the THEMIS HDZ coordinates (local magnetic north, east, vertical).

All data is 1 second raw magnetometer telemetry. NB: it may be that data is not retrieved during Antarctic winter.

Data can be browsed at http://mist.nianet.org/CDFdata/, or accessed via ftp at mist.nianet.org (port 21, username THEMIS,  password Angelopoulos), or via WebDAV ftp interface at mist.nianet.org:8080 (same username and password).

Although no processing to CDF is required, a processing script is used to generate ASCII files of the data (consistent with the other gmag data that TDAS stores). See Section 4.22 for information on the processing script.

Contact names (at Virginia Tech):

Bob Clauer	 rclauer_at_vt.edu (General information/requests)

Daniel Weimer 	dweimer_at_vt.edu (Data availability/format - responsible for producing CDFs)

Website: http://mist.nianet.org/

### Main Scripts/Programs

A cronjob on gaia2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/call_wget_antarctic_gmag.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variable

CONFIGDIR=${THMSOC}/src/config.

The script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/wget_antarctic_gmag.ksh

for each site (PG1 and PG2) for the current year. The script is also called for the previous year if the current month is January. Note that the scripts are called for the full year simply because the data is organized only by year and not by month.

The script wget_antarctic_gmag.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/wget_antarctic_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

PHP_SCRIPTS=${THMSOC}/src/php

from [2] WEBSITE= “ftp://mist.nianet.org/CDF”

GMAGWORKDIR="${WORKDIR}/antarctic2do"

TEMPDIR="${WORKDIR}/temp_dir/antarctic_temp"

L2MAGDIR=${THEMISDATA}/thg/l2/mag.

wget_antarctic_gmag.ksh calls /usr/bin/wget to download new or updated gmag  CDF files from the ftp site. Information on the downloaded files is written to the database on astraea2 by the script

/disks/socware/thmsoc_dp_current/src/php/gmag_cdf.php.

A copy of the downloaded file is placed in the directory

/disks/themisdata/workdir/antarctic2do

for downstream processing to ASCII.

### Products and Storage

Downloaded data files are stored in the same location as standard gmag cdf files

/disks/themisdata/thg/l2/mag/SITE/YYYY/

and follow the standard file naming convention

thg_l2_mag_SITE_YYYYMMDD_v01.cdf

where SITE is the three letter code for the site: pg1 or pg2.

### Process Logs

/disks/themisdata/process_logs/webdownloads/antarctic_gmag_log_YYMMDD

/disks/themisdata/process_logs/webdownloads/wget_output_antarctic_gmag_YYMMDD_SITE_$$

### Database Information

Information on the downloaded files is stored in the database gmag_cdf  on astraea2, in tables gbo_PG1_cdffiles and gbo_PG2_cdffiles.

### Web Information

The sites PG1 and PG2 will be included in the table at http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php.

## Ground Magnetometer (GMAG) Data Collection – Leirvogur

### Description

Data from the Leirvogur magnetometer is downloaded using wget.

Website: http://www.raunvis.hi.is/~halo/lrv.html

Contact: Gunnlaugur Björnsson gulli@hi.is

Note:

- The Leirvogur magnetometer in Iceland is one of the magnetometers used to generate the Kyoto AE indices.

- Preliminary 10 second resolution data is available daily from the ftp site: ftp://ftp.raunvis.hi.is/pub/lrv/

Monthly 1 minute resolution definitive data is made available at the beginning of each month, for the previous month. At this point the 10 second files are deleted from the ftp site.

This routine downloads both sets of data (Note that a check of April 2012 files showed no appreciable difference between the preliminary and the definitive data).

- Lerivogur data is provided in standard coordinates: H is the total horizontal field magnitude in nT; D is the declination angle between geographic north and the H vector, in 1/10000 radians in this case; Z is the field magnitude in the vertical direction in nT. The data will be rotated to approximate local geomagnetic coordinates when processed to CDF.

### Main Scripts/Programs

A cronjob on gaia2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/call_wget_lrv_gmag.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variable

CONFIGDIR=${THMSOC}/src/config.

The script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/wget_lrv_gmag.ksh

for the current year, and the previous year if it is currently January.

The script wget_lrv_gmag.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/wget_lrv_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

PHP_SCRIPTS=${THMSOC}/src/php

from [2] WEBSITE= ftp://ftp.raunvis.hi.is/pub/lrv								LOCALWEBMIRROR="${THEMISDATA}/thg/mirrors/mag/lrv_ascii"

GMAGWORKDIR="${WORKDIR}/lrv2do".

wget_lrv_gmag.ksh calls /usr/bin/wget to download new or updated gmag files from the ftp site. The script checks for both daily 10 second resolution files and monthly 1 minute resolution files.

Information on the downloaded files is written to the database on astraea2 by the script

/disks/socware/thmsoc_dp_current/src/php/wget_lrv_gmag.php.

A copy of the downloaded 10 second resolution files only is placed in the directory

/disks/themisdata/workdir/lrv2do

for downstream processing to CDF.

### Products and Storage

Downloaded data files are stored at

/disks/themisdata/thg/mirrors/mag/lrv_ascii/SITE/YYYY

and follow file naming convention

YYDOY.sec.gz

for daily 10 second resolution files, and

lrvYYmonth.min

for monthly files eg 12001.sec.gz and lrv12jan.min.

### Process Logs

/disks/themisdata/process_logs/webdownloads/lrv_gmag_log_YYMMDD

/disks/themisdata/process_logs/webdownloads/wget_output_lrv_gmag_YYMMDD_SITE_$$

### Database Information

Information on the downloaded files is stored in the table lrv_gmag in the database web_downloads on astraea2.

### Web Information

None as yet.

## Ground Magnetometer (GMAG) Data Collection – AARI

### Description

Data from the Russian magnetometers in the AARI network are downloaded using rsync.

Website: http://www.aari.ru/clgmi/geophys/index.html

Contact: Oleg Troshichev olegtro@aari.nw.ru

Alexander Janzhura alex_j@aari.ru (for queries relating to data format, availability, download etc).

Note:

- Currently we have data from AMD, DIK, PBK, TIK.

- Data is downloaded in IAGA2002 format, in H E Z coordinates. The data provided is the variation, but the baseline is unknown. AARI suggested that in the near future they intend to install new instruments that would allow absolute measurements.

- Details for the AARI server are in the download script described below. A pair of SSH keys has been set up to allow password-less access for download. A password has been provided to us - if needed it is available in the emails from Alexander Janzhura.

### Main Scripts/Programs

A cronjob on gaia2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/call_aari_gmag_mirror.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variable

CONFIGDIR=${THMSOC}/src/config.

The script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/aari_gmag_mirror.ksh

for the current and previous month.

The script aari_gmag_mirror.ksh  loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/aari_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

PHP_SCRIPTS=${THMSOC}/src/php

from [2] REMOTE_SERVER_NAME="themis@193.227.232.172:"

RSYNC_OPTIONS_A="-az --log-format=\"%i|%n|%t|%l\" --stats"				UCB_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/aari_ascii

AARILOGDIR=$LOGDIR/webdownloads/aari_gmag

GMAGWORKDIR="${WORKDIR}/aari2do"

TEMPDIR="${WORKDIR}/temp_dir/aari_temp".

aari_gmag_mirror.ksh calls /usr/bin/rsync to download new or updated gmag files from the AARI server site.

Information on the downloaded files is written to the database web_downloads on astraea2 by the script

/disks/socware/thmsoc_dp_current/src/php/aari_gmag.php.

A copy of the downloaded is placed in the directory

/disks/themisdata/workdir/aari2do

for downstream processing to CDF.

### Products and Storage

Downloaded data files are stored at

/disks/themisdata/thg/mirrors/mag/aari_ascii/SITE/YYYY/MM

and follow file naming convention

SITEYYYYMMDDvmin.min,

where SITE={amd, dik, pbk, tik}

### Process Logs

/disks/themisdata/process_logs/webdownloads/aari_gmag/aari_gmag_mirror_log_YYMMDD

/disks/themisdata/process_logs/webdownloads/aari_gmag/rsync_output_aari_gmag_YYMMDD_SITE_$$

### Database Information

Information on the downloaded files is stored in the table aari_gmag in the database web_downloads on astraea2.

### Web Information

None as yet.

## Ground Magnetometer (GMAG) Data Collection – Monitor

### Description

Monitor the reception of GMAG data from all external sites and notify ops personnel when data is not being received.

### Main Scripts/Programs

A cronjob on gaia launches the following script (disabled 25 Sep 09):

/disks/socware/thmsoc_dp_current/src/ksh/chk4late_gmag.ksh

Additional scripts:

/disks/socware/thmsoc_dp_current/src/php/get_last_filetime.php – Checks the various databases for the time of last file received. Notifies ops personnel if time limits are exceeded.

### Products and Storage

None.

### Process Logs

None.

### Database Information

The various databases on the MySQL server that store gmag collection information are queried for the time of the last file received. For particular databases, check the collection sections of this document.

### Web Information

None.

## Ground Magnetometer (GMAG) Data – Convert Raw GBO Data to Level 2 (L2) CDF Data Product

### Description

The raw GBO GMAG data is converted into calibrated physical units and stored in CDF format. The CDF files are stored on the DP server and are available for download via http.

Note: Data is occasionally retrieved from Calgary for the BERK magnetometer. This data comes from testing and trouble shooting at Berkeley. When this data is downloaded it may result in a warning message from the processing scripts as no calibration file is available. This data does not need to be processed to CDF so these warnings can be ignored.

### Main Scripts/Programs

A cronjob on auxo launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/ucla_rmd2all.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ucla_rmd2all.config,

defining the environment variables

from [1]	WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	LOGDIR=/disks/themisdata/process_logs/ucla_rmd2all

LOGFILE=${LOGDIR}/UCLA_RMD2ALL_Log$(date '+%y%m%d')

EPO_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ucla_rmd

ATHA_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/uatha_rmd

GBO_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ucalgary_rmd

TABLE_FILES_DIR=/home/thmsoc/software_dev/c_prog/UCLA_Cal

UCB_FLAT_HOME=/disks/themisdata/thg/l1/mag

RMD2FFPATH=/home/thmsoc/software_dev/c_prog/leel_rmd_noleap/code

FFMERGEPATH=/home/thmsoc/software_dev/c_prog/ffmerge/bundle

KSHSCRIPTS=/home/thmsoc/software_dev/ksh.

This script checks the directory /disks/themisdata/workdir/gmag_mirror for files like GBO_RMDdir*, EPO_RMDdir*, and ATH_RMDdir*, which contain information on the station and date of the raw data to process into CDF (Level 2) products. The script checks whether a calibration file exists for each site at

${TABLE_FILES_DIR}/${site}.txt.

The program

/home/thmsoc/software_dev/c_prog/leel_rmd_noleap/code/RMD2FF

is called on each RMD file. This is UCLA supplied C-code that has been compiled for Solaris only (which is why this is running on auxo). This code converts the raw RMD file into an intermediate “Flat File” format, also using the calibration file.

Resulting hourly flat files are merged into a single flat file for each day using the program

/home/thmsoc/software_dev/c_prog/ffmerge/bundle/ffmergesungnucmp

(more UCLA supplied C-code to merge the hourly Flat Files created by the RMD2FF program). The daily flat files are stored at

/disks/themisdata/thg/l1/mag/[SITE]/YYYY/

with filename

BYYDOY_[SITE}.ffd and BYYDOY_[SITE].ffh.

The script

${KSHSCRIPTS}/date2doy

is called to convert the dates in the filename from format YYMMDD to YYDOY.

ucla_rmd2all.ksh then calls the script

/disks/socware/thmsoc_dp_current/src/ksh/ucla_flat2cdf.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/setup_themis_UCLA.borne

[2] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[3] /disks/socware/thmsoc_dp_current/src/config/ucla_rmd2all.config,

defining the environment variables

from [1]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_UCLA_FF_DIR=$THMSOC/idl/thmsoc/ucla_ff

IDL_DIR=/disks/apollo/export/idl_${idl_level}

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_UCLA_FF_DIR

IDL_STARTUP=cdf_startup.pro

IDL_DEVICE=Z

from [2]	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

WORKDIR=${THEMISDATA}/workdir

WORKMAGSTACKS=${WORKDIR}/magStacks2Do

from [3]	UCB_FLAT_HOME=/disks/themisdata/thg/l1/mag

DATA_ROOT=/disks/themisdata

L2MAGDIR=${DATA_ROOT}/thg/l2/mag

CDFMASTERS=${THMSOC}/src/mastercdfs/thg/

KSHSCRIPTS=/home/thmsoc/software_dev/ksh.

LOGFILE=${LOGDIR}/UCLA_RMD2ALL_Log$(date '+%y%m%d')

ucla_flat2cdf.ksh runs the IDL routine uff2cdf to convert Flat Files to CDF Level 2 data products. This IDL routine also makes use of the mastercdfs located at

${CDFMASTERS}/thg_l2_mag_[SITE]*,

and copied to

${L2MAGDIR}/garage/mastercdfs

for processing.

Resulting CDFS are copied to the directory

${L2MAGDIR}/[SITE]/YYYY

with filenames

thg_l2_mag_[SITE]_YYYYMMDD_v01.cdf.

The script

${KSH_SCRIPTS}/fileChkSum.ksh

is used to update the checksum file.

The date of the processed file is copied to a file

${WORKMAGSTACKS}/stack_YYYYMMDD_*

for downstream stackplot production.

The php script

gmag_cdf.php

is run to update the MySQL database with process results information.

ucla_rmd2all.ksh then calls the script

/disks/socware/thmsoc_dp_current/src/ksh/ucla_flat2ascii.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/setup_themis_UCLA.borne

[2] /disks/socware/thmsoc_dp_current/src/config/ucla_rmd2all.config

[3] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variables

from [1]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_UCLA_FF_DIR=$THMSOC/idl/thmsoc/ucla_ff

IDL_DIR=/disks/apollo/export/idl_${idl_level}

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_UCLA_FF_DIR

IDL_STARTUP=cdf_startup.pro

IDL_DEVICE=Z

from [2]	UCB_FLAT_HOME=/disks/themisdata/thg/l1/mag

DATA_ROOT=/disks/themisdata

ASCIIMAGDIR=${DATA_ROOT}/thg/ascii_data/mag

LOGFILE=${LOGDIR}/UCLA_RMD2ALL_Log$(date '+%y%m%d')

from [3]	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

KSH_SCRIPTS=${THMSOC}/src/ksh.

ucla_flat2ascii.ksh runs the IDL routine uff2asc  to convert Flat Files to ASCII formatted Level 2 data products. Resulting ASCII files are saved to

${ASCIIMAGDIR}/[SITE]/YYYY

with filenames

thg_l2_mag_[SITE]_YYYYMMDD_v01.txt.

The script

${KSH_SCRIPTS}/fileChkSum.ksh

is run to update the checksum file.

uclaflat2ascii.ksh also calls the php script

gmag_ascii.php

to update the MySQL database with process results information.

If reprocessing of specific stations and dates is required, use the following script:

/disks/socware/thmsoc_dp_current/src/ksh/ucla_rmd2all_regen.ksh

### Products and Storage

The Flat File naming convention takes the following form:

BYYDDD_[SITE].ffd

where SITE = BMLS, CCNV, CHBG, DRBY, EKAT, FYTS, GBAY, HOTS, INUV, KAPU, KIAN, KUUJ, LARG, LETH, LOYS, MCGR, PGEO, PINE, PTRS, REDR, RMUS, ROTH, SNAP, SWNO, TPAS, UKIA, WHIT, YKNF.

These files are stored at:

/disks/themisdata/thg/l1/mag/[site]/YYYY

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY

The ASCII File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY

### Process Logs

Logfiles for the process are at

/disks/themisdata/process_logs/ucla_rmd2all/ UCLA_RMD2ALL_LogYYMMDD*

### Database Information

Databases gmag_cdf_files and gmag_ascii_files on the MySQL server (host astraea2) contain tables for each site epo_[site]_cdffiles (epo_[site]_asciifiles) or gbo_[site]_cdffiles (gbo_[site]_asciifiles), containing information on each CDF and ASCII file created.

### Web Information

Status on the latest processed files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php

A full inventory of CDF files can be created can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_cdf_list.txt

## Ground Magnetometer (GMAG) Data – Convert CARISMA ASCII to Level 2 Data Product

### Description

The CARISMA ASCII data is converted into CDF format. The CDF files are stored on the DP server and are available for download via http.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/call_candat_ascii2all.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variables

WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror.

call_candat_ascii2all.ksh calls the script

/disks/socware/thmsoc_dp_current/src/ksh/candat_ascii2all.ksh

for each site and date listed in

$GMAGMIRROR/CAN_ASCfiles*.

The script candat_ascii2all.ksh loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/ucla_rmd2all.config

[4] /disks/socware/thmsoc_dp_current/src/config/candat_ascii2all.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

KSH_SCRIPTS=${THMSOC}/src/ksh

WORKMAGSTACKS=${WORKDIR}/magStacks2Do

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

IDL_DIR=/disks/apollo/export/idl_${idl_level}

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	DATA_ROOT=/disks/themisdata

L2MAGDIR=${DATA_ROOT}/thg/l2/mag

ASCIIMAGDIR=${DATA_ROOT}/thg/ascii_data/mag

from [4]	UALOGDIR=/disks/themisdata/process_logs/gbo/carisma_gmag

LOGFILE=${UALOGDIR}/carisma_cdf_log_$(date '+%y%m%d')

UCB_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ualberta_ascii

CDFMASTERS=$THMSOC/src/mastercdfs/thg/.

IDL_UALBERTA_ASCII_DIR=$THMSOC/idl/thmsoc/ualberta_ascii

IDL_PATH=$IDL_PATH':'+$IDL_UALBERTA_ASCII_DIR

candat_ascii2all.ksh runs the IDL procedure make_canadian_gbo_cdf2 to produce a CDF and a txt file. The CDFs are copied to the directory

${L2MAGDIR}/[SITE]/YYYY,

the txt files are copied to the directory

${ASCIIMAGDIR}/[SITE]/YYYY.

The script

${KSH_SCRIPTS}/fileChkSum.ksh

is run to update the checksum files.

The date of the created file is copied to a file

${WORKMAGSTACKS}/stack_YYYYMMDD_*

for downstream stack plot production.

Finally, the php scripts gmag_cdf.php and gmag_ascii.php are called to update the astraea2 MySQL database with the process results information.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

where site = atha, fsim, fsmi, gill, pina, rank, snkq.

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY

The unzipped ASCII txt files with file names

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_logs/gbo/carisma_gmag/carisma_cdf_log_YYMMDD

/disks/themisdata/process_logs/gbo/carisma_gmag/carisma_idlout_YYMMDD_*

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site gbo_[site]_cdffiles (gbo_[site]_asciifiles), containing information on each CDF (ASCII file) created.

### Web Information

Status on the latest processed files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php

A full inventory of CDF files can be created can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_cdf_list.txt

## Ground Magnetometer (GMAG) Data – Convert GIMA NetCDF to Level 2 Data Product

### Description

The GIMA NetCDF data is converted into CDF format. The CDF files are stored on the DP server and are available for download via http.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/call_gima_netcdf2all.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variables

WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror.

This script checks the directory /disks/themisdata/workdir/gmag_mirror for files like GIMA_NC2ALL*, which contain information on the station and date of the NetCDF data to process into CDF (Level 2) products. For each station and date it calls the script

/disks/socware/thmsoc_dp_current/src/ksh/gima_netcdf2all.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/gima_netcdf2all.config

defining the environment variables

from [1]	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

KSH_SCRIPTS=${THMSOC}/src/ksh

WORKDIR=${THEMISDATA}/workdir

WORKMAGSTACKS=${WORKDIR}/magStacks2Do

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

IDL_DIR=/disks/apollo/export/idl_${idl_level}

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	GIMALOGDIR=$LOGDIR/gbo/gima_gmag

LOGFILE=${GIMALOGDIR}/gima_netcdf2all$(date '+%y%m%d')

DATA_ROOT=/disks/themisdata

L2MAGDIR=${DATA_ROOT}/thg/l2/mag

UCB_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ualaska_netcdf

ASCIIMAGDIR=${DATA_ROOT}/thg/ascii_data/mag.

gima_netcdf2all.ksh  makes use of a mapping file

/disks/socware/thmsoc_dp_current/src/netcdf2cdf/netcdf_to_cdf_mapping.dat

and master CDFs in

/disks/socware/thmsoc_dp_current/src/mastercdfs/thg/,

and calls an IDL routine netcdf2cdf_gmag which converts the NetCDF data into CDF format (and produces a txt file version). The resulting CDFs are copied to

${L2MAGDIR}/[SITE]/YYYY,

the txt files are copied to

${ASCIIMAGDIR}/[SITE]/YYYY

The script

${KSH_SCRIPTS}/fileChkSum.ksh

is called to update checksum files.

The date of the new file is written to

${WORKMAGSTACKS}/stack_YYYYMMDD

for downstream stack plot production.

The php scripts gmag_cdf.php and gmag_ascii.php are called to update the MySQL database on astraea2 with process results information.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

where site = fykn, gako, arct, bett, cigo, eagl, hlms, homr, kako, pokr, trap.

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY.

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/gbo/gima_gmag/gima_netcdf2allYYMMDD

/disks/themisdata/process_logs/gbo/gima_gmag/idl_netcdf2cdf_log&

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site gbo_[site]_cdffiles (gbo_[site]_asciifiles), containing information on each CDF (ASCII file) created.

### Web Information

Status on the latest processed files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php

A full inventory of CDF files can be created can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_cdf_list.txt

## Ground Magnetometer (GMAG) Data – Convert MACCS ASCII data to CDF

### Description

The MACCS ASCII data is converted into CDF format. The CDF files are stored on the DP server and are available for download via http.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/call_maccs_ascii2all.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variables

WORKDIR=${THEMISDATA}/workdir

GMAGMIRROR=${WORKDIR}/gmag_mirror

CONFIGDIR=${THMSOC}/src/config.

This script checks the directory /disks/themisdata/workdir/gmag_mirror for files like *.sec, which need to be processed into CDF (Level 2) products. The site names are obtained from

${CONFIGDIR}/maccs_site_list.txt

For each station and date it calls the script

/disks/socware/thmsoc_dp_current/src/ksh/maccs_ascii2all.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/maccs_ascii2all.config

defining the environment variables

from [1]	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

KSH_SCRIPTS=${THMSOC}/src/ksh

WORKDIR=${THEMISDATA}/workdir

WORKMAGSTACKS=${WORKDIR}/magStacks2Do

CONFIGDIR=${THMSOC}/src/config

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

IDL_DIR=/disks/apollo/export/idl_${idl_level}

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	MACCSLOGDIR=${LOGDIR}/gbo/maccs_gmag

LOGFILE=${MACCSLOGDIR}/maccs_cdf_log_$(date '+%y%m%d')

IDLOUT=${MACCSLOGDIR}/maccs_idlout_$(date '+%y%m%d')

L2MAGDIR=${THEMISDATA}/thg/l2/mag

UCB_MIRROR_HOME=${THEMISDATA}/thg/mirrors/mag/maccs_ascii

ASCIIMAGDIR=${THEMISDATA}/thg/ascii_data/mag

CDFMASTERS=$THMSOC/src/mastercdfs/thg/.

maccs_ascii2all reads the file

${CONFIGDIR}/maccs_site_list.txt

to translate between the three letter MACCS codes for sites (e.g. NAN) and the four-letter THEMIS codes (e.g. NAIN).

Using  master CDFs in

/disks/socware/thmsoc_dp_current/src/mastercdfs/thg/,

the script calls an IDL routine thm_maccs_gmag_l2gen which converts the ASCII data into CDF format (and produces a txt file version). The resulting CDFs are copied to

${L2MAGDIR}/[SITE]/YYYY,

the txt files are copied to

${ASCIIMAGDIR}/[SITE]/YYYY

The script

${KSH_SCRIPTS}/fileChkSum.ksh

is called to update checksum files.

The date of the new file is written to

${WORKMAGSTACKS}/stack_YYYYMMDD

for downstream stack plot production.

The php scripts gmag_cdf.php and gmag_ascii.php are called to update the MySQL database on astraea2 with process results information.

Additional scripts:

A cronjob on astraea2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/maccs_ascii2all_cleanup.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/maccs_ascii2all.config,

defining the environment variables

from [2] MACCSLOGDIR=${LOGDIR}/gbo/maccs_gmag

L2MAGDIR=${THEMISDATA}/thg/l2/mag.

This script deletes log files and scratch directories older than 32 days, namely the files in

$MACCSLOGDIR

and

$L2MAGDIR/garage.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY.

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/gbo/maccs_gmag/maccs_cdf_log_YYYYMMDD

/disks/themisdata/process_logs/gbo/maccs_gmag/macs_idlout_YYYYMMDD

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site, containing information on each CDF (ASCII file) created.

### Web Information

Status on the latest processed files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php

A full inventory of CDF files created can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_cdf_list.txt

## Ground Magnetometer (GMAG) Data – Convert Greenland/Denmark/Norway ASCII data to CDF

### Description

The Greenland/Denmark/Norway magnetometer data obtained from TGO in IAGA 2002 format is converted to CDF. The data is rotated from geographic coordinates to local geomagnetic coordinates using declination angles stored in the mastercdfs.

### Main Scripts/Programs

A cronjob on astraea2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/green_ascii2all_new.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/wget_green_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

unset IDL_PATH

IDL_DIR=/disks/apollo/export/idl_${idl_level};

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR ;

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	GMAGWORKDIR="${WORKDIR}/greenMag2Do"

TEMPDIR="${WORKDIR}/temp_dir/gmag_temp"

GREENMASTERDIR="${IDL_THMSOC_DIR}/greenland_gmag/mastercdfs_new"

L2MAGDIR=${THEMISDATA}/thg/greenland_gmag/l2

ASCIIMAGDIR=${THEMISDATA}/thg/ascii_data/greenland_gmag.

The script looks at all files in

$GMAGWORKDIR ( = /disks/themisdata/workdir/greenMag2Do)

of the format *.min and runs the IDL procedure

thm_greenmag_l2gen_new.pro,

passing the ascii file name, master cdf directory, and output file name.

The procedure thm_greenmag_l2gen_new.pro creates the CDF file with the help of the master cdfs found at

/disks/socware/thmsoc_dp_current/idl/thmsoc/greenland_gmag/mastercdfs_new/.

The routine also generates an ascii file.

The php scripts gmag_cdf.php and gmag_ascii.php are called to update the  MySQL database on astraea2 with process results information.

NB: an earlier version of thm_greenmag_l2gen_new.pro read the ascii files with the help of an IDL template.  Some of the sites recently made available have a different number of comment lines in their header making use of a template difficult.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY.

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/webdownloads/green_ascii2all_new_YYYYMMDD*

/disks/themisdata/process_logs/webdownloads/green_ascii2all_new_idl_YYYYMMDD*

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site, containing information on each CDF (ASCII file) created.

### Web Information

The latest Greenland data available can be checked in the tables: http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php.

## Ground Magnetometer (GMAG) Data – Convert INTERMAGNET ASCII data to CDF

### Description

The INTERMAGNET  magnetometer data obtained in IAGA 2002 format is converted to CDF.

Sites are currently: ABK, FCC, YKC.

Note: The data for the current sites we retrieve through INTERMAGNET is provided in geographic XYZ coordinates. The IDL processing routine has been updated as of April 2012 to rotate the data into local geomagnetic coordinates HDZ before saving to CDF. The declination angle for the rotation is stored in the master cdf, and was calculated using IGRF11 with a date of  2007-17-02 (see http://www.ngdc.noaa.gov/geomag-web/#igrfwmm to calculate declination angles). The transformation between XYZ and HDZ is thus only approximately correct.

### Main Scripts/Programs

A cronjob on astraea2 launches the script 	/disks/socware/thmsoc_dp_current/src/ksh/intermagnet_ascii2all.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/wget_intermagnet_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

unset IDL_PATH

IDL_DIR=/disks/apollo/export/idl_${idl_level};

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR ;

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	GMAGWORKDIR="${WORKDIR}/intermagnet2Do"

TEMPDIR="${WORKDIR}/temp_dir/intermagnet_temp"

CDFMASTERS=$THMSOC/src/mastercdfs/thg/

L2MAGDIR=${THEMISDATA}/thg/l2/mag							ASCIIMAGDIR=${THEMISDATA}/thg/ascii_data/mag.

intermagnet_ascii2all loops through all files in the directory

/disks/themisdata/workdir/intermagnet2do,

generates and runs an idl batch file calling the idl routine

/disks/socware/thmsoc_dp_current/idl/thmsoc/intermagnet_gmag/thm_intermagnetmag_l2gen.pro

to generate a CDF file and an ascii file from the data.

The mastercdfs located in

/disks/socware/thmsoc_dp_current/src/mastercdfs/thg/

are used in creating the CDFs.

The script

/disks/socware/thmsoc_dp_current/src/ksh/fileChkSum.ksh

is called to update the checksum listing for the created files in the files

/disks/themisdata/thg/l2/mag/[site]/YYYY/CHECKSUMS

and

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY/MM/CHECKSUMS.

The php scripts gmag_cdf.php and gmag_ascii.php are called to update the MySQL database on astraea2 with process results information.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY.

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY/MM.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/webdownloads/ intermagnet_ascii2all_YYYYMMDD*

/disks/themisdata/process_logs/webdownloads/intermagnet _ascii2all_idl_YYYYMMDD*

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site, containing information on each CDF (ASCII file) created.

### Web Information

The latest INTERMAGNET data available can be checked in the tables http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php.

## Ground Magnetometer (GMAG) Data – Convert US Geological Survey ASCII data to CDF

### Description

The USGS magnetometer data obtained in IAGA 2002 format is converted to CDF.

Sites are currently: BRW.

See  4.10 (USGS download script) for further information on the format of the downloaded data. Note that the back data to 2007 was provided in a different format and thus cannot be processed using the script described here. Back data processed using /disks/socware/thmsoc_dp_current/src/ksh/usgs_raw_ascii2all.ksh.

### Main Scripts/Programs

A cronjob on astraea2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/usgs_ascii2all.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/wget_usgs_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

unset IDL_PATH

IDL_DIR=/disks/apollo/export/idl_${idl_level};

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR ;

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	GMAGWORKDIR="${WORKDIR}/usgs2do"

TEMPDIR="${WORKDIR}/temp_dir/usgs_temp"

CDFMASTERS=$THMSOC/src/mastercdfs/thg/

L2MAGDIR=${THEMISDATA}/thg/l2/mag							ASCIIMAGDIR=${THEMISDATA}/thg/ascii_data/mag.

usgs_ascii2all loops through all files in the directory

/disks/themisdata/workdir/usgs2do,

generates and runs an idl batch file calling the idl routine

/disks/socware/thmsoc_dp_current/idl/thmsoc/usgs_gmag/thm_usgsmag_l2gen.pro

to generate a CDF file and an ascii file from the data.

The mastercdfs located in

/disks/socware/thmsoc_dp_current/src/mastercdfs/thg/

are used in creating the CDFs.

The php scripts gmag_cdf.php and gmag_ascii.php are called to update the MySQL database on astraea2 with process results information.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY.

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/webdownloads/ usgs_ascii2all_YYYYMMDD*

/disks/themisdata/process_logs/webdownloads/usgs _ascii2all_idl_YYYYMMDD*

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site, containing information on each CDF (ASCII file) created.

### Web Information

The latest USGS CDF and ASCII files available can be checked in the tables: http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php.

## Ground Magnetometer (GMAG) Data – Convert Antarctic CDF data to ASCII

### Description

The Antarctic magnetometer data (sites PG1 and PG2) is converted to ASCII format.

As the Antarctic data is provided in CDF format, no processing to CDF is required. We do however write an ASCII file of the data for consistency, as for all other gmag sites available through THEMIS the data is provided in both CDF and ASCII. For more information about the Antarctic data see Section 4.11.

### Main Scripts/Programs

A cronjob on astraea2 launches the script	/disks/socware/thmsoc_dp_current/src/ksh/antarctic_cdf2ascii.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/wget_antarctic_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

unset IDL_PATH

IDL_DIR=/disks/apollo/export/idl_${idl_level};

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR ;

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	GMAGWORKDIR="${WORKDIR}/antarctic2do"

TEMPDIR="${WORKDIR}/temp_dir/antarctic_temp"					  	L2MAGDIR=${THEMISDATA}/thg/l2/mag

ASCIIMAGDIR=${THEMISDATA}/thg/ascii_data/mag.

antarctic_cdf2ascii.ksh loops through all files in the directory

/disks/themisdata/workdir/antarctic2do,

generates and runs an idl batch file calling the idl routine

/disks/socware/thmsoc_dp_current/idl/thmsoc/thm_antarctic_asciigen.pro

to generate an ascii file from the data.

The php script gmag_ascii.php is called to update the MySQL database on astraea2 with process result information.

### Products and Storage

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/webdownloads/antarctic_cdf2ascii_YYYYMMDD*

/disks/themisdata/process_logs/webdownloads/antarctic _cdf2ascii_idl_YYYYMMDD*

### Database Information

Database gmag_ascii_files on the MySQL server on astraea2 contains tables for each site, containing information on each ASCII file created.

### Web Information

The latest Antarctic data available can be checked in the tables http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php.

## Ground Magnetometer (GMAG) Data – Convert Leirvogur ASCII data to CDF

### Description

The Leirvogur magnetometer data obtained in ASCII format is converted to CDF.

The 10 second resolution preliminary data provided by LRV contains components

H: total horizontal field magnitude in nT

D: angle between geographic north and H in 1/10000 radians

Z: vertical field magnitude in nT.

For consistency with other GMAG data, the LRV data is rotated into local magnetic coordinates

H: field magnitude in local magnetic north direction in nT

D: field magnitude in local magnetic east direction in nT

Z: vertical field magnitude in nT.

The declination angle used for the rotation is the mean value between 2007 and 2010, calculated from the annual means for those years (provided by Leirvogur Observatory in the 2010 yearbook). This declination is stored in the mastercdf.

Note that 1 minute resolution monthly definitive data for LRV is downloaded but not converted to CDF.

### Main Scripts/Programs

A cronjob on astraea2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/lrv_ascii2all.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/wget_lrv_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

unset IDL_PATH

IDL_DIR=/disks/apollo/export/idl_${idl_level};

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR ;

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	GMAGWORKDIR="${WORKDIR}/lrv2do"

TEMPDIR="${WORKDIR}/temp_dir/lrv_temp"

CDFMASTERS=$THMSOC/src/mastercdfs/thg/

L2MAGDIR=${THEMISDATA}/thg/l2/mag							ASCIIMAGDIR=${THEMISDATA}/thg/ascii_data/mag.

lrv_ascii2all loops through all files *sec.gz in the directory

/disks/themisdata/workdir/lrv2do,

generates and runs an idl batch file calling the idl routine

/disks/socware/thmsoc_dp_current/idl/thmsoc/lrv_gmag/thm_read_lrv10secfile.pro

to generate a CDF file and an ascii file from the data.

The mastercdfs located in

/disks/socware/thmsoc_dp_current/src/mastercdfs/thg/

are used in creating the CDFs.

The php scripts gmag_cdf.php and gmag_ascii.php are called to update the MySQL database on astraea2 with process results information.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY.

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/webdownloads/lrv_ascii2all_YYYYMMDD*

/disks/themisdata/process_logs/webdownloads/lrv _ascii2all_idl_YYYYMMDD*

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site, containing information on each CDF (ASCII file) created.

### Web Information

The latest LRV CDF and ASCII files available can be checked in the tables: http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php.

## Ground Magnetometer (GMAG) Data – Convert AARI ASCII data to CDF

### Description

Data from AARI magnetometers (AMD, DIK, PBK, TIK) obtained in IAGA2002 format is converted to CDF.

The 1 minute resolution variation data provided by AARI contains components

H: variation in field magnitude in local magnetic north direction in nT

E: variation in field magnitude in local magnetic east direction in nT

Z: variation in vertical field magnitude in nT.

Definitive baseline values are not known so the data remains as variation only.

### Main Scripts/Programs

A cronjob on astraea2 launches the script

/disks/socware/thmsoc_dp_current/src/ksh/aari_ascii2all.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/aari_gmag.config,

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

WORKDIR=${THEMISDATA}/workdir

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

unset IDL_PATH

IDL_DIR=/disks/apollo/export/idl_${idl_level};

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR ;

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR ;

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	GMAGWORKDIR="${WORKDIR}/aari2do"

TEMPDIR="${WORKDIR}/temp_dir/aari_temp"

CDFMASTERS=$THMSOC/src/mastercdfs/thg/

L2MAGDIR=${THEMISDATA}/thg/l2/mag							ASCIIMAGDIR=${THEMISDATA}/thg/ascii_data/mag.

aari_ascii2all loops through all files in the directory

/disks/themisdata/workdir/aari2do,

and generates and runs an idl batch file calling the idl routine

/disks/socware/thmsoc_dp_current/idl/thmsoc/thm_aarimag_l2gen.pro

to generate a CDF file and an ascii file from the data.

The mastercdfs located in

/disks/socware/thmsoc_dp_current/src/mastercdfs/thg/

are used in creating the CDFs.

The php scripts gmag_cdf.php and gmag_ascii.php are called to update the MySQL database on astraea2 with process results information.

### Products and Storage

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY.

The ASCII file naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY.

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_log/webdownloads/aari_gmag/aari_ascii2all_YYYYMMDD*

/disks/themisdata/process_logs/webdownloads/aari_gmag/aari _ascii2all_idl_YYYYMMDD*

### Database Information

Database gmag_cdf_files (gmag_ascii_files) on the MySQL server on astraea2 contains tables for each site, containing information on each CDF (ASCII file) created.

### Web Information

The latest AARI CDF and ASCII files available can be checked in the tables: http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php.

## Ground Magnetometer (GMAG) Data – Make Stack Plot

### Description

The L2 CDF data is used to create magnetometer stack plots – a single plot window containing the H, D, or Z components from a subset of sites.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/call_make_stack.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variables

WORKDIR=${THEMISDATA}/workdir

WORKMAGSTACKS=${WORKDIR}/magStacks2Do.

This script checks the directory /disks/themisdata/workdir/magStacks2Do for files like stack*, which contain information on dates for which new CDF (Level 2) products have been produced. It then calls the script

/disks/socware/thmsoc_dp_current/src/ksh/make_mag_stack_plots.ksh

for each date that needs to be processed.

The script  make_mag_stack_plots.ksh loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

[3] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config

defining the environment variables

from [1]	LOGDIR=${THEMISDATA}/process_logs

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

IDL_DIR=/disks/apollo/export/idl_${idl_level}

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z

from [3]	STACKLOGDIR=${LOGDIR}/gbo/mag_stackplots

LOGFILE=${STACKLOGDIR}/STACKPLOTS_Log$(date '+%y%m%d')

DATA_ROOT=/disks/themisdata

STACKPLOTS=${DATA_ROOT}/thg/summary_plots/mag/stackplots.

make_mag_stack_plots.ksh calls the IDL routine thm_gmag_stackplot, which converts the CDF data into plots (png). The resulting png files are copied to

${STACKPLOTS}/YYYY,

and the php script gmag_stackplots.php is called to update  MySQL database on astraea2 with process results information.

Additional scripts:

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/stacks_cleanup.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variable

from [1] LOGDIR=${THEMISDATA}/process_logs.

stacks_cleanup.ksh deletes files of the form IDLOUT_STACK* in $LOGDIR that are older than 10 days.

/disks/socware/thmsoc_dp_current/src/ksh/call_make_stack.ksh – Use this for reprocessing.

### Products and Storage

The plot file naming convention takes the form:

thg_l2_mag_[type]_YYYYMMDD_vnn.png

where type = hlla,dlla,zlla,hhla,dhla,zhla

These files are stored at:

/disks/themisdata/thg/summary_plots/mag/stackplots/YYYY

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_logs/gbo/mag_stackplots/STACKPLOTS_LogYYMMDD

### Database Information

Database gmag_stackplots on the MySQL server on astraea2 contains the table stackplot_file_list, which lists the stackplot png files created.

### Web Information

Status on the latest processed files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_stackplots_table.php

A full inventory of stack plot files produced can be found at (not updated as of Dec 2008):

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_stack_list.txt

## AEIndex Generation

### Description

Create AEIndex CDFs from GMAG L2 CDFs.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/call_make_ae_index.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config.

This script calls the script

/disks/socware/thmsoc_dp_current/src/ksh/make_ae_index.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne,

defining the environment variables

from [1]	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

LOCAL=/mydisks/home/thmsoc

LOGDIR=${THEMISDATA}/process_logs

from [2]	THEMIS_DATA_DIR=/disks/themisdata/

IDL_BASE_DIR=$THMSOC/idl

IDL_GENERAL_SSL_DIR=${IDL_BASE_DIR}/ssl_general

IDL_THEMIS_DIR=${IDL_BASE_DIR}/themis

IDL_EXTERNAL_DIR=${IDL_BASE_DIR}/external

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc

IDL_DIR=/disks/apollo/export/idl_${idl_level}

IDL_PATH=\+${IDL_DIR}/lib

IDL_PATH=$IDL_PATH':'+$IDL_GENERAL_SSL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THEMIS_DIR

IDL_PATH=$IDL_PATH':'+$IDL_EXTERNAL_DIR

IDL_PATH=$IDL_PATH':'+$IDL_THMSOC_DIR

IDL_STARTUP=idl_startup.pro

IDL_DEVICE=Z.

make_ae_index.ksh makes use of the mastercdf at

${IDL_THMSOC_DIR}/l1gen/mastercdfs/thg_l1_idx_00000000_v01.cdf,

and calls the IDL function thm_l1gen_idx to produce the AEIndex CDF. Resulting CDFs are copied to

${THEMISDATA}/thg/l1/mag/idx/YYYY,

and the script

${KSH_SCRIPTS}/fileChkSum.ksh

is run to update check sum files. The php script gmag_cdf.php  is run to update the  MySQL database on astraea2 with process result information.

### Products and Storage

The AEIndex file naming convention takes the form:

thg_l1_idx_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l1/mag/idx/YYYY

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_logs/ae_index/make_ae_index_YYYYMMDD

### Database Information

Database gmag_cdf_files on the MySQL server on astraea2 contains table gbo_aeIndex_cdffiles listing information on each CDF file created.

### Web Information

None.

## Ground Magnetometer (GMAG) Data – Check for Missing CDFs

### Description

Generate a list of missing GMAG CDFs for use by processing scripts.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/gen_gmag_missing_cdf_list.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]

This script checks the list files

${FILELISTS}/gmag_cdf_list_[SITE].txt

${FILELISTS}/gmag_raw_*_[SITE].txt

(see sections 4.31 and 4.32 for how these list files are generated) and determines if a raw data file exists but no CDF has been made. Missing CDFs are written to the list

${FILELISTS}/gmag_missing_cdf_list_[SITE].txt

### Products and Storage

Entries for missing CDFs are placed in files with the naming convention:

gmag_missing_cdf_list_[site].txt

These files are stored at:

/disks/themisdata/workdir/filelists

### Process Logs

None.

### Database Information

None.

### Web Information

None.

## Ground Magnetometer (GMAG) Data – Generate Missing CDFs

### Description

When raw data files exist but no CDF has been made via the normal generation process, the following scripts will use the missing CDF list mentioned above, to generate the appropriate files.

### Main Scripts/Programs

A cronjob on auxo launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/ucla_rmd2all_missing.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/ucla_rmd2all.config

[2] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config,

defining the environment variables

from [1]	LOGDIR=/disks/themisdata/process_logs/ucla_rmd2all

LOGFILE=${LOGDIR}/UCLA_RMD2ALL_Log$(date '+%y%m%d')

TABLE_FILES_DIR=/home/thmsoc/software_dev/c_prog/UCLA_Cal

UCB_FLAT_HOME=/disks/themisdata/thg/l1/mag

EPO_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ucla_rmd

GBO_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ucalgary_rmd

RMD2FFPATH=/home/thmsoc/software_dev/c_prog/leel_rmd_noleap/code

FFMERGEPATH=/home/thmsoc/software_dev/c_prog/ffmerge/bundle

KSHSCRIPTS=/home/thmsoc/software_dev/ksh

from [2]	CONFIGDIR=${THMSOC}/src/config

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu".

ucla_rmd2all_missing.ksh loops through all sites in

$CONFIGDIR/lc_site_list_ucla_all.txt

and uses the file

$CONFIGDIR/lc_site_list_ucla_epo.txt

to classify sites as EPO or GBO. The script checks that calibration files exist for the sites at

${TABLE_FILES_DIR}/[SITE].txt

For each date in

$CONFIGDIR/gmag_missing_cdf_list_[SITE].txt

the script runs the C code RMD2FF (must be run on Sun OS)  to create flat files from the RMD files

(also makes use of the file

$EPO_MIRROR_HOME/site_list.txt

to translate between long and short forms of the EPO site names). The flat files are merged into a single flat file for each day using

$FFMERGEPATH/ffmergesungnucmp,

the date format is translated from YYMMDD to YYDOY using

$KSHSCRIPTS/date2doy,

and the resulting files BYYDOY_[SITE].ffd and BYYDOY_[SITE].ffh are copied to

$UCB_FLAT_HOME/[SITE]/YYYY/.

The script then calls

/home/thmsoc/software_dev/ksh/ucla_flat2cdf.ksh  Changed Sep 2011

/disks/socware/thmsoc_dp_current/ksh/ucla_flat2cdf.ksh

to generate CDFs from the flatfiles, and

/home/thmsoc/software_dev/ksh/ucla_flat2ascii.ksh Changed Sep 2011

/disks/socware/thmsoc_dp_current/ksh/ucla_flat2ascii.ksh

to generate ASCII files from the flatfiles (see 4.15 for discussion of these scripts).

A cronjob on astraea launches the following scripts (No longer):

/disks/socware/thmsoc_dp_current/src/ksh/call_gima_netcdf2all_missing.ksh

### Products and Storage

The Flat File naming convention takes the following form:

BYYDDD_[SITE].ffd

These files are stored at:

/disks/themisdata/thg/l1/mag/[site]/YYYY

The CDF File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.cdf

These files are stored at:

/disks/themisdata/thg/l2/mag/[site]/YYYY

The ASCII File naming convention takes the form:

thg_l2_mag_[site]_YYYYMMDD_vnn.txt

These files are stored at:

/disks/themisdata/thg/ascii_data/mag/[site]/YYYY

### Process Logs

Logfiles for the process are at

/disks/themisdata/process_logs/ucla_rmd2all/ UCLA_RMD2ALL_LogYYMMDD*

### Database Information

Databases gmag_cdf_files and gmag_ascii_files on the MySQL server on astraea2 contain tables for each site, containing information on each CDF and ASCII file created.

### Web Information

Status on the latest processed files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_ascii_table.php

and

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_processing/gmag_cdf_table.php

A full inventory of CDF files can be created can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_cdf_list.txt

## Ground Magnetometer (GMAG) Data – EPO JPEG Processing

### Description

The 10 EPO magnetometers (same type as GBO) produce jpeg plots of the XYZ/HDB components as well spectrographs at 30 minute and 24 hour cadence. The plots are generated at UCLA and sent to the Berkeley server, where they are made available as ‘live data’ on http://ds9.ssl.berkeley.edu/themis/classroom_geons_data.html.

Previously these plots were also archived, but as of 2010 the process was changed such that the archive XYZ/HDB component day and time series jpegs are produced instead using TDAS software. As of March 2010 a decision was made to no longer archive spectral plots (according to Igor Ruderman, Oct 2011).

Once on the archive the separate component plots are merged into single plot files, file information is written to a database, and plots are made available for viewing through the GEONS website.

Contact information:

UCLA		Kathryn Rowe	krowe_at_igpp.ucla.edu

Richard Hart 	rhart _at_igpp.ucla.edu

Berkeley		Laura Peticolas	laura_at_sunearth.ssl.berkeley.edu (THEMIS E/PO deputy lead)

Nancy Ali 	nancy.ali_at_ssl.berkeley.edu (THEMIS E/PO lead)

Igor Ruderman 	igor_at_ssl.berkeley.edu

Karen Meyer	karena_at_ssl.berkeley.edu

### Main Scripts/Programs

A cronjob on auxo launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/make_epo_plots_daily.ksh

/disks/socware/thmsoc_dp_current/src/ksh/epo_magfile_append.ksh

make_epo_plots_daily.ksh generates component jpeg plots and saves them to /disks/horae/raid1/themis_epo.

epo_magfile_append scans the EPO site subdirectories found at /disks/horae/raid1/themis_epo for recent (last 12 days) jpg files. If files are found it runs the program /usr/local/bin/convert to merge the separate jpeg files. The resulting files are catalogued in a MySQL database on Juneau.

In detail, make_epo_plots_daily.ksh calls configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current /src/config/setup_themis_idl64.bourne,

defining environment variables

From [1]	 THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

SCRATCH=${THEMISDATA}/scratch

From [2] IDL_BASE_DIR=$THMSOC/idl

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc.

The logfile is defined in make_epo_plots_daily.ksh as

EPO_LOGFILE=${LOGDIR}/epo/epo_plots_make_${processdate}.

make_epo_plots_daily.ksh calls

${IDL_THMSOC_DIR}/ucla_epo_gmag/epo_plots_daily_batchfile,

which calls

make_epo_plots_daily_wrapper,

an IDL routine that is a wrapper for

make_epo_plots.pro.

NB: the sites for which jpgs are generated is hardcoded in make_epo_plots:

sites = ['kian','mcgr','ptrs','ccnv','ukia','hots','pine','fyts','swno','rmus','bmls','loys','drby']

By default processing is attempted for the last five days.

epo_magfile_append.ksh  calls the configuration file

/disks/socware/thmsoc_dp_current/src/config/thmsoc_epo.config,

defining the environment variables

LOGDIR=/disks/themisdata/process_logs/epo/

LOGFILE=$LOGDIR/EPO_Log$(date '+%y%m%d')

EPO_HOME=/disks/horae/raid1/themis_epo

SCHOOL CCNV PINE PTRS UKIA FYTS RMUS SWNO LOYS DRBY HOTS BMLS MCGR KIAN

LOCKFILE=/var/tmp/epo_append_lock

FIND_MTIME="-12",

and calls

usr/local/bin/convert

to merge jpegs.

Additional scripts:

/disks/socware/thmsoc_dp_current/src/php/epo_cmdline_input.php – File information is stored in the database EPOMAG located on the MySQL database server on juneau.

Relating to the display of the jpg files on the web (unsure who has responsibility for maintaining this):

/disks/www/sprg/themis/GEONS/geons_data.php

/disks/www/sprg/themis/GEONS/pan_display.php

/disks/www/sprg/themis/GEONS/process_form_input.php

### Products and Storage

The JPEG file naming convention takes the form:

[SITE]_[TYPE]_MMDDYYYY_HHMMSS.jpg

where

TYPE = {DS1, DS2, DS3, DSB, DSD, DSH, TS1, TS2, TS3, TSB, TSD, TSH, DStamp, TStamp}

for the files produced by make_epo_plots_daily.ksh, and

TYPE = {DS123, DSBDH, TS123, TSBDH}

for the files produced by epo_magfile_append.ksh. Spectra are of the type

TYPE = {TSpectra, DSpectra}.

These files are stored at:

/disks/horae/raid1/themis_epo/[site]/YYYY/MM/DD

### Process Logs

Log files for these processes take the form:

/disks/themisdata/process_logs/epo/epo_plots_make_YYMMDD

/disks/themisdata/process_logs/epo/EPO_LogYYMMDD

### Database Information

Database EPOMAG on the MySQL server on Juneau contains tables for each site, containing information on each jpg created.

### Web Information

The archived jpg files can be viewed at:

http://sprg.ssl.berkeley.edu/themis/GEONS

NB: the files in

/disks/horae/raid1/themis_epo/[site]/YYYY/MM/DD

are mapped to the website:

http://sprg.ssl.berkeley.edu/themis/GEONS/SCHOOLS

and the search form at

http://sprg.ssl.berkeley.edu/themis/GEONS

relies on the information in the EPOMAG database. Files relating to the webdisplay of data can be found at:

/disks/www/sprg/themis/GEONS

(both geons_data.php and pan_display.php need to be modified to add new years to the drop down list).

## Ground Magnetometer (GMAG) Data – EPO JPEG Monitor

### Description

Checks for JPEGs produced by the scripts described in 4.29 above. Sends alerts if missing.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/epo_jpg_check.ksh,

which calls the configuration file

/disks/socware/thmsoc_dp_current/src/config/thmsoc_epo.config,

defining the environment variables

EPO_HOME=/disks/horae/raid1/themis_epo

SCHOOL CCNV PINE PTRS UKIA FYTS RMUS SWNO LOYS DRBY HOTS BMLS MCGR KIAN

CHECK_MTIME="-2"

CONTACT_LIST="pcruce@igpp.ucla.edu jimm@ssl.berkeley.edu floresaa@igpp.ucla.edu lphilpott@igpp.ucla.edu" .

### Products and Storage

None.

### Process Logs

None. Email warnings are sent to the contact list if files are missing.

### Database Information

None.

### Web Information

None.

## GMAG Raw Data File Inventory

### Description

Generate an inventory of the raw GMAG data files collected.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/make_gmag_raw_files.ksh,

which loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config.

make_gmag_raw_files.ksh  is the parent script which calls numerous sub-scripts that list files collected for each station.

Additional scripts:

[1]	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_epormds.ksh,

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	UCLA_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ucla_rmd.

This script loops through the sites listed in

${CONFIGDIR}/ucla_rmd_site_list.txt

and checks the directory

${UCLA_MIRROR_HOME}/[SITE]

for RMD files. A list of the files is written to

${FILELISTS}/gmag_raw_epo_[SITE].txt

[2]	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_gbormds.ksh

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	UCAL_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ucalgary_rmd.

This script loops through the sites listed in

${CONFIGDIR}/ucalgary_rmd_site_list.txt

and checks the directory

${UCAL_MIRROR_HOME}

for RMD files. A list of the files is written to

${FILELISTS}/gmag_raw_gbo_[SITE].txt

[3]	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_ualbascii.ksh

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	UCLA UALB_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ualberta_ascii.

This script loops through the sites listed in

${CONFIGDIR}/ ualberta_ascii_site_list.txt

and checks the directory

${UALB_MIRROR_HOME}

for *.gz files. A list of the files is written to

${FILELISTS}/gmag_raw_alb_[SITE].txt

[4]	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_ualkncdf.ksh

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	UALA_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/ualaska_netcdf.

This script loops through the sites listed in

${CONFIGDIR}/ ualaska_netcdf_site_list.txt

and checks the directory

${UALA_MIRROR_HOME}

for files. A list of the files is written to

${FILELISTS}/gmag_raw_alk_[SITE].txt

[5]	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_greenland.ksh

(Note: this script only checks the site NAQ/NRSQ. As NAQ is now included with the other Greenland/Norway/Denmark sites it is unnecessary to continue running this script)

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	GRNL_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/greenland_ascii.

This script loops through the sites listed in

${CONFIGDIR}/greenland_ascii_site_list.txt

and checks the directory

${ GRNL_MIRROR_HOME }

for  files. A list of the files is written to

${FILELISTS}/gmag_raw_grnl_[SITE].txt

[6]	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_maccs.ksh

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	MACCS_MIRROR_HOME=/disks/themisdata/thg/mirrors/mag/maccs_ascii.

This script loops through the sites listed in

${CONFIGDIR}/ maccs_site_list.txt

and checks the directory

${ MACCS_MIRROR_HOME }

for *.sec files. A list of the files is written to

${FILELISTS}/gmag_raw_maccs_[SITE].txt

[7]	/disks/socware/thmsoc_dp_current/src/ksh/gen_gmag_raw_list.ksh

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

This script generates an ascii table of all raw files available by iterating through all dates listed in

${CONFIGDIR}/date_list.txt

and sites listed in

${CONFIGDIR}/lc_site_list.txt

(being all EPO, GBO, Alberta, Alaska, MACCS, and Greenland site NRSQ, and (as of Sep 2011) Athabasca sites) and looking to see whether the date is listed in

${FILELISTS}/gmag_raw_*_[SITE].txt.

The final table is saved to

${FILELISTS}/gmag_raw_list.txt

### Products and Storage

Lists are kept in the following files:

/disks/themisdata/workdir/filelists/gmag_raw_gbo_[site].txt

/disks/themisdata/workdir/filelists/gmag_raw_alb_[site].txt

/disks/themisdata/workdir/filelists/gmag_raw_alk_[site].txt

/disks/themisdata/workdir/filelists/gmag_raw_epo_[site].txt

/disks/themisdata/workdir/filelists/gmag_raw_maccs_[site].txt

/disks/themisdata/workdir/filelists/gmag_raw_grnl_nrsq.txt

These files are used to build an ASCII display of data availability. This file is:

/disks/themisdata/workdir/filelists/gmag_raw_list.txt

### Process Logs

None.

### Database Information

None.

### Web Information

The raw gmag data availability display can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_raw_list.txt.

## GMAG CDF Data File Inventory

### Description

Generate an inventory of the CDF and ASCII GMAG data files that have been produced.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/make_gmag_cdf_files.ksh,

loading the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config.

make_gmag_cdf_files.ksh is the parent script which calls numerous sub-scripts that list files collected for each station.

Additional scripts:

[1]	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_cdfs.ksh

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

LOCAL=/mydisks/home/thmsoc

from [2]	DATA_ROOT=/disks/themisdata

L2MAGDIR=${DATA_ROOT}/thg/l2/mag.

This script loops through all sites in

${CONFIGDIR}/lc_site_list.txt

(being EPO, GBO, Alberta, Alaska, MACCS, and Greenland site NRSQ, and (as of Sep 2011) Athabasca sites) creating a file

${FILELISTS}/gmag_cdf_list_[site].txt

that contains a list of the dates of  all CDFs in

${L2MAGDIR}/[site].

[2] 	/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_ascii.ksh

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

LOCAL=/mydisks/home/thmsoc

from [2]	DATA_ROOT=/disks/themisdata

ASCIIMAGDIR=${DATA_ROOT}/thg/ascii_data/mag

This script loops through all sites in

${CONFIGDIR}/lc_site_list.txt

(being EPO, GBO, Alberta, Alaska, MACCS, and Greenland site NRSQ, and (as of Sep 2011) Athabasca sites) creating a file

${FILELISTS}/gmag_ascii_list_[site].txt

that contains a list of the dates of  all txt files in

${ASCIIMAGDIR}/[site].

[3]	/disks/socware/thmsoc_dp_current/src/ksh/gen_gmag_cdf_list.ksh .

loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_mag.config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

LOCAL=/mydisks/home/thmsoc.

The script loops through all dates in

${CONFIGDIR}/date_list.txt

and sites in

${CONFIGDIR}/lc_site_list.txt

(being EPO, GBO, Alberta, Alaska, MACCS sites, and Greenland site NRSQ, and (as of Sept 2011) Athabasca sites) and creates a table in the file

${FILELISTS}/gmag_cdf_list.txt

that shows the dates that CDFs exist for all of the sites.

### Products and Storage

Lists are kept in the following files:

/disks/themisdata/workdir/filelists/gmag_cdf_list_[site].txt

/disks/themisdata/workdir/filelists/gmag_ascii_list_[site].txt

These files are used to build an ASCII display of data availability (currently only CDFs). This file is:

/disks/themisdata/workdir/filelists/gmag_cdf_list.txt

### Process Logs

None.

### Database Information

None.

### Web Information

The raw gmag data availability display can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_cdf_list.txt

## GMAG Stack Plot Data File Inventory

These scripts are no longer run automatically.

### Description

Generate an inventory of the GMAG stack plots that have been produced.

### Main Scripts/Programs

A cronjob on astraea launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/list_gmag_stackplots.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_gmag_stack_list.ksh

### Products and Storage

Lists are kept in the following files:

/disks/themisdata/workdir/filelists/gmag_stack_list_[type].txt

These files are used to build an ASCII display of stack plot availability. This file is:

/disks/themisdata/workdir/filelists/gmag_stack_list.txt

### Process Logs

None.

### Database Information

None.

### Web Information

The raw gmag data availability display can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/gmag_stack_list.txt

## GMAG EPO JPEG Plot File Inventory

### Description

Generates lists of what EPO JPEG files have been collected or generated and creates the web display for this information.

NB: Spectral plots were not archived past March 2010.

As of June 2012 this process has changed. Previously two scripts were run: list_gmag_epojpgs.ksh created a list of jpg filenames for each EPO site; gen_gmag_jpg_list.ksh read through the list of filenames and created ascii display files for each site (one display file to show availability of hour files and the other to show availability of day files). As the list and display files were regenerated for 2007 onwards each time the script was run it was a very time consuming process. These two scripts have been replaced by a single script that lookings in the database for availability and only generates a list for the current year (lists for past years have been created and stored in the appropriate place). This new script still takes quite some time to run.

Note that the new script file inventory only shows availability for ‘appended’ files DS123, DSBDH, TS123, TSDH. The older version also showed availability of component files. The last generated full lists from the previous process have been archived to /disks/themisdata/workdir/filelists/epo_jpg_full_list_062010. The old scripts are still in place in SVN and can be reinstated if necessary.

### Main Scripts/Programs

A cronjob on astraea2 launches the following script:

/disks/socware/thmsoc_dp_current/src//ksh/gen_gmag_jpg_list_new.ksh

The script gen_gmag_jpg_list_new.ksh loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/thmsoc_epo.config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	SCHOOL CCNV PINE PTRS UKIA FYTS RMUS SWNO LOYS DRBY HOTS BMLS MCGR KIAN.

The script creates an ascii file showing the jpg file availability for each school, looping through all dates in the current year up to the current date, all hours in

${CONFIGDIR}/hour_list.txt,

and datatypes in

${CONFIGDIR}/gmag_epojpg_tstype_short.txt

and

${CONFIGDIR}/gmag_epojpg_dstype_short.txt.

To check the existence of files the script calls the php script

/disks/socware/thmsoc_dp_current/src/php/epo_jpg_check_date.php.

The information is written to the files

${FILELISTS}/[site]_gmag_epojpg_TSList.txt

${FILELISTS}/[site]_gmag_epojpg_DSList.txt

### Products and Storage

The ascii display files are found at:

/disks/themisdata/workdir/filelists

Filenames take the form:

[SITE]_gmag_epojpg_[TYPE].txt

Where TYPE = TSList or DSList

NB: The files [SITE]_day_list and [SITE]_hr_list found in

/disks/danaid/home/www/html/data_inventory/ground_data/mag/epo_jpg_lists

(and mapped to the URL

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/epo_jpg_lists)

are symbolic links to the above files at /disks/themisdata/workdir/filelists.

### Process Logs

None.

### Database Information

None.

### Web Information

The raw gmag data availability displays can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/mag/epo_jpg_lists

## All Sky Imager (ASI) Low-Rate Data Collection – THEMIS GBO

### Description

Low rate ASI data is initially collected by the University of Calgary and stored on a data server. A wget (previously rsync) process at UCB pulls new and updated files from this server.

Note: As of November 2011 there are 21 active ASI sites. All data goes through the University of Calgary regardless of who ‘owns’ the site.

### Main Scripts/Programs

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/gbo_asi_rt_mirror_batch.ksh,

which loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config.

This script sets the time period arguments and calls the main rsync script

/disks/socware/thmsoc_dp_current/src/ksh/gbo_asi_rt_mirror.ksh,

loading the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/gbo_asi_rt_mirror.config,

defining the environment variables

from [1]	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	UCB_MIRROR_HOME=${THEMISDATA}/thg/mirrors/asi/low_res_rsync

LOGDIR=${THEMISDATA}/process_logs/gbo				 LOGFILE=$LOGDIR/GBO_ASI_RT_MIRROR_$(date '+%y%m%d')

WLOGFILE=$LOGDIR/WGET_GBO_ASI_RT_MIRROR_$(date '+%y%m%d')

WEBSITE_NAME="http://aurora.phys.ucalgary.ca/data/themis/imager"

DB_INPUT_FILES=${THEMISDATA}/workdir/db_input_files

This script runs wget to download any new or updated files. A record of the files is written to the database gbo_asi_rt_mirror using the script

/disks/socware/thmsoc_dp_current/src/php/update_asi_rt_tbl.php.

When rsync was used for the download process a record of the rsync statistics was also written to the database using

/disks/socware/thmsoc_dp_current/src/php/gbo_asi_rt_mirror_tbl_input_stats.php.

It is more difficult to get useful download statistics from wget, so this php script is no longer run.

Additional scripts:

A cronjob on gaia2 launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/rsync_gbo_cleanup.ksh,

loading the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/gbo_asi_rt_mirror.config,

defining the environment variable

from [2] LOGDIR=${THEMISDATA}/process_logs/gbo.

This script removes all files in the log directory beginning RSYNC that are older than 10 days (this includes gmag download files from other networks).

### Products and Storage

The low-rate data files are stored locally at:

/disks/themisdata/thg/mirrors/asi/low_res_rsync/YYYY/MM/DD/[site]/utHH/

(note that the directory name remains rsync although download now uses wget).

### Process Logs

/disks/themisdata/process_logs/gbo/GBO_ASI_RT_MIRROR_YYMMDD

/disks/themisdata/process_logs/gbo/WGET_GBO_ASI_RT_MIRROR_YYMMDD_stream[1-3]_[pid]

### Database Information

The database gbo_asi_rt_mirror is found on the DB MySQL server on astraea2. It contains tables for each GBO station listing the ASI files collected for each. Also, there’s a table listing rsync statistics.

### Web Information

Status on the latest collected files can be found at:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/asi_rt_calgary.php

A full inventory of collected files can be found at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/asi/asi_lowrate_files

## All Sky Imager (ASI) High-Rate Data Collection – THEMIS GBO

### Description

Disk drives containing the high resolution image data are recovered on a quarterly basis and are shipped to UC Berkeley for offloading of data onto the main THEMIS data server. This is the main process for retrieving the high resolution files. However, particular periods of interest, or data gaps can filled in with intermittent downlinks over the internet (script mentioned below).

### Main Scripts/Programs

The following file details all of the major steps in the collection process:

/home/thmsoc/software_dev/ksh/gbo_harddrives_readme.ksh

The process begins with mounting the USB drives on sunshine in room 236, SSL-Addition. After mounting the drive, the following script is run manually:

/home/thmsoc/software_dev/ksh/cp_asi_hardrive.ksh

This script copies data off the hard drive on to a scratch location. At the beginning and end of the copy process the script notifies users via email.

When cp_asi_hardrive.ksh is finished the following script is run manually:

/home/thmsoc/software_dev/ksh/chk_asi_gunzip.ksh

This script checks gzipped files for errors before moving them to their final location on the data server.

When chk_asi_gunzip.ksh is finished, run the following script:

/home/thmsoc/software_dev/ksh/update_asi_hires_tbl.ksh

This script will load file information into a database on the DP MySQL server.

The high resolution ASI files can also be downloaded over the internet using the following script:

/disks/socware/thmsoc_dp_current/src/ksh/gbo_asi_full_mirror.ksh

### Products and Storage

The high-rate data files are stored locally at:

/disks/themisdata/thg/mirrors/asi/hi_res_copy/YYYY/MM/DD/[site]/utHH/

### Process Logs

/home/thmsoc/software_dev/logs/ASI_HD_COPY_LogYYMMDD

### Database Information

The database gbo_asi_hires_mirror is found on the DB MySQL server on astraea2. It contains tables for each GBO station listing the ASI files collected for each.

### Web Information

TBD

## All Sky Imager (ASI) Low-Rate Data File Inventory

### Description

Generate an inventory of the low-rate ASI data files collected.

### Main Scripts/Programs

A cronjob on astraea2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/list_lowrate_asi_files.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_lowrate_asi_display.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_lowrate_asi_display_summary.ksh

/disks/socware/thmsoc_dp_current/src/ksh/chk_lowrate_asi_files.ksh (this does not appear to run automatically anymore)

These scripts will generate file lists, create displays, and check on file reception.

- list_lowrate_asi_files.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi_config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	LOWRES_RSYNC_DIR=${MIRROR_MAIN}/low_res_rsync.

This script loops through the current and previous months, and each site in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt.

For each datatype in

/disks/socware/thmsoc_dp_current/src/config/asi_dtype_list.txt

the script writes a list of files to

/disks/themisdata/workdir/filelists/asi_lowrate_list_${site}_${dtype}_${yearMonth}.txt.

NB: It is also possible to pass year, month and site arguments to this script.

- gen_lowrate_asi_display.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi_config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

The script loops through all the sites in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt,

all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and all datatypes in

/disks/socware/thmsoc_dp_current/src/config/asi_dtype_list.txt.

For all hours in

/disks/socware/thmsoc_dp_current/src/config/asi_hour_list.txt

it checks for the existence of files in the lists

/disks/themisdata/workdir/filelists/asi_lowrate_list_${site}_${dtype}_${yyyymm}.txt

and creates an ascii table showing file availability

/disks/themisdata/workdir/filelists/asi_lowrate_display_${site}.txt.

- gen_lowrate_asi_display_summary.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi_config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

The script loops through all the sites in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt,

all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and all datatypes in

/disks/socware/thmsoc_dp_current/src/config/asi_dtype_list.txt.

The number of files of each type for each date is written to the ascii table

/disks/themisdata/workdir/filelists/asi_lowrate_display_${site}_sum.txt.

### Products and Storage

Lists are kept in the following files:

/disks/themisdata/workdir/filelists/asi_lowrate_list_[site]_[type].txt

These files are used to build ASCII displays of data availability. These files are:

/disks/themisdata/workdir/filelists/asi_lowrate_display_[site].txt

/disks/themisdata/workdir/filelists/asi_lowrate_display_[site]_sum.txt/

### Process Logs

None.

### Database Information

None.

### Web Information

ASI low-rate data availability displays can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/asi/asi_lowrate_files

## All Sky Imager (ASI) High-Rate Data File Inventory

### Description

Generate an inventory of the high-rate ASI data files collected.

### Main Scripts/Programs

A cronjob on astraea2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/make_hi_asi_file_list.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_hirate_asi_display_daily.ksh

These scripts will generate file lists and create ascii displays.

- make_hi_asi_file_list.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi_config

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

from [2]	HIRES_COPY=${MIRROR_MAIN}/hi_res_copy.

For the current and previous month this script loops through all sites in the list

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt

and writes a list of hi res files for that site and month to the list

/disks/themisdata/workdir/filelists/asi_hirate_list_${site}_YYYYMM.txt.

- gen_hirate_asi_display_daily.ksh

This script loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

defining the environment variables

CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

For each date up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and each hour in

/disks/socware/thmsoc_dp_current/src/config/asi_hour_list.txt

the script loops through all sites in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt,

and creates a table showing how many hires files are available for that site and month

/disks/themisdata/workdir/filelists/asi_hirate_display.txt

### Products and Storage

Lists are kept in the following files:

/disks/themisdata/workdir/filelists/ asi_hirate_list_${site}_YYYYMM.txt

These files are used to build an ASCII display of data availability. The files is:

/disks/themisdata/workdir/filelists/ asi_hirate_display.txt

### Process Logs

None.

### Database Information

None.

### Web Information

ASI high-rate data availability displays can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/asi/asi_highrate_files/asi_hirate_display.txt

## All Sky Imager (ASI) Level 1 (L1) CDF Data File Inventory

### Description

Generate an inventory of the CDF data files that have been produced.

### Main Scripts/Programs

A cronjob on astraea2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/list_l1_ast_cdfs.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_ast_l1_cdf_list.ksh

/disks/socware/thmsoc_dp_current/src/ksh/list_l1_asf_cdfs.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_asf_inventory_display.ksh

/disks/socware/thmsoc_dp_current/src/ksh/list_l1_ask_cdfs.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_ask_l1_cdf_list_display.ksh

- list_l1_ast_cdfs.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	L1ASIDIR=${DATA_ROOT}/thg/l1/asi.

For each of the current and previous month, the script loops through each site in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt

and generates a list of the days that the l1 ast cdfs are available for that site for that month:

/disks/themisdata/workdir/filelists/ast_l1_cdf_list_${site}_YYYYMM.txt

(entries in the form YYYYMMDD).

- gen_ast_l1_cdf_list.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

This script loops through all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and all sites in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt,

generating an ascii table showing l1 ast file availability for each site and date:

/disks/themisdata/workdir/filelists/ast_l1_cdf_list.txt.

- list_l1_asf_cdfs.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	L1ASIDIR=${DATA_ROOT}/thg/l1/asi.

For each of the current and previous month, the script loops through each site in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt

and generates a list of the days that the l1 asf cdfs are available for that site for that month:

/disks/themisdata/workdir/filelists/asf_l1_cdf_list_${site}_YYYYMM.txt

(entries in the form YYYYMMDD).

- gen_asf_inventory_display.ksh

This script loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

defining the environment variables

CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

This script loops through all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

all hours in

/disks/socware/thmsoc_dp_current/src/config/asi_hour_list.txt,

and all sites in

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt,

checking in the file

asf_l1_cdf_list_${site}_YYYYMM.txt

to determine if a file is available for that date, and generating an ascii table showing the availability of asf l1 cdfs for each site and each date:

/disks/themisdata/workdir/filelists/asf_l1_cdf_list.txt

- list_l1_ask_cdfs.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi.config,

defining the environment variables

from [1] LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

This script writes a list of l1 ask files to

/disks/themisdata/workdir/fileslists/ask_l1_cdf_list.txt.

- gen_ask_l1_cdf_list_display.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi.config,

defining the environment variables

from [1] CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

The script loops through all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and checks the list

/disks/themisdata/workdir/fileslists/ask_l1_cdf_list.txt,

to determine whether files are available for each date, generating the ascii table

/disks/themisdata/workdir/filelists/ask_l1_cdf_list_display.txt.

### Products and Storage

Lists are kept in the following files:

/disks/themisdata/workdir/filelists/ast_l1_cdf_list_${site}_YYYYMM.txt

/disks/themisdata/workdir/filelists/asf_l1_cdf_list_${site}_YYYYMM.txt

/disks/themisdata/workdir/fileslists/ask_l1_cdf_list.txt

These files are used to build an ASCII display of data availability. These files are:

/disks/themisdata/workdir/filelists/ast_l1_cdf_list.txt

/disks/themisdata/workdir/filelists/asf_l1_cdf_list.txt

/disks/themisdata/workdir/filelists/ask_l1_cdf_list_display.txt

### Process Logs

None.

### Database Information

None.

### Web Information

ASI low-rate data availability displays can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/asi/

(mapped from /disks/danaid/home/www/html/data_inventory/ground_data/asi, where the cdf list files are symbolic links to the above mentioned files in /disks/themisdata/workdir/filelists/).

## All Sky Imager (ASI) Site Summaries

### Description

Generates lists of the low rate asi summary files (files like {SITE}.YYYY.MM.DD.HH.MM.gif).

### Main Scripts/Programs

A cronjob on astraea2 launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/list_asi_site_summaries.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_asi_site_summary_display.ksh

/disks/socware/thmsoc_dp_current/src/ksh/list_asi_allsite_summaries.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_asi_allsite_summary_display.ksh

/disks/socware/thmsoc_dp_current/src/ksh/gen_grand_asi_display.ksh

- list_asi_site_summaries.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	DATA_ROOT=/disks/themisdata

L0ASIDIR=${DATA_ROOT}/thg/l0/asi.

For each of the current and previous month, the script loops through each site in

/disks/socware/thmsoc_dp_current/src/config/uc_asi_site_list.txt

and generates a list of the asi summary files that are available for that site for that month:

/disks/themisdata/workdir/filelists/asi_summary_list_${site}_YYYYMM.txt.

- gen_asi_site_summary_display.ksh

This script loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

defining the environment variables

CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

This script loops through all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and all sites in

/disks/socware/thmsoc_dp_current/src/config/uc_asi_site_list.txt,

counting entries in the files

/disks/themisdata/workdir/filelists/asi_summary_list_${site}_YYYYMM.txt

generating an ascii table showing the number of asi summary files for each site and date:

/disks/themisdata/workdir/filelists/asi_site_summary_display.txt.

- list_asi_allsite_summaries.ksh

This script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/ground_asi.config,

defining the environment variables

from [1]	CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists

from [2]	DATA_ROOT=/disks/themisdata

L0ASIDIR=${DATA_ROOT}/thg/l0/asi.

For each of the current and previous month, the script loops through each of the following types:

average, keograms, summary, orbit, themis_foot, themis_south

and generates a list of the files of that type for the given month:

/disks/themisdata/workdir/filelists/asi_summary_list_TYPE_YYYYMM.txt

- gen_asi_allsite_summary_display.ksh

This script loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

defining the environment variables

CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

This script loops through all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and through each of the following types:

average, keograms, summary, orbit, themis_foot, themis_south,

checking the files

/disks/themisdata/workdir/filelists/asi_summary_list_TYPE_YYYYMM.txt

to determine the number of files of each type for each month, and creating the ascii display file

/disks/themisdata/workdir/filelists/asi_allsite_summary_display.txt

- gen_grand_asi_display.ksh

This script loads the configuration file

/disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

defining the environment variables

CONFIGDIR=${THMSOC}/src/config

LOCAL=/mydisks/home/thmsoc

WORKDIR=${THEMISDATA}/workdir

FILELISTS=${WORKDIR}/filelists.

This script loops through all dates up to the current date in

/disks/socware/thmsoc_dp_current/src/config/date_list.txt,

and all sites in the list

/disks/socware/thmsoc_dp_current/src/config/lc_asi_site_list.txt.

It loops through all datatypes in the list

/disks/socware/thmsoc_dp_current/src/config/asi_dtype_list.txt,

looking in the files

/disks/themisdata/workdir/filelists/asi_lowrate_list_SITE_TYPE_YYYYMM.txt

to determine the number of files of each type.

It also looks through the files of type

/disks/themisdata/workdir/filelists/asi_summary_list_SITE_YYYYMM.txt

to determine the number of summary files.

Finally, for each of the types:

average keograms summary

the script looks in the files

/disks/themisdata/workdir/filelists/asi_summary_list_TYPE_YYYYMM.txt

to determine the number of files for that type.

This information is displayed in the ascii file

/disks/themisdata/workdir/filelists/asi_grand_display.txt

### Products and Storage

Lists are kept in the following files:

/disks/themisdata/workdir/filelists/ asi_summary_list_${site}_YYYYMM.txt

/disks/themisdata/workdir/filelists/ asi_summary_list_TYPE_YYYYMM.txt

These files are used to build an ASCII display of data availability. These files are:

/disks/themisdata/workdir/filelists/ asi_site_summary_display.txt	/disks/themisdata/workdir/filelists/ asi_allsite_summary_display.txt	/disks/themisdata/workdir/filelists/ asi_grand_display.txt

### Process Logs

None.

### Database Information

None.

### Web Information

ASI low-rate data availability displays can be viewed at:

http://themis.ssl.berkeley.edu/data_inventory/ground_data/asi/

(mapped from /disks/danaid/home/www/html/data_inventory/ground_data/asi, where the list files are symbolic links to the above mentioned files in /disks/themisdata/workdir/filelists/).

## All Sky Imager (ASI) Products

### Description

Generate and reprocess ASI cdf products and gif products.

### Main Scripts/Programs

A cronjob on auxo launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/make_asi_products.ksh

/disks/socware/thmsoc_dp_current/src/ksh/reprocess_asi.ksh

- make_asi_products.ksh

This script calls the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

defining the environment variables

from [1]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

SCRATCH=${THEMISDATA}/scratch

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	IDL_BASE_DIR=$THMSOC/idl

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc.

This script calls the idl batchfile

/disks/socware/thmsoc_dp_current/idl/thmsoc/asi/batchfile,

compiling a number of IDL routines:

@compile_cdaweb

.run IDLmakecdf (compile the routines necessary for writing cdfs)

.run thm_asi_create_ask_cdf

.run thm_asi_create_ast_cdf

.run thm_asi_create_asf_cdf

.run thg_asi_imager_readfile

.run thg_asi_thumbs

.run istp_cdf_readfile

.run thg_asi_getimage

and running the script

.run thg_asi_daily_script (this is a main program that generates a variety of products)

NB: the routine thg_asi_setup.init run from within these routines sets up a number of variables including the output file directories.

thg_asi_daily_script.pro calls a number of IDL routines to generate ASI products, including:

themis_daily_overview (generate gif: summary.YYYY.MM.DD.gif)

themis_full_overview (generate gif: average.YYYY.MM.DD.gif)

themis_daily_keograms_new (generate gif: keograms.YYYY.MM.DD.gif)

thm_asi_create_ask_cdf (generate ask cdf)

automatic_script (incls calls to make_hour_plots to generate hourly overview plots [SITE].YYYY.MM.DD.HH.(MM).gif and thm_asi_create_ast_cdf  to generate ast cdfs)

(products are generated for three days prior to the current date).

- reprocess_asi.ksh

This script calls the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

and calls the scripts

check_ask_files.ksh

check_ast_files.ksh

using the function

/disks/socware/thmsoc_dp_current/src/ksh/funcs/pn_day

to calculate the start and end dates (4 and 3 days before the present) to pass to the scripts.

check_ask_files.ksh/check_ast_files.ksh use the script gen_idl_line.ksh to create an IDL batch file to run the IDL procedures check_ask_files.pro/check_ast_files.pro,  which check for ask/ast cdf files and attempt to generate any that are missing.

### Products and Storage

ASI cdfs:

/disks/themisdata/thg/l1/asi/[SITE]/YYYY/MM/thg_l1_ast_SITE_YYYYMMDD_v01.cdf

(/disks/themisdata/thg/l1/asi/[SITE]/YYYY/MM/thg_l1_asf_SITE_YYYYMMDD_v01.cdf)

/disks/themisdata/thg/l1/asi/ask/YYYY/thg_l1_ask_YYYYMMDD_v01.cdf

Image products

/disks/themisdata/thg/l0/asi/YYYY/MM/average.YYYY.MM.DD.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/keograms.YYYY.MM.DD.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/summary.YYYY.MM.DD.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/DD/[SITE]/[SITE].YYYY.MM.DD.HH.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/DD/[SITE]/[SITE].YYYY.MM.DD.HH.MM.gif

### Process Logs

ASI products logs:

/disks/themisdata/process_logs/asi/asi_processing_log_YYMMDD.txt

### Database Information

None.

### Web Information

None.

## All Sky Imager (ASI) Orbits

### Description

Generate orbit gif products.

### Main Scripts/Programs

A cronjob on auxo launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/make_asi_orbits.ksh

This script calls the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

[2] /disks/socware/thmsoc_dp_current/src/config/setup_themis.bourne

defining the environment variables

from [1] THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

SCRATCH=${THEMISDATA}/scratch

SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu jwl@ssl.berkeley.edu lphilpott@igpp.ucla.edu"

from [2]	IDL_BASE_DIR=$THMSOC/idl

IDL_THMSOC_DIR=${IDL_BASE_DIR}/thmsoc.

The script runs the IDL batch files

/disks/socware/thmsoc_dp_current/idl/thmsoc/asi/orbit_batchfile

/disks/socware/thmsoc_dp_current/idl/thmsoc/asi/lunar_orbit_batchfile

/disks/socware/thmsoc_dp_current/idl/thmsoc/asi/lunar_orbit_sse_batchfile

orbit_batchfile calls

.run map_themis_state_t96

.run map_themis_state_south_t96

.run compass

.run istp_cdf_readfile

.run t96_mgnp

.run bshock_2

.run mpause_2

.run thg_asi_state_daily_script

to compile the various scripts, and  calls the IDL procedure process_modified _orbit_dates.pro.

lunar_orbit_batchfile and lunar_orbit_sse_batchfile call process_modified_orbit_dates.pro with keywords /lunar and /sse_lunar respectively.

map_themis_state_t96.pro generates the gifs themis_foot_YYYY-MM-DD.gif

map_themis_state_south_t96.pro generates the gifs themis_south_YYYY-MM-DD.gif

process_modified_orbit _dates.pro generates orbit gifs:

orbit_moon_YYYY-MM-DD_HHHH.gif (where the first HH is the start hour and the second HH is the end hour).

orbit_moon_sse_YYYY-MM-DD_HHHH.gif (HHHH as above)

orbit_YYYY-MM-DD_HHHH.gif (HHHH as above)

### Products and Storage

/disks/themisdata/thg/l0/asi/YYYY/MM/themis_foot_YYYY-MM-DD.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/themis_south_YYYY-MM-DD.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/orbit_moon_YYYY-MM-DD_HHHH.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/orbit_moon_sse_YYYY-MM-DD_HHHH.gif

/disks/themisdata/thg/l0/asi/YYYY/MM/orbit_YYYY-MM-DD_HHHH.gif

### Process Logs

/disks/themisdata/process_logs/orbits/idl_orbits_YYMMDD

/disks/themisdata/process_logs/orbits/idl_lunar_orbits_YYMMDD

/disks/themisdata/process_logs/orbits/idl_lunar_orbits_sse_YYMMDD

### Database Information

None.

### Web Information

None.

## All Sky Imager (ASI) Mosaic Image Production

### Description

Create or update the ASI Mosaic plots using the latest data.

### Main Scripts/Programs

A cronjob on thailo launches the following script:

/disks/socware/thmsoc_dp_current/src/ksh/run_asi_mosaic.ksh

This script creates and runs an IDL batch file which creates or updates the mosaic files.

The script loads the configuration files

[1] /disks/socware/thmsoc_dp_current/src/config/asi_mosaic_setup.bourne

[2] /disks/socware/thmsoc_dp_current/src/config/soc_it_to_me.config

defining the environment variables

from [2]	THEMISDATA="/disks/themisdata"

LOGDIR=${THEMISDATA}/process_logs

MOSAICWORK=/home/thmsoc/asi_mosaic_cronjob.

The script runs the idl routine

run_create_themis_mosaics_hr.pro,

which itself runs

create_themis_mosaics_hr.pro

to generate the ASI mosaics that eventually end up at

/disks/themisdata/thg/l0/asi/YYYY/MM/DD/MOSA/MOSA.YYYY.MM.DD.HH.MM.SS.gif

### Products and Storage

The mosaic file naming convention takes the form:

MOSA.YYYY.MM.DD.HH.MM.SS.gif

These files are stored at:

/disks/themisdata/thg/l0/asi/YYYY/MM/DD/MOSA/

### Process Logs

Log files for this process take the form:

/disks/themisdata/process_logs/mosaics/make_mosaic_YYMMDD

### Database Information

None.

### Web Information

The mosaic plots can be viewed at:

http://themis.ssl.berkeley.edu/gbo/display.py

# Databases

Many of the scripts described in this document write file information and process statistics to database tables accessed via the MySQL database server on astraea2. Some of the information in these tables is used to generate the status information available on the website at http://themis.ssl.berkeley.edu/status.shtml.

Access to the MySQL database server on astraea2 requires username and password that can be found in any of the relevant php scripts.

Databases on astraea2 (not all are relevant):

information_schema

CD_Production

Probe_StateFile_Production

Process_Logs

epo_ucla_rmd_mirror

file_tracker_themis

gbo_asi_hires_mirror

gbo_asi_rt_mirror

gbo_ua_canmag_mirror

gbo_ualaska_mirror

gbo_uatha_rmd_mirror

gbo_uc_gmag_rmd_mirror

gmag_ascii_files

gmag_cdf_files

gmag_stackplots

mysql

overplot_process

performance_schema

probe_l0_process

probe_l2_processing

test

web_downloads

web_usage

Note that schools involved in the EPO program access ascii files through http://themis.ssl.berkeley.edu/EPO_Access/, which relies on information in the gmag_ascii_files database.

Information on the EPO JPG files is written to the MySQL database EPOMAG on Juneau. This database is used by the GEONS site http://sprg.ssl.berkeley.edu/themis/GEONS/ to provide EPO plots. The EPOMAG database on Juneau access information can be found in the relevant php scripts.

Note:

1.  The SSL sysadmins administer the MySQL database servers. Contact them if maintenance or creation of a new database is required.

2.  Following outages or crashes the MySQL database server may come online after cronjobs begin running. In this case information may not be correctly written to the databases.  It is necessary to check that the database tables are up to date following any problems.

## Cron-Job Warning Notification Database

The notification database is hosted by astraea2, under the name Process_Logs. The cron-job warning logs are fed to the Thmsoc_Log table via the thmsoc_dblog.php routine with the following arguments:

thmsoc_dblog.php process_name severity message

Severity 1 Example: thmsoc_dblog.php $(basename $0) 1 “This is a warning message”

The severity codes are as follows:

        - Urgent – for fatal errors and network problems

        - Warning – for non-fatal errors

        - Informative – for non-error information

The thmsoc_dbnotify.php routine fetches all unreported cron-job error log entries for a given severity from the Thmsoc_Log table, and sends email notifications to the requested list:

Severity 1 Example:  thmsoc_dbnotify.php 1 someone@ssl.berkeley.edu

Separate notification cron-jobs should be implemented for the various severity levels with the following recommended schedules:

Severity 1)  every 30 minutes

Severity 2)  every 4 hours

Severity 3)  every 12 hours

Severity 1 thmsoc_dbnotify cron-job example:

1,31 * * * * THMSOC=/disks/socware/thmsoc_dp_current ; export THMSOC ; 	SOC_EMAIL="jimm@ssl.berkeley.edu pcruce@igpp.ucla.edu 	jwl@ssl.berkeley.edu" ; export 	SOC_EMAIL ; ${THMSOC}/src/php/thmsoc_dbnotify.php 1 $SOC_EMAIL

# Website Activities

## Process Web Server Logs

### Description

The THEMIS Web server logs are archived and processed for information relating to data usage by external users.

### Main Scripts/Programs

A cronjob on danaid (the THEMIS web server) launches the following scripts:

/disks/socware/thmsoc_dp_current/src/ksh/grab_weblog.ksh

/disks/socware/thmsoc_dp_current/src/ksh/process_weblogs.ksh

The first script copies the logs from the temporary server location. The second script parses information from the logs and places it into a database on the DP MySQL server.

Additional Scripts:

/disks/socware/thmsoc_dp_current/src/ksh/process_weblog4sum.ksh – searches log for information related to summary/tohban plot usage.

/disks/socware/thmsoc_dp_current/src/ksh/process_weblog4data.ksh – searches log for information related to usage of the web interface for downloading CDF data.

/disks/socware/thmsoc_dp_current/src/ksh/process_weblog4swdl.ksh – searches the log for information related to the usage of THEMIS Data Analysis Software (TDAS) for downloading data.

/disks/socware/thmsoc_dp_current/src/php/update_weblog_cdf_access.php – archives usage information in database on DP MySQL server.

### Products and Storage

The THEMIS web server log files are renamed to:

thmweb_accesslog_StartStop

where StartStop=DayMonthDayMonthYear

example: thmweb_accesslog_24Feb02Mar08

Data derived from the log files is stored in separate files, broken up by usage:

mysql_thmweb_accesslog_DayMonthDayMonthYear_type

where type = sum, data, or swdl

These files are initially stored at:

/disks/themisdata/weblogs

### Process Logs

None.

### Database Information

The database web_usage is found on the DB MySQL server on astraea2. It contains tables for each usage type listing access statistics.

### Web Information

Currently, there are 2 high level views of usage. A mission level view:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/webstats_summary.php

And a view of related to UAlberta/CARISMA data usage:

http://themis.ssl.berkeley.edu/data_processing_check/ground_data_mirrors/webstats_carisma_summary.php

## Website Maintenance

### THEMIS – Critical Site Files

The THEMIS site root directory is located on the SSL server: /disks/danaid/home/www/html

Critical files for site operation are located in the following subdirectories:

/common/css/ themisStyles.css:  Cascading style sheet (CSS) for entire site layout, graphical and type formatting, and front/content page header configurations.

/common/js/:  Javascript source files for file pre-loading, menu formatting, summary plot script functions.

/includes/ navigation-scripts-css.lbi:  site main menu source code, to revise menu links.

/menu/ themis-menu.css: site main menu layout and text formatting (do not edit).

Note:	 The web related php scripts in the subdirectories data_processing_check, EPO_Access, and vc_check are symbolic links to the master versions of these scripts at

/disks/socware/thmsoc_dp_current/src/php/webserver_scripts/.

When updates to these scripts are necessary the scripts should be checked in to SVN and pushed into the production version.

### THEMIS – Beta Test Page

All updates and/or edits to THEMIS web images and content pages must first be saved into the Beta subdirectory in the site root folder, which contains a mock-up of all “live” content.  First, open the “live” source file in the appropriate root directory, then save a copy to the corresponding folder in the Beta subdirectory, overwriting the existing Beta copy if necessary.  After testing and formatting is complete, links to the Beta pages should be submitted to David King and the PI (or source of update request) for approval.  The approved Beta file(s) may then be transferred to the root directory, either overwriting the original or saving the original file with an appended date if needed for version tracking. Alternatively, the source code may also be copied from the Beta file and carefully pasted to the appropriate section in the root directory file.

### THEMIS – News Updates

Updates to news items must be performed on both the root directory files “index.shtml” and “news.shtml”

Any news text must be first added to the homepage index file inside the <div id=“divUpdateNews”> and <p class=”news”> tags, adding the date of entry and front page headline text up to 400 characters.**   The accompanying news image must be placed inside <div id="divLaunchVideo">, no wider than 128px and no taller than 200px for the caption to fit.

Any additional text and images/video beyond the 400 character front page limit must be added to the “news.shtml” content page inside the <P class=”pageTitle”> tag, below the header “<h1>THEMIS News</h1>.” Include a news item summary title and the phrase “(continued from home page):” followed by the press release date and additional news text.  All images or videos should be scaled to 300px wide, with figure caption and appropriate media source credit.  Include citation and shortcut PDF links to all published papers.

**Please note: before adding a new front page news entry to “index.shtml,” the previous entry’s front page headline must be appended to the corresponding entry in the “news.shtml” page for archiving.

### THEMIS – GBO Station Updates

The latest GBO station details should be uploaded to:

/ images/ASI/THEMIS_GMAG_Station_List_mmm_yyyy.xlsx

The corresponding link to this file must also be updated on the following pages:

instrument_gmags.shtml

asi_map.shtml

Additionally, any updates to station counts, affiliations, or classifications should be made here:

instrument_gmags.shtml

gmag_desc.shtml

### THEMIS – Publications

Recent publications (2011-2012) are stored on the SSL server:

/disks/danaid/home/www/html/pubs/20XX_refereed

for peer-reviewed articles and all others under “pubs/20XX_nonrefereed.”  Publications are entered in both HTML and Excel formats in each folder and must be listed in alphabetical order, with author last name and first initial, month and year of acceptance, journal name, and then the full citation, with a link to the abstract, or if unavailable, to the publisher’s “in press” article page.

Older publications (pre-2010) are stored on the IGPP server RESEARCH1, using the same format:

//research1/research1/space_emergency/obitwo/cache5/data3/public/THEMIS/SCI/Pubs/

Regardless of source location, each year of publications must be correctly linked via the file “publications.shtml,” in the Themis site root directory.

### THEMIS – Nuggets

THEMIS nuggets, or research summaries, are currently stored on the IGPP server RESEARCH1:

Summary page:

//research1/research1/space_emergency/obitwo/cache5/data3/public/THEMIS/SCI/Pubs/Nuggets/ /nuggets_20YY/nuggets_YY.html

The summary page should list nuggets in reverse chronological order by month of acceptance, most recent first.  Each summary should be in lay language and no more than 2-3 sentences, with a 100px square image, linking to the detailed nugget.

Nugget page:

//research1/research1/space_emergency/obitwo/cache5/data3/public/THEMIS/SCI/Pubs/Nuggets/ /nuggets_20YY/author/author_YY.html

Each nugget should follow the same format with Title, Author, Introduction, Results, Conclusion, Reference, and  Biographical Note.  Figures should be thumbnailed to 300px wide and link to the full size image (no larger than 1000px wide), and should be accompanied by a detailed caption.

Each year of nugget summaries must be correctly linked via the page “publications.shtml,” in the Themis site root directory.

Additional nugget images may be added to the slideshow on the THEMIS front page by editing “index.shtml” under the section <div id=“divnuggets”>, following the existing javascript slidelink script format.  Slideshow source images and an Adobe Photoshop PSD template can be found on the SSL site:

/disks/danaid/home/www/html/images/index.table/nuggets

### ARTEMIS – Critical Site Files

All ARTEMIS site files are located on the SSL server: /disks/danaid/home/www/artemis

Critical files for site operation are located in the following subdirectories:

/common/css/ artemis_styles.css:  Cascading style sheet (CSS) for entire site layout, graphical and type formatting, front/content page header configurations.

/common/js/:  Javascript source files for file pre-loading, menu formatting, summary plot script functions.

/includes/ navigation-scripts-css.lbi:  site main menu source code, to revise menu links.

/menu/ themis-menu.css: site main menu layout and text formatting (do not edit).

### ARTEMIS – Beta Test Page

All updates and/or edits to ARTEMIS web images and content pages must first be saved into the Beta subdirectory in the site root folder, which contains a mock-up of all “live” content.  First, open the “live” source file in the appropriate root directory, then save a copy to the corresponding folder in the Beta subdirectory, overwriting the existing Beta copy if necessary.  After testing and formatting is complete, links to the Beta pages should be submitted to David King and the PI (or source of update request) for approval.  The approved Beta file(s) may then be transferred to the root directory, either overwriting the original or saving the original file with an appended date if needed for version tracking. Alternatively, the source code may also be copied from the Beta file and carefully pasted to the appropriate section in the root directory file.

### ARTEMIS – News Updates

Updates to news items must be performed on both the root directory files “index.shtml” and “news.shtml”

Any news text must be first added to the homepage index file inside the <div id=“divUpdateNews”> and <p class=”news”> tags, adding the date of entry and front page headline text up to 400 characters.**   The accompanying news image must be placed inside <div id="divLaunchVideo">, no wider than 128px and no taller than 200px for the caption to fit.

Any additional text and images/video beyond the 400 character front page limit must be added to the “news.shtml” content page inside the <p class=”pageTitle”> tag, below the header “<h1>ARTEMIS News</h1>.” Include a news item summary title and the phrase “(continued from home page):” followed by the press release date and additional news text.  All images or videos should be scaled to 300px wide, with figure caption and appropriate media source credit.  Include citation and shortcut PDF links to all published papers.

**Please note: before adding a new front page news entry to “index.shtml,” the previous entry’s front page headline must be appended to the corresponding entry in the “news.shtml” page for archiving.

### ARTEMIS – Publications

Recent publications (2011-2012) are stored on the SSL server:

/disks/danaid/home/www/artemis/pubs/20XX_refereed

for peer-reviewed articles and all others under “pubs/20XX_nonrefereed.”  Publications are entered in both HTML and Excel formats in each folder and must be listed in alphabetical order, with author last name and first initial, month and year of acceptance, journal name, and then the full citation, with a link to the abstract, or if unavailable, to the publisher’s “in press” article page.

Older publications (pre-2010) are stored on the IGPP server RESEARCH1, using the same format:

//research1/research1/space_emergency/obitwo/cache5/data3/public/THEMIS/SCI/Pubs/artemis

Regardless of source location, each year of publications must be correctly linked via the file “publications.shtml,” in the ARTEMIS site root directory.

### ARTEMIS – Nuggets

ARTEMIS nuggets, or research summaries, are currently stored on the SSL server:

Summary page:

/disks/danaid/home/www/artemis/nuggets/nuggets_20YY/nuggets_YY.html

The summary page should list nuggets in reverse chronological order by month of acceptance, most recent first.  Each summary should be in lay language and no more than 2-3 sentences, with a 100px square image, linking to the detailed nugget.

Nugget page:

/disks/danaid/home/www/artemis/nuggets/nuggets_20YY/author/author_YY.html

Each nugget should follow the same format with Title, Author, Introduction, Results, Conclusion, Reference, and  Biographical Note.  Figures should be thumbnailed to 300px wide and link to the full size image (no larger than 1000px wide), and should be accompanied by a detailed caption.

Each year of nugget summaries must be correctly linked via the page “publications.shtml,” in the Themis site root directory.

Additional nugget images may be added to the slideshow on the ARTEMIS front page by editing “index.shtml” under the section <div id=“divnuggets”>, following the existing javascript slidelink script format.  Slideshow source images and an Adobe Photoshop PSD template can be found on the SSL site:

/disks/danaid/home/www/artemis/images/index.table/nuggets

# Software Distribution Administration

  - SVN Repository

The Themis Data Analysis Software (TDAS) is part of a Subversion (SVN) repository, residing on ambrosia.ssl.berkeley.edu. (For information regarding SVN, go to http://subversion.tigris.org/ .)  Access to the SVN repository is restricted, For access, developers are required to connect via SSH keys. Setup for SVN access is documented  at  http://themis.ssl.berkeley.edu/downloads/thm_crib_svn_cmdline.txt for command line users and http://themis.ssl.berkeley.edu/downloads/thm_crib_svn_gui.txt, for GUI users.

This section will discuss administration of the SVN repository. SVN administration is done by the THMSW user, which developers can access using SSH. (This is possible only from a local SSL workstation; type ssh thmsw@ambrosia and input your passphrase.) Once the developer has THMSW access, then he can access the THMSVN account.

The home directory of the THMSW user is /disks/socware. A number of shell scripts are located here which are used for administration.

6.2 THMSW Shell Scripts

Currently a number of shell scripts are used:

Thm_snapshot.sh  creates the nightly build of TDAS software for distribution. This is called in a cronjob each day.

Thm_release_tdas_6.sh creates a “release” of the current software, note that this MUST be called with arguments. E.g.,

/bin/csh thm_release_tdas_6.sh  tdas_6_00 tdas_6_00 tdas_6_00-COMMENT

The shell scripts:

thm_update_idx_exclude.sh

thm_update_production_calibration.sh

thm_update_production_config.sh

thm_update_production_gmag_mastercdf.sh

thm_update_production_idl.sh

thm_update_production_ksh.sh

thm_update_production_php.sh

are used to update various production directories.

6.3 TDAS Releases

TDAS occasionally is released with a version number. A release version of TDAS has gone through an  intensive QA process and is expected to perform without undue bugs, and without difficult to understand “features”.  To release a version of TDAS, issue the following commands as the THMSW user. This example is the script for releasing TDAS_7_00:

# removing and creating tdas_7_00 from scratch . DO THIS IF YOU ARE REPLACING A RELEASE #DURING QA

svn delete $SOCREPOS/thmsoc/branches/tdas_7_00 -m "deleting tdas_7_00 branch, rebuild from scratch"

svn delete $SOCREPOS/idl_socware/branches/tdas_7_00 -m "deleting tdas_7_00 branch"

svn delete $SOCREPOS/ssl_general/branches/tdas_7_00 -m "deleting tdas_7_00 branch"

svn delete $SOCREPOS/tdas/branches/tdas_7_00 -m "deleting tdas_7_00 branch"

rm -rf /disks/socware/tdas_7_00

rm -rf /disks/themisdata/socware/tdas_7_00

svn delete $SOCREPOS/tdas/tags/tdas_7_00 -m "Deleting tdas_7_00 tag"

svn delete $SOCREPOS/thmsoc/tags/tdas_7_00 -m "Deleting tdas_7_00 tag"

svn delete $SOCREPOS/ssl_general/tags/tdas_7_00 -m "Deleting tdas_7_00 tag"

svn delete $SOCREPOS/idl_socware/tags/tdas_7_00 -m "Deleting tdas_7_00 tag"

# Start here if there is no branch already

svn copy $SOCREPOS/thmsoc/trunk $SOCREPOS/thmsoc/branches/tdas_7_00 -m "Creating tdas_7_00 branch"

svn copy $SOCREPOS/ssl_general/trunk $SOCREPOS/ssl_general/branches/tdas_7_00 -m "ssl_general 7_00 branch"

svn mkdir $SOCREPOS/idl_socware/branches/tdas_7_00 -m "Create directory for tdas_7_00 branch"

svn copy $SOCREPOS/idl_socware/trunk/external $SOCREPOS/idl_socware/branches/tdas_7_00/external -m "Create tdas_7_00 branch"

svn mkdir $SOCREPOS/tdas/branches/tdas_7_00 -m "creating dir for tdas_7_00 in tdas/branches"

svn mkdir $SOCREPOS/tdas/branches/tdas_7_00/external -m "creating dir for tdas_7_00 in tdas/branches"

# Once you have a branch, and only want to release the new version, start here.

/bin/csh thm_release_tdas_6.sh tdas_7_00 tdas_7_00 tdas_7_00-jmm_20120227

#version 9888

The appropriate zip file will be available at the URL http://themis.ssl.berkeley.edu/socware/tdas_7_00/tdas_7_00.zip

The final step to the release is to change the link pointing to the latest release in the THEMIS Web software page:

http://themis.ssl.berkeley.edu/software.shtml

6.4 Adding New Users

The thmsw account is for building the /idl/socware distributions, and  is the gateway to svn administration.  It is not necessary for users to have access to it to use svn.

To log in as thmsvn, first log in to the thmsw account, then  type "thmsvn", which is an alias for ssh using a key that is restricted to svn use. Then cd to the  .ssh directory and  follow the examples/instructions in the thmsvn authorized_keys  file to add the new user. The user will provide a public SSH key for this purpose.

To add a new user’s email address to the notification message list, edit the file /home/thmsvn/repos/hooks/post-commit.

# Appendix

## GBO/EPO Site Map

The following map shows the location of the GBO and EP installations:

## THEMIS Data Mirror Sites

The following are mirror sites where THEMIS/ARTEMIS data can be accessed:

US-East Coast – Space Physics Data Facility – Goddard Space Flight Center

THEMIS Data Mirror Site - http://cdaweb.gsfc.nasa.gov/data/themis/

Administrator: Tami Kovalick: tamara.j.kovalick@nasa.gov

Japan – Institute of Space & Astronautical Science (ISAS) at JAXA

ISAS/JAXA THEMIS data mirror site - http://themis.stp.isas.jaxa.jp/data/themis/

Data accessible via any HTTP client tool (wget)

THEMIS Data Mirror Site at DARTS - http://darts.isas.jaxa.jp/stp/themis/

Data available via DARTS:

      - THA-THE spacecraft level-0 to 2 data : fully mirrored

      - GBO GMAG geomagnetic field level-2 data : fully mirrored

      - GBO ASI all-sky imager level-1 data: partially mirrored - thg_ast (thumbnail) and thg_ask (keogram)

      - Greenland geomagnetic field data

THEMIS data access via TDAS:

Set “Remote data directory” under File -> Configuration Settings of the TDAS GUI to

http://themis.stp.isas.jaxa.jp/data/themis/

Data Transfer: Using rsync via the themis-rsync server

Administrators: 	Dr. Iku Shinohara:  iku@stp.isas.jaxa.jp

darts-admin@ML.isas.jaxa.jp

France – Plasma Physics Data Center (CDPP) at Center for Space Radiation Studies (CERS)

CDPP THEMIS data mirror site - http://cdpp.cesr.fr/themisdata/

Data accessible via any HTTP client tool (wget)

CERS web-based THEMIS data analysis tools:

      - CLWEB - http://clweb.cesr.fr/ (for detailed studies)

      - AMDA - http://cdpp-amda.cesr.fr/DDHTML/index.html (visualisation, data mining, managing "simple" data)

THEMIS data access via TDAS:

Set “Remote data directory” under File -> Configuration Settings of the TDAS GUI to

http://cdpp.cesr.fr/themisdata/

Administrators:	Emmanuel Penou: penou@cesr.fr

Myriam Bouchemit: myriam.bouchemit@irap.omp.eu

UCLA – Institute of Geophysics and Planetary Physics (IGPP)

IGPP THEMIS data mirror site - http://themis-data.igpp.ucla.edu/

THEMIS data access via TDAS:

Set “Remote data directory” under File -> Configuration Settings of the TDAS GUI to

http://themis-data.igpp.ucla.edu/

Data Transfer: Using rsync via the themis-rsync server (nightly)

Administrators: 	Todd King:  tking@igpp.ucla.edu - 310.206.7120,

Bill Harris: bharris@igpp.ucla.edu - 310.825.9320

Chile – Site under construction

Data Transfer: Using rsync via the themis-rsync server

Administrator:	Marina Stepanova:  marina.stepanova@usach.cl

Currently (6/19/2012), the THEMIS data mirroring server is Horae, which will soon be retired and replaced by the VM server Ambrosia, via the DNS alias  “themis-rsync”. The “thmdata” user account allows read-only access to all of /disks/themisdata/, and should be the primary account used for rsync and scp mirroring jobs. The “thmsoc” secure shell authorized_keys corresponding to the mirror sites' administrators have been ported to the  “thmdata” authorized_keys, and all future themis-rysnc access should be via “thmdata.”

The default THEMIS data directories to be mirrored are as follows:

/disks/themisdata/tha

/disks/themisdata/thb

/disks/themisdata/thc

/disks/themisdata/thd

/disks/themisdata/the

/disks/themisdata/thg/l0

/disks/themisdata/thg/l1

/disks/themisdata/thg/l2

/disks/themisdata/thg/ascii_data

/disks/themisdata/thg/greenland_gmag

/disks/themisdata/thg/greenland_zipfiles

## Software Extensions for TDAS

The following missions are providing packages/plug-ins which are (to be) included in the TDAS distribution:

a)  Energization and Radiation in Geospace (ERG) Mission (plug-in)

Contacts: Yoshizumi Miyoshi (miyoshi@.stelab.nagoya-u.ac.jp),

erg-sc-core@st4a.stelab.nagoya-u.ac.jp

ERG site: http://gemsissc.stelab.nagoya-u.ac.jp/erg/

b) Inter-university Upper atmosphere Global Observation NETwork (IUGONET)

Contact: Tomoaki Hori Stel (horit@stelab.nagoya-u.ac.jp)

UDAS site: http://www.iugonet.org/en/software.html

c) Radiation Belt Storm Probes (RBSP) – will be part of TDAS

Contact: Peter Schroder (peters@ssl.berkeley.edu)

RBSP site: http://rbsp.jhuapl.edu/

## IDL Technical Support

IDL Vendor - Exelis (IDL was formerly owned by ITT)

Exelis IDL Technical Support Page - http://www.exelisvis.com/language/en-US/Support.aspx

Sales Rep:  Brian Farr	303-402-4670     email: Brian.Farr@exelisvis.com

Technical Support:	303-413-3920     email: support@exelisvis.com