# Fluxgate Magnetometer Module (FGM.A)

The FGM module manage the FGM instrument interfaces for commands and telemetry.

## Initialization.

The FGM module initializes the FGM range settings to zero (namely "Full Scale"), sets the FGMH and FGML DMA channels to point to "TrashCan"  and enables the FGM DMA logic.

## Operation.

### FGM Houskeeping Readback

The FGM module uses a 4Hz interrupt for reading back the FGM status byte contained in the FGM messages and shall provide these status bits to SOH.

### DMA Channel Management

The module monitors at 4 Hz the FGMH and FGML DMA Channels, providing new DMA addresses within 1 second of the last channel swap, and providing a swap enable for each channel when the packet should complete at the next 1 second tick.

The algorithm for determining when to swap reads the rate code (3 bits) and uses a table lookup to find a mask of seconds. When the mask & seconds is zero, it is time to swap.

### Fluxgate Magnetometer Engineering Telemetry

Every 125 msec, the module buffers 16-bit BX, BY, BZ points from the DCB registers and formats a CCSDS APID 405 packet for a possible transmission every 2 seconds. If requested by the TM module, the FGM module has a packet ready for delivery to the TM low speed output.

### Spin Fit Data Generation

The FGM module provides 16-bit BX, BY, BZ points from the DCB registers when requested by the FIT module.

## Commands.

The FGM module provides initialization, frequency control and range control for the FGM using the following commands:

- IFGEINIT	Sends the Default CDI Sequence to FGE

- IFGECONF	Sets Config. Byte to Mark all FGM Packets

- IFGEFREQ	Sets FGE TML Sampling Rate. Codes [0 to 7]

- IFGERANGEX	Sets FGE Range X,  R = Range Value

- IFGERANGEY	Sets FGE Range Y,  R = Range Value

- IFGERANGEZ	Sets FGE Range Z,  R = Range Value

The FGEINIT command sends the FGM Initial Configuration list. This list  contains settings for the DACs etc on the FGE control circuit and also contains a "Start FGM" command.