From:	M. Bester

To:	Operations & Science Team

Date:	12-Oct-2006

Re:	Ephemeris Format Definition

Ephemeris Format Definition

- Introduction

Ephemeris files containing position, velocity, attitude and other relevant orbit and mission parameters are used to exchange and process orbit and trajectory information within the THEMIS flight dynamics system, in particular with MDT, GTDS, GMAN and SatTrack. Ephemeris files in the format described here or in alternate formats are also used to distribute pre-launch orbit data to the THEMIS team and to the science community. Ephemeris data are also archived along with the mission science data for further scientific analysis.

- Ephemeris File Format

Ephemeris files are written in plain ASCII format, and contain one header line plus an unlimited number of data lines. The header line identifies the content in each column and consists of names of parameters plus their associated units, enclosed in double quotes and separated by commas. The data are listed sequentially, and columns are separated by any number of white space characters. Each line – header or data – is terminated with a linefeed character (ASCII 10). An additional carriage return character (ASCII 13) is allowed also. File reader functions should be implemented in a case insensitive form. Time steps from one line to the next may be as small as 0.001 s.

Several samples illustrating how headers are formed are shown below. Allowed data columns and associated entries in the header line are summarized in Table 1. Additional parameters may be added in the future. Note that for clarity of this document, the single header line is broken up into several lines.

”Date (UTC)”,”Time (UTC)”,”ECI TOD X [km]”,”ECI TOD Y [km]”,”ECI TOD Z [km]”,

"ECI TOD VX [km/s]”,”ECI TOD VY [km/s]”,”ECI TOD VZ [km/s]”,

”Anomalistic Orbit [rev]”

”ECI TOD AX [---]”,”ECI TOD AY [---]”,”ECI TOD AZ [---]”

”SARA TOD [deg]”,”SADEC TOD [deg]”,”Spin Rate [rpm]”

”Total Mass [kg]”,”Fuel Mass [kg]”,”Total Delta V [m/s]”,”Maneuver Status [---]”

For the Date and Time columns the time zone is enclosed in round brackets, and for all other columns units are enclosed in square brackets. If a parameter is dimensionless, then the unit is shown as three dashes.

Note that all position, velocity and attitude components are to be expressed in the same, Earth Centered Inertial (ECI) true-of-date (TOD) (true equator and true equinox of date) reference frame. Presently, the second valid reference frame is J2000.0 (mean equator and mean equinox of J2000.0). When the latter is specified, then J2000.0 needs to be inserted into the header entries of all vector components in the following way:

”ECI J2000.0 X [km]”,”ECI J2000.0 Y [km]”,”ECI J2000.0 Z [km]”

Other reference frames may be implemented in the future. Allowed length units are km (kilometers), sm (statute miles), nm (nautical miles) and ft (feet), and allowed angle units are deg (degrees) and rad (radians). Hour angle units may be expressed in h (hours), deg (degrees) or rad (radians).

| Table 1: Definition of Header Elements and Data Columns |
| --- |
| Parameter | Allowed Header Entries | Data Format | Number of Decimal Places |
| Date | Date (UTC) | yyyy/ddd yyyy/mm/dd dd-Mmm-yyyy | Fixed Format |
| Time | Time (UTC) | hh :mm :ss.sss | Fixed Format |
| Position | ECI TOD X [km] ECI TOD Y [km] ECI TOD Z [km] | Double Precision | 16 |
| Velocity | ECI TOD VX [km/s] ECI TOD VY [km/s] ECI TOD VZ [km/s] | Double Precision | 16 |
| Attitude (Body Z Axis) | ECI TOD AX [---] ECI TOD AY [---] ECI TOD AZ [---] | Double Precision | 12 |
| Spin Axis Right Ascension / Declination | SARA TOD [deg] SADEC TOD [deg] | Double Precision | 6 |
| Geographic Coordinates | Latitude [deg N] or [deg S] Longitude [deg W] or [deg E] Altitude [km] or Height [km] | Double Precision | 6 6 6 |
| Celestial Coordinates | RA TOD [h] DEC TOD [deg] | Double Precision | 12 9 |
| Orbital Elements | SMA [km] ECC [---] INC [deg] RAAN [deg] ARGP [deg] MA [deg] or TA [deg] | Double Precision | 12 12 12 12 12 12 |
| Orbit | Anomalistic Orbit [rev] or Nodal Orbit [rev] | Double Precision | 9 |
| Mass | Total Mass [kg] Fuel Mass [kg] | Double Precision | 3 3 |
| Delta V | Total Delta V [m/s] | Double Precision | 3 |
| Spin Rate | Spin Rate [rpm] | Double Precision | 3 |

| Table 1 (Continued): Definition of Header Elements and Data Columns |
| --- |
| Parameter | Allowed Header Entries | Data Format | Number of Decimal Places |
| Ground Network Access Status Code | GN Status [---] | Coded Integer 0-65535 | 0 |
|  |  | Ground Station 1 … Ground Station 16 | 1 32768 |  |
| Space Network Access Status Code | SN Status [---] | Coded Integer 0-65535 | 0 |
|  |  | TDRS 1 … TDRS 16 | 1 32768 |  |
| Space Environment Region Crossing Status Code | SE Region Status [---] | Coded Integer 0-262143 | 0 |
|  |  | Earth Shadow Lunar Shadow Atmospheric Absorption Zone South Atlantic Anomaly Northern Auroral Zone Southern Auroral Zone Perigee Passage Inner & Outer Radiation Belts Deep Plasma Sphere Foreshock Solar Wind Solar Wind Beam High Magnetic Field Average Plasma Sheet Bowshock Crossing Magnetopause Crossing Ground Based Observatories 2-Day Conjunctions 4-Day Conjunctions | 1 2 4 8 16 32 64 128 256 512 1024 2048 4096 8192 16384 32768 65536 131072 |  |

| Table 1 (Continued): Definition of Header Elements and Data Columns |
| --- |
| Parameter | Allowed Header Entries | Data Format | Number of Decimal Places |
| Maneuver Status Code | Maneuver Status [---] | Coded Integer XYYZZZ | 0 |
|  |  | Unpowered Flight (Coast) X=0, YY=00, ZZZ=000 Maneuver Sequence Number ZZZ Maneuver Type Code YY Launch Vehicle Maneuver Axial-thrust Maneuver Side-thrust Maneuver Beta-thrust Maneuver Attitude Precession Spin Rate Change Maneuver Sequencing Code X No Segmentation Segmented Maneuver | 0 001-999 0 1 2 3 4 5 0 1 |  |
| Data Processing Status Code | Data Status [---] | Coded Integer 0-65535 | 0 |
|  |  | No Change Orbit Determination Maneuver Reconstruction Attitude Determination Mass Properties Update RCS Parameter Update Spare | 0 1 2 4 8 16 32-32768 |  |

- Regions of Interest

Definitions of the Regions of Interest (ROIs) are summarized in Table 2 below. Note that not all of these regions are used with THEMIS but are listed for compatibility with other missions.

| Table 2: Regions of Interest |
| --- |
| Region Name | Acronym | Region Definition |
| Earth Shadow | ESH | Solar disk obscured by Earth by more than 1% (99% visible) (including umbra and penumbra) |
| Lunar Shadow | LSH | Solar disk obscured by Moon by more than 1% (99% visible) (including umbra and penumbra) |
| Atmospheric Absorption Zone | AAZ | Spacecraft sees Sun through Earth atmosphere |
| South Atlantic Anomaly | SAA | Region defined by mission specific latitude/longitude contour |
| Northern Auroral Zone | NAZ | Region defined by mission specific latitude/longitude contour |
| Southern Auroral Zone | SAZ | Region defined by mission specific latitude/longitude contour |
| Perigee Passage | PGP | Spacecraft passes within ± 1 hour of perigee |
| Inner & Outer Radiation Belts | RBT | Spacecraft within L-shell at L = 4 RE (IGRF model) |
| Deep Plasma Sphere | PSP | Spacecraft within L-shell at L = 4 RE (IGRF model) |
| Foreshock Solar Wind | SHK | Outside of nominal bowshock distance D minus a tolerance t t = min(3 RE, ½ sheath thickness) |
| Solar Wind Beam | SWB | XGSE > threshold radius (20 RE) |
| High Magnetic Field | HMF | Spacecraft within radial distance of 5 RE (approximation of B field magnitude > 300 nT) |
| Average Plasma Sheet | APS | Spacecraft within XGSE < -5 RE, thickness of plasma sheet = 5 RE, hinge point at -10 RE (Hammond model) |
| Bowshock Crossing | BSC | Bowshock crossing ± 1.5 hours |
| Magnetopause Crossing | MPC | Magnetopause crossing ± 1.5 hours |
| Ground Based Observatories | GBO | UTC range of Ground Based Observatories: 06:30 UTC ± 6 h on tail season wedding day ± 60 days 18:30 UTC ± 6 h on dayside season wedding day ± 60 days |
| 2-Day Conjunctions | C2D | THEMIS P2 / P3 / P4 Probe alignment |
| 4-Day Conjunctions | C4D | THEMIS P1 / P2 / P3 / P4 Probe alignment |

- Sample Ephemeris File

The following data set is an abbreviated sample ephemeris file illustrating date, time and Cartesian spacecraft position columns:

”Date (UTC)”,”Time (UTC)”,”ECI TOD X [km]”,”ECI TOD Y [km]”,”ECI TOD Z [km]”

2005/277  00:00:00.000    6124.037249   -1710.773860   -2770.373467

2005/277  00:01:00.000    6126.919825   -1305.861124   -2978.072602

2005/277  00:02:00.000    6103.464919    -895.334874   -3172.935022

2005/277  00:03:00.000    6053.784434    -480.961425   -3354.126556

2005/277  00:04:00.000    5978.102991     -64.522149   -3520.872702

2005/277  00:05:00.000    5876.756717     352.194241   -3672.461856