THEMIS

FGM CAL File and Processing

THM-SOC_113_FGM_CALPROC

October, 2006

Timothy Quinn, THEMIS Science Operations

Dr. John Bonnell, THEMIS EFI

Dr. Alain Roux, THEMIS SCM

Dr. Uli Auster, THEMIS FGM

Dr. Davin Larson, THEMIS SST

Dr. Krishan Khurana, THEMIS Science ACS

Michael Ludlam, THEMIS ISE

Peter Harvey, THEMIS Project Manager

Vassilis Angelopoulos, THEMIS Principal Investigator

# Document Revision Record

| Rev. | Date | Description of Change | Approved By |
| --- | --- | --- | --- |
| 1 | 2006-10-06 | Draft | - |
| 2 |  |  |  |

# Distribution List

| Name | Email |
| --- | --- |
| Harald Frey, U.C. Berkeley | hfrey@ssl.berkeley.edu |
| Edita Georgescu, MPE Garching | eg@mpe.mpg.de |
| Karl Heinz Fornaconr, UCB | k-h.fornacon@tu-bs.de |
| Hannes Schwarzl, UCLA | schwarzl@igpp.ucla.edu |
| Krishan Khurana, UCLA | kkhurana@igpp.ucla.edu |
| Werner Magnes, IWF | Werner.Magnes@oeaw.ac.at |

# TBD List

| Identifier | Description |
| --- | --- |

Table of Contents

Document Revision Record	2

Distribution List	2

TBD List	2

1.	Introduction	2

1.1	Purpose and Scope.	2

1.2	Applicable Documents.	2

2.	Definition of quantities (coordinate systems, transformation matrices, offsets)	2

2.1	Coordinate systems:	2

2.2	Offsets and Transformation Matrices	2

3.	Creation of Cal Files	2

4.	Application of Cal Files	Error! Bookmark not defined.

# Introduction

## Purpose and Scope.

The document describes the calibration procedure from raw data (in a non orthogonal sensor system) into a coordinate system which is defined by spacecraft spin axis and sun sensor direction (SSL). Creation and application of the Cal File is described. The document contains the preflight determined initial values and gives an overview how the L0..L2 data are processed.

## Applicable Documents.

- THM_SYS_012_PDMP				THEMIS Project Data Management Plan

- THM_SOC_101_TIME				THEMIS TIME Definition

- THM_SOC_108_GMAG_L1_VARNAMES		THEMIS GMAG Variable Name Def’s

- THM_SOC_110_COORDINATES			THEMIS Science Coord. Systems Def.

- THM_SOC_111_SUNSENSPROC			THEMIS SUN SENSOR Science Processing

- THM_SOC_112_ATTPAIPROC			THEMIS Science ATT & Inertia Determ.

- THM_SOC_113_FGM_CALPROC		THEMIS FGM CAL File and Processing

- SAI-SPEC-1079A (Oct 26, 2005)			THEMIS Coordinate systems

- SAI-RPT-0722a (September, 2006)			Probe Alignment Report (MSSS data, p18)

- pturin e-mail on Faro alignment results (9/28/06)	FGM, SCM mag alignments

- THM-MB-MEC-005-Magnetometer clocking r7.pdf 	MAG clocking angles

# Definition of quantities (coordinate systems, transformation matrices, offsets)

## Coordinate systems:

FS	-	non orthogonal sensor system

FGS	-	orthogonal sensor system (blue system in Figure 1,  x-axis and xy-plane unchanged versus FS)

UNIT	-	FGM sensor system as defined by ICD (see red system in Figure 1).

SPG	-	Spinning Probe Geometric (or probe coordinate system) This system is defined by the mechanical designers of the probe in SAI-SPEC-1079A - see Figure 3. The z-axis is directed through the probe normal to the attachment plane. The x-axis is aligned normal to the face sheet of Solar Panel1. This face has an adjacent corner, moving counterclockwise, housing the ESA. In other words the ESA shall fall in the +x/+y quadrant of the probe coordinate system. The y-axis completes a right handed orthogonal triad.

SR:	-	spin aligned spacecraft system. This system points with z along the Spin axis of the probe. (the momentum vector is along the principal axis of inertia). The Izz was measured during spin balance tests at JPL to be within 0.25deg of the geometric axis assuming (by modeling) magnetometer booms have been deployed but EFI booms are stowed. As fuel is consumed this angle is expected to change but not by much. A more precise determination of the difference between geometric Z and spin axis and its function of time will be done during inflight calibration by minimizing the spin tone in the Z component. These two angles are recorded in the daily STATE file.

SSL:	-	Spinning SunSensor – L-vectorZ.  Also this system points with z along the Spin axis of the probe. The x axis of the system points towards the Sun Sensor (Miniature Spinning Sun Sensor) look direction. Theoretical angle between the Sun Sensor look direction and the probe X axis is 135 deg (rotation about spin axis). The pointing of the sun sensor is shown in Figure 2, excerpt from SAI-spec 1079a.

Remark: Names of coordinate systems are partly defined in THM_SOC_110_COORDINATES (UNIT, SPG, SSL) or taken from Cluster nomenclature (FS, FGS, SR).

## Offsets and Transformation Matrices

- Ranging Factor   kr

derived by range value which has to be extracted from the fgm header.

kr = 50000/2(16+range)

- Sensor Offset

Offset in standard mode (closed feedback) depends on feedback “zero” current therefore it is dominated by FGE. Offsets of sensors are close to zero. Offsets are determined by pre-flight calibration and depends on mode. Mode dependency will be not processed because we assume that FGM operates most time in standard mode. Open loop modes are used for health checks and in emergency case only. Pre-flight determined standard mode offsets shall be used as default.

Table of offsets (derived from pre-flight tests made in Europe, Berkeley and JPL):

|  | Ofgm_x | Ofgm_y | Ofgm_z |
| --- | --- | --- | --- |
| Probe 1 (FGE4) | -5 | -11 | - |
| Probe 2 (FGE1) | -6 | -8 | -5 |
| Probe 3 (FGE2) | -5 | -7 | -5 |
| Probe 4 (FGE3) | -8 | -3 | -3 |
| Probe 5 (FGE5) | -3 | -3 | -3 |

- Orthogonalisation Matrix

Orthogonality depends on alignment of the feedback coil system, therefore it depends only on FGS. Misalignment is known from ground calibration with high precision, nevertheless it will be updated by inflight calibration.

Table of angel of non-orthogonality (derived from measurements in JH and Magnetsrode):

|  | alphaxy | alphaxz | alphayz |
| --- | --- | --- | --- |
| Probe 1 (FGS6) | 0.0031 | 0.0016 | 0.0023 |
| Probe 2 (FGS1/9) | 0.0065 | 0.0028 | 0.0107 |
| Probe 3 (FGS2) | -0.0021 | -0.0041 | -0.0049 |
| Probe 4 (FGS3) | 0.0012 | 0.0085 | 0.0040 |
| Probe 5 (FGS5) | -0.0090 | -0.0016 | 0.0066 |

- Sensor Accommodation Matrix

with:

First the individual error of each sensor alignment due to its mounting tolerances has to be eliminated by rotation about preflight determined angles betaxy, betaxz and betayz, and second the rotation about the z axis has to be performed. Munit will be not modified during inflight calibration

Table of angel of sensor accommodation (derived from measurements in JH):

|  | betaxy | betaxz | betayz |
| --- | --- | --- | --- |
| Probe 1 (FGS6) | -0.1166° | 0.1218° | -0.1248° |
| Probe 2 (FGS1/9) | -1.2698° | -0.0398° | -0.3797° |
| Probe 3 (FGS2) | -0.1368° | 0.1480° | 0.5058° |
| Probe 4 (FGS3) | 0.3398° | -0.2799° | -0.0473° |
| Probe 5 (FGS5) | 0.2963° | 0.0754° | -0.6155° |

- Boom Accommodation Matrix Mprobe

Boom accommodation matrices probe individual and different for stowed and deployed boom. Values are determined by Paul. Mprobe will be not modified during inflight calibration.

Table of matrices of boom accommodation (measured by Paul):

|  | stowed boom | deployed boom |
| --- | --- | --- |
| Probe 1 (FGS6) |  |  |
| Probe 2 (FGS1/9) |  |  |
| Probe 3 (FGS2) |  |  |
| Probe 4 (FGS3) |  |  |
| Probe 5 (FGS5) |  |  |

- Spin Alignment Matrix Mspin

The Z-axis has been fine tuned by rotation about Xprobe and Yprobe to the spin axis.

Initial values can be derived from the measurements by Paul during post I&T spin balance and alignment measurement (see MAG_Sensor_to spin_axis PTVA.xls).

with:	    =90,xx° (depends on probe)

= 0.25°

= 45.0°

The alignment of the x axis to the sun sensor will be done separately see definition of  Msun

We separate the spin alignment from the combined spin alignment/sun sensor orientation matrix in the following way:

This gives us the following initial spin alignment matrix:

Mspin will be updated by inflight calibration

- Scale Values Matrix Mscale in dependency of UCLA calibration output

Mscale will be updated by inflight calibration using input from UCLA Earth field model fitting.

- Spacecraft Offset Osc

Osc will be updated by inflight calibration, Osc_x and Osc_y are determined by spin tone minimisation, Osc_z by Hedgecock method

Initial values for the deployed boom are taken from the magnetic cleanliness measurement

- Sun Pulse Matrix

Direction of sun sensor is determined by Paul for each individual probe.

Msun will not be modified during inflight calibration.

Table of angles () with respect to sun sensor (measured by Paul):

|  | stowed boom | deployed boom |
| --- | --- | --- |
| Probe 1 (FGS6) | 135.00 | 135.17 |
| Probe 2 (FGS1/9) | 135.00 | 134.88 |
| Probe 3 (FGS2) | 135.00 | 134.98 |
| Probe 4 (FGS3) | 135.00 | 135.07 |
| Probe 5 (FGS5) | 135.00 | 134.92 |

- Phase Alignment Matrix

The phase of the rotation has to be tuned by rotation about Zprobe.

Mphase will be updated by inflight calibration using input from UCLA Earth field model fitting.

- Filter Matrix

The averaging effect of spin plane components has to be compensated by rescaling of X and Y components in dependency on the sampling rate and filter mode (Mfilter). In filter mode-3 data are calculated by averaging 128Hz raw data. Averaging of data before despinning causes an amplitude error as well as a spin phase error of the components perpendicular to the spin axes. The error depends on the ratio of spin frequency fspin and sampling frequency fsample.

with                 and

# Creation of Cal Files

The following manipulations have to be done with the FGM raw data to calibrate them and to bring them from FS to SSL system

| Step | Description | Purpose Coordinate system Update by inflight calibration? |
| --- | --- | --- |
| 1 | Multiplication with kr | To eliminate the ranging, range information from header In FS system No inflight issue |
| 2 | Subtraction of Ofgm | Compensation of sensor offset In FS system Only offsets in open loop mode are updated |
| 3 | Multiplication with Mort | Orthogonalisation of sensor system From FS to FGS system Update part of inflight calibration |
| 4 | Multiplication with Munit | Compensation of sensor accommodation tolerances and rotation into Unit system by From FGS to Unit system No inflight issue |
| 5 | Multiplication with Mprobe | Compensation of boom accommodation tolerances and Rotation into Probe system From Unit to Probe system No inflight issue |
| 6 | Multiplication with Mspin | Alignment of Z-axis to spin axis From Probe to SR-System Updated by inflight calibration |
| 7 | Multiplication with Mscale | Fine tuning of Scale values In SR system Inflight calibration |
| 8 | Subtraction of Osc | Compensation of spacecraft offset In SR system Inflight calibration |
| 9 | Multiplication with Msun | Rotation in Sun sensor direction From SR in SSL system No inflight issue |
| 10 | Multiplication with Mphase | Fine tuning of Phase From preliminary to perfect SSL Inflight updated by UCLA input |
| 11 | Multiplication with Mfilter | Compensation of Filter influence, mode information from header (mode and sampling frequency)and from Cal File (spin frequency) necessary In SSL No inflight issue |

After applying the steps 1-11 the magnetic field Bssl in SSL system can be written

Bssl  =  Mfilter  Mphase   Msun   (Mscale  Mspin   Mprobe   Munit   Mort   (kr * Bfs  - Ofgm)  -  Osc)

With exception of Mfilter and kr which depends on sampling frequency, mode and range all other parameters can be summarized in a calibration Matrix Mcal and a calibration Offset Ocal with:

Ocal  =  Mphase   Msun   Mscale  Mspin   Mprobe   Munit   Mort   Ofgm  +  Mphase   Msun   Osc

Mcal  =  Mphase   Msun   (Mscale  Mspin   Mprobe   Munit   Mort

Therefore Bssl  can be written as:

Bsr  =  Mfilter  ( Mcal   kr * Bfs  - Ocal )

The data processing software has to upload the actual Mcal and  Ocal  from the Calibration File, the factor kr has to be uploaded from the header information and the Filter Matrix has to be derived by sampling frequency (header) and spin frequency (Cal File).

# Initial Cal Files:

For THA (Probe 1) the initial Cal File for deployed boom has the following elements:

Time (2007-02-28T09:38:55.123Z) 3.61 11.00 5.35 0.08291 –0.003200 –0.99635 –0.00041 1.00000 0.00116 –0.99654 –0.00292 –0.08448 Spin-period (1.12345)

# Text boxes

Figure3

Figure2

Figure1

Figure 1 SPG system, probe view from top.