THEMIS

GBO All-Sky Imager Calibration File Definition

THM-SOC-117

November 08, 2006

Timothy Quinn, THEMIS Science Operations

Dr. B. Jackel, THEMIS ASIs

Dr. H. Frey, THEMIS ASIs

Vassilis Angelopoulos, THEMIS PI

# Document Revision Record

| Rev. | Date | Description of Change | Approved By |
| --- | --- | --- | --- |
| 1 | 2006-11-07 | Draft | - |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 |  |  |  |
| 5 |  |  |  |
| 6 |  |  |  |
| 7 |  |  |  |
| 8 |  |  |  |

# Distribution List

| Name | Email |
| --- | --- |
| Jim Lewis, U.C. Berkeley | jwl@ssl.berkeley.edu |
| Stuart Harris | sharris@ssl.berkeley.edu |
| Dr. Eric Donovan, U of Calgary | eric@phys.ucalgary.ca |
| Dr. Stephen Mende, UCB | mende@ssl.berkeley.edu |
| Dr. Dave Sibeck, NASA GSFC | david.g.sibeck@nasa.gov |

# TBD List

| Identifier | Description |
| --- | --- |

Table of Contents

Document Revision Record	2

Distribution List	2

TBD List	2

1.	Introduction	4

1.1	Purpose and Scope.	4

1.2	Applicable Documents.	4

1.3	General calibration file content	4

2.	Calibration parameter definition	4

2.1	General parameters	4

2.2	Parameters related to mapping of images	5

2.3	Quantitative calibration	7

# Introduction

## Purpose and Scope.

THEMIS Level 1 ASI data are stored in CDF files.  This document defines the additional calibration files that together with plotting tools have to be used in order to plot the data in a scientifically useful way (produce physical quantities and plots) and integrate analysis and plotting routines together with the rest of THEMIS data products (GMAGs and spacecraft). The calibration files will contain all the information that is necessary to derivative L2 files from L1 data files.

## Applicable Documents.

- THM_SYS_012_PDMP				THEMIS Project Data Management Plan

- THM_SOC_101_TIME				THEMIS TIME Definition

- THM_SOC_108_GMAG_L1_VARNAMES		THEMIS GMAG Variable Name Def’s

- THM_SOC_109_ASI_L1_VARNAMES		THEMIS ASI variable name definition

## General calibration file content

Each of the 20 GBO stations will have one calibration file that will contain all information necessary to calibrate full-resolution images, thumbnail images, and keogram strips. The validity of a certain parameter set will be marked with a validity start- and end-time. All the following varaibale names will be shown for the example of Athabasca station (“atha”) but will apply in the same way to all the other 19 stations of the THEMIS GBO array as they are defined in document THM_SOC_109_ASI_L1_VARNAMES.

# Calibration parameter definition

## General parameters

The general parameters refer to the time and time range of validity of a certain parameter set and station parameters that are not expected to change dramatically over the time of the mission. Whenever a parameter in the calibration files needs to be updated, a completely new parameter set with a new start- and end-time will be put into the file.

Table 1: THEMIS GBO station general calibration parameters

| Variable | Type | Purpose |
| --- | --- | --- |
| thg_asc_atha_time | REAL*8 | Start time of validity of parameter set in seconds since 1970-01-01/00:00:00, first set will have 0.0 |
| thg_asc_atha_tend | REAL*8 | End time of validity of parameter set in seconds since 1970-01-01/00:00:00, last set will have 4.E9 (2096-10-02/07:06:00) |
| thg_asc_atha_epoch | EPOCH | CDF Epoch for start time |
| thg_asc_atha_epoch0 | EPOCH | EPOCH value of time baseline 1970-01-01/00:00:00.000 |
| range_epoch | EPOCH, 2 elements | Epoch values of first and last data record |
| thg_asc_atha_longitude | REAL*4 | Geographic longitude of station |
| thg_asc_atha_latitude | REAL*4 | Geographic latitude of station |
| thg_asc_atha_altitude | REAL*4 | Geographic altitude of station |
| thg_asc_atha_maglong | REAL*4 | Geomagnetic longitude of station |
| thg_asc_atha_maglat | REAL*4 | Geomagnetic latitude of station |
| thg_asc_atha_midnight | CHAR | UT of magnetic midnight at station |

## Parameters related to mapping of images

These parameters will allow the mapping the image pixels into useful coordinates (geographic and geomagnetic).

Table 2: THEMIS GBO station mapping calibration parameters

| Variable | Type | Purpose |
| --- | --- | --- |
| thg_asc_atha_32_elevation | REAL*4, 1024x4 values of degrees from 0. at horizon to 90. at zenith | Elevation of 1024 pixel corners of thumbnails from lower-left, lower-right, upper-right, upper-left |
| thg_asc_atha_32_azimuth | REAL*4, 1024x4 values of degrees from 0. at geographic north, 90. at geographic east, and 180 at geographic south | Azimuth of 1024 pixel corners of thumbnails from lower-left, lower-right, upper-right, upper-left |
| thg_asc_atha_32_latitude | REAL*4, 1024x4 values of degrees | Geographic latitude of 1024 pixel corners of thumbnails from lower-left, lower-right, upper-right, upper-left at assumed altitude |
| thg_asc_atha_32_longitude | REAL*4, 1024x4 values of degrees | Geographic longitude of 1024 pixel corners of thumbnails from lower-left, lower-right, upper-right, upper-left at assumed altitude |
| thg_asc_atha_32_altitude | REAL*4, single value | geographic altitude that was used to calculate latitude/longitude |
| thg_asc_atha_32_maglat | REAL*4, 1024x4 values of degrees | Geomagnetic latitude of 1024 pixel corners of thumbnails from lower-left, lower-right, upper-right, upper-left at assumed altitude |
| thg_asc_atha_32_maglong | REAL*4, 1024x4 values of degrees | Geomagnetic longitude of 1024 pixel corners of thumbnails from lower-left, lower-right, upper-right, upper-left at assumed altitude |
| thg_asc_atha_img_elevation | REAL*4, 257x257 values of degrees from 0. at horizon to 90. at zenith | Elevation of lower left corner of all 256x256 pixels of full resolution images |
| thg_asc_atha_img_azimuth | REAL*4, 257x257 values of degrees from 0. at geographic east, and 180 at geographic south | Azimuth of lower left corner of all 256x256 pixels of full resolution images |
| thg_asc_atha_img_latitude | REAL*4, 257x257 values of degrees | Geographic latitude of lower left corner of all 256x256 pixels of full resolution images |
| thg_asc_atha_img_longitude | REAL*4, 257x257 values of degrees | Geographic longitude of lower left corner of all 256x256 pixels of full resolution images |
| thg_asc_atha_img_maglat | REAL*4, 257x257 values of degrees | Geomagnetic latitude of lower left corner of all 256x256 pixels of full resolution images |
| thg_asc_atha_img_maglong | REAL*4, 257x257 values of degrees | Geomagnetic longitude of lower left corner of all 256x256 pixels of full resolution images |

## Quantitative calibration

Those parameters will be used to transform the image counts into physical quantitative units once a thorough instrument and star calibration will be performed. Most of the will at this time just contain default values.

Table 3: THEMIS GBO station quantitative calibration parameters

| Variable | Type | Purpose |
| --- | --- | --- |
| thg_asc_atha_offset | UINT2, default is 0 | DC offset to transform Value = counts - offset |
| thg_asc_atha_radial | REAL*4, 128 elements, default is 1.0 | Radial sensitivity correction to obtain flat field with Value = radial * value |
| thg_asc_atha_sensitivity | REAL*4, default is 1.0 | Calibration factor to obtain the same apparent brightness of Polaris in all cameras Value = sensitivity * value |