THEMIS

L2 File Definitions

THM-SOC-125

September 2011

Lydia Philpott, THEMIS Science Software Engineer

Jim Lewis, THEMIS Science Software Engineer

Pat Cruce, THEMIS Science Software Engineer

Aaron Flores, THEMIS Science Software Engineer

Ben Sadeghi, THEMIS Science Software Engineer

Jim McTiernan, THEMIS Science Software Engineer

David A. King, THEMIS Science Software Manager

Vassilis Angelopoulos, THEMIS Principal Investigator

# Document Revision Record

| Rev. | Date | Description of Change | Approved By |
| --- | --- | --- | --- |
| - | Sep 2011 | Initial Version | D. King |

# Distribution List

| Name | Email |
| --- | --- |

Table of Contents

Document Revision Record	2

Distribution List	2

1. Introduction	4

1.1 Purpose and Scope	4

1.2 Applicable Documents	4

2. Common Data Format	4

3. L1->L2 Processing	5

4. L2 CDFs	5

4.1 ESA (Electrostatic Analyzer)	13

4.2 SST (Solid State Telescope)	16

4.3 MOM (On board Moments)	16

4.4 EFI (Electric Field Instrument)	19

4.5 FBK (Filter Bank Data)	21

4.6 FFT (On Board Fast Fourier Transform)	22

4.7 FGM (Fluxgate Magnetometer)	24

4.8 FIT (On Board Spin-Fit Electric and Magnetic Field Data)	25

4.9 GMAG (Ground Magnetometer)	27

4.10 SCM (Search Coil Magnetometer)	28

# Introduction

## Purpose and Scope

Three levels of THEMIS data products exist: “Level 0” (L0), “Level 1” (L1), and “Level 2” (L2). L0 data is in the form of raw packets. L1 data is time-tagged, uncalibrated data, stored in Common Data Format (CDF) files. L2 data, also stored as CDF files, consists of calibrated data in geophysically relevant coordinates. This document discusses the structure of the L2 CDF files, together with the processes involved in producing them. For a discussion of the L1 data files see the L1 File Definitions document. For a discussion of the L2 GMAG data files in particular, see the Ground Magnetometer L2 Data Files Variable Name Definition document.

## Applicable Documents

- THM_SOC_124_L1_FILE_DEF			THEMIS  L1 File Definitions

- THM_SOC_108_GMAG_L2_VARNAMES	THEMIS Ground Magnetometer L2 Data Files Variable Name Definition

- THM_SOC_110_COORDINATES	THEMIS Science Coordinate Systems Definition

- thm_l2gen_demo.txt	Detailed example of L1->L2 processing

- THM_SOC_101_TIME	THEMIS Science TIME Definition

- THM_SOC_135_TIME_CONVENTIONS	THEMIS/ARTEMIS timekeeping conventions

# Common Data Format

CDF (Common Data Format) is a means of storing and manipulating multidimensional data sets and associated metadata.  Full documentation, software, conversion tools, and so on, are available from NASA/GSFC at http://cdf.gsfc.nasa.gov/. CDF files are manipulated using the CDF library application programming interfaces (APIs) – users are isolated from the actual format in which the data is stored. The resulting files can be transported between any of the platforms supported by CDF.

CDF files contain “variables” (the data) and “attributes”. Variables are organized as multidimensional arrays, ranging from 0-dimensional arrays for scalar data, up to 10. Each variable is also assigned a data type, for example CDF_BYTE, CDF_CHAR, CDF_INT4. A “CDF record” is comprised of an array for each of the variables – CDFs can contain multiple records, but the array size for a variable cannot vary between records. CDFs can also contain ‘virtual’ variables. The values for virtual variables are not contained within the CDF, instead they can be calculated by some external code.

The attributes in a CDF are divided into global attributes (gAttributes), which include the metadata describing the CDF file, and variable attributes (vAttributes), which describe the properties of the variables.  Global attributes include information such as the project and PI names; variable attributes include information such as the units for the data. THEMIS CDFs are designed to comply with ISTP/IACG guidelines, which can be found at http://spdf.gsfc.nasa.gov/istp_guide/istp_guide.html. These guidelines specify certain required attributes, variables, naming conventions for variables, etc.  The compliance of a given CDF with ISTP guidelines can be checked with the ISTP Skeleton Editor: skteditor, available at  http://sscweb.gsfc.nasa.gov/skteditor/.

For each L2 data type a mastercdf file exists that gives all the attribute and variable information but does not include any data, e.g. tha_l2_esa_00000000_v01.cdf gives the attribute and variable information for the L2 data from the THEMIS Probe A Electrostatic Analyzer. As will be discussed later in the document, these master CDFs are used in the creation of the L2 CDFs. Mastercdfs can be edited by converting them to skeleton table format (using, for example the SPDF skeletontable tool), editing the resulting text file and converting back to CDF (using, for example the SPDF skeletonCDF tool). See section 4 below for an example of a skeleton table. Note that you can also use the ISTP Skeleton Editor to edit a CDF or a skeleton table, while checking ISTP compliance.

Note that it is recommended that users download the NASA IDL CDF patch available at (as of July 2011) http://cdf.gsfc.nasa.gov/html/cdf_patch_for_idl6x_new3.html.

More details on THEMIS CDFs can be found in thm_soc_124_L1_file_def.doc

# L1->L2 Processing

A detailed example of the L1->L2 processing can be found in thm_l2gen_demo.txt.

L2 files are generated automatically every day using a script create_probe_l2cdf.ksh. All L1 files created in the previous 36 hours are processed. In addition, if L1 state files have been created in the previous 36 hours, then the L2 files which use coordinate transformations (all but SST, FFT, and FBK) are processed, even if there is no new L1 data for those instruments.

To generate L2 files, the TDAS software is used to first load, and then calibrate the corresponding L1 (or L0) data. The resulting tplot variables are then written to a CDF with the help of a mastercdf file. In the resulting L2 CDF all metadata comes from the mastercdf, and is not inherited from the L1 data or calibration process.

L2 files are reprocessed whenever there are changes in calibration files. This is reasonably infrequent, with the exception of FGM where calibration files are updated every few months.

# L2 CDFs

By convention THEMIS time is measured as the number of unleaped seconds since 1-Jan-1970 00:00:00 GMT. The time variables that appear in L2 CDFs will be discussed briefly below. For more detail see the L1 File Definitions document and the THEMIS Science Time document. For discussion on THEMIS time conventions and leap seconds see the THEMIS Time Conventions document (thm_soc_135_time_conventions).

A data variable ‘varname’ has an associated time variable ‘varname_time’ e.g. tha_peif_time in table below, together with a variable of the type CDF_EPOCH, e.g. tha_peif_epoch0, that has a nonvarying value of 1-Jan-1970 00:00:00.000.  Variables are linked to a time variable and an epoch variable through the attributes DEPEND_TIME and DEPEND_EPOCH0. For example, for the variable tha_peif_data_quality, DEPEND_TIME has the value ‘tha_peif_time’ and DEPEND_EPOCH0 has the value ‘tha_peif_epoch0’. In addition, each THEMIS variable has a virtual variable of the type CDF_EPOCH/CDF_EPOCH16 with the name ‘varname_epoch’, e.g. tha_peif_epoch. This virtual variable is for use by CDAWeb, and is calculated using functions ‘comp_themis_epoch’ and ‘comp_themis_epoch16’ provided by SPDF.  The variable attribute DEPEND_0 points to the virtual epoch variable.

The final time variable encountered in the L2 CDFs is the range_epoch variable. This variable, of type CDF_EPOCH, contains the minimum and maximum times associated with any of the variables in the particular CDF.

Below is an example skeleton table – in this case an excerpt from the L2 skeleton table for ESA. The global attributes are listed first, followed by the variable attribute names. Finally, for each variable the attributes, attribute types, and attribute values are given.

| ! Skeleton table for the "tha_l2_esa_00000000_v01" CDF. ! Generated: Friday, 19-Aug-2011 15:11:57 ! CDF created/modified by CDF V3.1.1 ! Skeleton table created by CDF V3.3.0 #header CDF NAME: tha_l2_esa_00000000_v01 DATA ENCODING: NETWORK MAJORITY: ROW FORMAT: SINGLE |
| --- |
| ! Variables | G.Attributes | V.Attributes | Records | Dims | Sizes |
| ! --------- | ------------ | ------------ | ------- | ---- | ----- |
| 0/383 | 35 | 28 | 0/z | 0 |  |
| #GLOBALattributes |  |  |  |
| ! Attribute | Entry | Data |  |
| ! Name | Number | Type | Value |
| --------- | ------ | ---- | ----- |
| "Project" | 1: | CDF_CHAR | { "THEMIS" } . |
| "Source_name" | 1: | CDF_CHAR | { "THA>Themis Probe A" } . |
| "Discipline" | 1: | CDF_CHAR | { "Space " - "Physics>Magnetospheric " - "Science" } . |
| "Data_type" | 1: | CDF_CHAR | { "ESA" } . |
| "Descriptor" | 1: | CDF_CHAR | { "L2>L2 DATA" } . |
| "Data_version" | 1: | CDF_CHAR | { "1" } . |
| "PI_name" | 1: | CDF_CHAR | { "V. Angelopoulos, C.W. " - "Carlson & J. McFadden" } . |
| "PI_affiliation" | 1: | CDF_CHAR | { "UCB, NASA NAS5-02099" } . |
| "TITLE" | 1: | CDF_CHAR | { "Electrostatic Analyzer (ESA)" } . |
| "TEXT" | 1: | CDF_CHAR | { "THEMIS-A: Electrostatic " - "Analyzer (ESA): " - "Electron/Ion " - "Ground-Calculated Energy " - "Fluxes (ions: 5 eV to 25 " - "keV) electrons: 6 eV to 30" - " keV) and Moments " - "(density, velocity, " - "pressure, and " - "temperature). Includes " - "FULL, REDUCED and BURST " - "modes. FULL: high angular " - "resolution, low (few min) " - "time resolution. REDUCED: " - "degraded angular " - "resolution, high (approx. " - "3 sec) time resolution. " - "BURST: high angular " - "resolution, high time " - "resolution; only short " - "bursts of data. Note that " - "angular resolution affects" - " moments since they are " - "obtained integrating over " - "the mode-specific angular " - "distribution. Moment Data " - "Quality flags (0: good " - "data; non-zero flags are " - "totals of values; 1: " - "missing S/C potential, 2: " - "Counter saturation, 4: " - "Solar Wind not in Solar " - "Wind Mode, or Solar Wind " - "Mode, not in Solar Wind, " - "8: (Reduced Mode only) " - "slow survey mode+flows, " - "16: electron density Gt " - "2*ion density, 32: ion " - "density Gt 2*electron " - "density, 64: Spacecraft " - "Maneuver)." } . |
| "Instrument_type" | 1: | CDF_CHAR | { "Particles (space)" } |
|  | 2: | CDF_CHAR | { "Plasma and Solar Wind" } . |
| "Mission_group" | 1: | CDF_CHAR | { "THEMIS" } . |
| "Logical_source" | 1: | CDF_CHAR | { "tha_l2_esa" } . |
| "Logical_file_id" | 1: | CDF_CHAR | { "tha_l2_esa_00000000_v01" } . |
| "Logical_source_description" | 1: | CDF_CHAR | { "THEMIS-A: Electrostatic " - "Analyzer (ESA): " - "Electron/Ion " - "Ground-Calculated Energy " - "Fluxes (ions: 5 eV to 25 " - "keV) electrons: 6 eV to 30" - " keV) and Moments " - "(density, velocity, " - "pressure, and " - "temperature). Includes " – "FULL, REDUCED and BURST " - "modes. FULL: high angular " - "resolution, low (few min) " - "time resolution. REDUCED: " - "degraded angular " - "resolution, high (approx. " - "3 sec) time resolution. " - "BURST: high angular " - "resolution, high time " - "resolution; only short " – "bursts of data. Note that " – "angular resolution affects" - " moments since they are " – "obtained integrating over " - "the mode-specific angular " - "distribution." } . |
| "Time_resolution" | 1: | CDF_CHAR | { "???" } . |
| "Rules_of_use" | 1: | CDF_CHAR | { "Open Data for Scientific Use" } . |
| "Generated_by" | 1: | CDF_CHAR | { "THEMIS SOC" } . |
| "Generation_date" | 1: | CDF_CHAR | { "Thu Sep 4 15:07:27 2008" } . |
| "Acknowledgement" | 1: | CDF_CHAR | { "NASA Contract NAS5-02099" } . |
| "MODS" | 1: | CDF_CHAR | { "Rev- 2006-09-18" } . |
| "ADID_ref" | 1: | CDF_CHAR | { "NSSD0110" } . |
| "LINK_TEXT" | 1: | CDF_CHAR | { "THEMIS ESA " } |
|  | 2: | CDF_CHAR | { "Higher resolution data and" - " analysis s/w from " } |
|  | 3: | CDF_CHAR | { "Detailed description of the " } |
|  | 4: | CDF_CHAR | { "Detailed explanation of the " } . |
| "LINK_TITLE" | 1: | CDF_CHAR | { "Processing History" } |
|  | 2: | CDF_CHAR | { "THEMIS mission website" } |
|  | 3: | CDF_CHAR | { "ESA Instrument" } |
|  | 4: | CDF_CHAR | { "ESA L2 Data Quality Flags" } . |
| "HTTP_LINK" | 1: | CDF_CHAR | { "http://themis.ssl.berkeley" - ".edu/esa_proc_history.shtm" - "l" } |
|  | 2: | CDF_CHAR | { "http://themis.ssl.berkeley" - ".edu" } |
|  | 3: | CDF_CHAR | { "http://themis.ssl.berkeley" - ".edu/instrument_esa.shtml" } |
|  | 4: | CDF_CHAR | { "http://themis.ssl.berkeley" - ".edu/esa_flag.shtml" } . |
| "File_naming_convention" | 1: | CDF_CHAR | { "source_descriptor_datatype" } . |
| "Caveats" | 1: | CDF_CHAR | { "See THEMIS website for " - "caveats" } . |
| "Validity" | 1: | CDF_CHAR | { "to be validated" } . |
| "Validator" | 1: | CDF_CHAR | { "tbd" } . |
| "Validate" | 1: | CDF_CHAR | { "Compatible with the ISTP " - "CDF Standards" } . |
| "Inst_mod" | 1: | CDF_CHAR | { "THM>xxxx" } . |
| "Parents" | 1: | CDF_CHAR | { "xxxx" } . |
| "Inst_settings" | 1: | CDF_CHAR | { "Not used" } . |
| "Software_version" | 1: | CDF_CHAR | { "xxxx" } . |
| "Sc_pot_source" | 1: | CDF_CHAR | { "None" } . |
| #VARIABLEattributes |  |  |  |
| "DISPLAY_TYPE" "FILLVAL" "FORMAT" "UNITS" "DEPEND_TIME" "DEPEND_EPOCH0" "DEPEND_0" "VAR_TYPE" "PROPERTY" "SC_ID" "CATDESC" "FIELDNAM" "VALIDMIN" "VALIDMAX" "TENSOR_ORDER" "SI_CONVERSION" "LABLAXIS" "SCALETYP" "COORDINATE_SYSTEM" "DEPEND_1" "DICT_KEY" "REPRESENTATION_1" "VAR_NOTES" "LABL_PTR_1" "VIRTUAL" "FUNCT" "COMPONENT_0" "COMPONENT_1" |  |  |  |
| #variables |  |  |  |
| ! No rVariables. |  |  |  |
| #zVariables |  |  |  |
| ! Variable | Data | Number |  |  | Record | Dimension |
| ! Name | Type | Elements | Dims | Sizes | Variance | Variances |
| ! -------- | ---- | -------- | ---- | ----- | -------- | --------- |
| "tha_peif_data_quality" | CDF_INT4 | 1 | 0 |  | T |  |
| ! Attribute | Data |  |
| ! Name | Type | Value |
| ! -------- | ---- | ----- |
| "DISPLAY_TYPE" | CDF_CHAR | { "time_series" } |
| "FILLVAL" | CDF_INT4 | { -2147483648 } |
| "FORMAT" | CDF_CHAR | { "i2" } |
| "DEPEND_TIME" | CDF_CHAR | { "tha_peif_time" } |
| "DEPEND_EPOCH0" | CDF_CHAR | { "tha_peif_epoch0" } |
| "DEPEND_0" | CDF_CHAR | { "tha_peif_epoch" } |
| "VAR_TYPE" | CDF_CHAR | { "data" } |
| "PROPERTY" | CDF_CHAR | { "scalar" } |
| "SC_ID" | CDF_CHAR | { "a" } |
| "CATDESC" | CDF_CHAR | { "ESA Full Mode Ion Moment Data Quality " - "(0: Good data, non-zero: Data may not " - "be suitable, see: " - "http://themis.ssl.berkeley.edu/esa_fla" - "g.shtml.) " } |
| "FIELDNAM" | CDF_CHAR | { "Data_Quality_Flag_ion Full ESA-A" } |
| "VALIDMIN" | CDF_INT4 | { 0 } |
| "VALIDMAX" | CDF_INT4 | { 112 } |
| "TENSOR_ORDER" | CDF_INT4 | { 0 } |
| "LABLAXIS" | CDF_CHAR | { "Data_Quality_Flag_ion Full ESA-A" } |
| "SCALETYP" | CDF_CHAR | { "linear" } . |
| ! RV values were not requested. |
| ! Variable | Data | Number |  |  | Record | Dimension |
| ! Name | Type | Elements | Dims | Sizes | Variance | Variances |
| ! -------- | ---- | -------- | ---- | ----- | -------- | --------- |
| "tha_peif_densityQ" | CDF_DOUBLE | 1 | 0 |  | T |  |
| ! Attribute | Data |  |
| ! Name | Type | Value |
| ! -------- | ---- | ----- |
| "DISPLAY_TYPE" | CDF_CHAR | { "time_series" } |
| "FILLVAL" | CDF_DOUBLE | { nan.0 } |
| "FORMAT" | CDF_CHAR | { "E13.6" } |
| "UNITS" | CDF_CHAR | { "cm^-3" } |
| "DEPEND_TIME" | CDF_CHAR | { "tha_peif_time" } |
| "DEPEND_EPOCH0" | CDF_CHAR | { "tha_peif_epoch0" } |
| "DEPEND_0" | CDF_CHAR | { "tha_peif_epoch" } |
| "VAR_TYPE" | CDF_CHAR | { "data" } |
| "PROPERTY" | CDF_CHAR | { "scalar" } |
| "SC_ID" | CDF_CHAR | { "a" } |
| "CATDESC" | CDF_CHAR | { "(Good data only) ESA Full (High " – "Angular Resolution, few minute time " – "res.) Mode, Ion Density " } |
| "FIELDNAM" | CDF_CHAR | { "N_ion Full ESA-A" } |
| "VALIDMIN" | CDF_DOUBLE | { 0.0 } |
| "VALIDMAX" | CDF_DOUBLE | { 1.0e+10 } |
| "TENSOR_ORDER" | CDF_INT4 | { 0 } |
| "SI_CONVERSION" | CDF_CHAR | { "1.0e6>m^-3" } |
| "LABLAXIS" | CDF_CHAR | { "N_ion Full ESA-A" } |
| "SCALETYP" | CDF_CHAR | { "log" } |
| "VIRTUAL" | CDF_CHAR | { "TRUE" } |
| "FUNCT" | CDF_CHAR | { "apply_esa_qflag" } |
| "COMPONENT_0" | CDF_CHAR | { "tha_peif_density" } |
| "COMPONENT_1" | CDF_CHAR | { "tha_peif_data_quality" } . |
| ! RV values were not requested. |
| . |
| . (other variables here) |
| . |
| ! Variable | Data | Number |  |  | Record | Dimension |
| ! Name | Type | Elements | Dims | Sizes | Variance | Variances |
| ! -------- | ---- | -------- | ---- | ----- | -------- | --------- |
| "tha_peif_t3_labl" | CDF_CHAR | 20 | 1 | 3 | F | T |
| ! Attribute | Data |  |
| ! Name | Type | Value |
| ! -------- | ---- | ----- |
| "FORMAT" | CDF_CHAR | { "a20" } |
| "VAR_TYPE" | CDF_CHAR | { "metadata" } |
| "CATDESC" | CDF_CHAR | { "tha_peif_t3_labl" } |
| "FIELDNAM" | CDF_CHAR | { "tha_peif_t3_labl" } |
| "DICT_KEY" | CDF_CHAR | { "label" } . |
| ! NRV values follow... |
| [1] = { "Tprp1_ion Full ESA-A" } |
| [2] = { "Tprp2_ion Full ESA-A" } |
| [3] = { "Tpar_ion Full ESA-A " } |
| . |
| . (other variables here) |
| . |
| ! Variable | Data | Number |  |  | Record | Dimension |
| ! Name | Type | Elements | Dims | Sizes | Variance | Variances |
| ! -------- | ---- | -------- | ---- | ----- | -------- | --------- |
| "tha_peif_time" | CDF_DOUBLE | 1 | 0 |  | T |  |
| ! Attribute | Data |  |
| ! Name | Type | Value |
| ! -------- | ---- | ----- |
| "FILLVAL" | CDF_DOUBLE | { nan.0 } |
| "FORMAT" | CDF_CHAR | { "F12.8" } |
| "UNITS" | CDF_CHAR | { "sec" } |
| "VAR_TYPE" | CDF_CHAR | { "support_data" } |
| "CATDESC" | CDF_CHAR | { "tha_peif_time, UTC, in seconds since " – "01-Jan-1970 00:00:00; marks center " – "time of data sample" } |
| "FIELDNAM" | CDF_CHAR | { "tha_peif_time" } |
| "VALIDMIN" | CDF_DOUBLE | { 0.0 } |
| "VALIDMAX" | CDF_DOUBLE | { 5.0e+09 } |
| "LABLAXIS" | CDF_CHAR | { "UT" } |
| "VAR_NOTES" | CDF_CHAR | { "Unleaped seconds. Sample start and end" – " time can be calculated from " – "tha_peif_delta_time (sample duration)." } . |
| ! RV values were not requested. |
| . |
| . (other variables here) |
| . |
| ! Variable | Data | Number |  |  | Record | Dimension |
| ! Name | Type | Elements | Dims | Sizes | Variance | Variances |
| ! -------- | ---- | -------- | ---- | ----- | -------- | --------- |
| "tha_peif_epoch0" | CDF_EPOCH | 1 | 0 |  | F |  |
| ! Attribute | Data |  |
| ! Name | Type | Value |
| ! -------- | ---- | ----- |
| "FILLVAL" | CDF_DOUBLE | { -1.0e+31 } |
| "FORMAT" | CDF_CHAR | { "E13.6"} |
| "UNITS" | CDF_CHAR | { "msec"} |
| "VAR_TYPE" | CDF_CHAR | { "support_data" } |
| "CATDESC" | CDF_CHAR | { "EPOCH0 of THEMIS time base"} |
| "FIELDNAM" | CDF_CHAR | { "tha_peif_epoch0"} |
| "VALIDMIN" | CDF_DOUBLE | { 5.99582e+13 } |
| "VALIDMAX" | CDF_DOUBLE | { 6.63012e+13} |
| "LABLAXIS" | CDF_CHAR | { "timebase"} |
| "VAR_NOTES" | CDF_CHAR | { "EPOCH of 01-Jan-1970 00:00:00"} . |
| ! NRV values follow... |
| [] = 01-Jan-1970 00:00:00.000 |
| . |
| . (other variables here) |
| . |
| #end |

The skeleton table excerpt shown here gives examples of the entries for three types of variable, data, metadata, and support data (identifiable by the “VAR_TYPE” attribute). Note that the metadata variable "tha_peif_t3_labl" has Record Variance = F, indicating that the values do not vary between CDF records. The values of this variable are also listed in the skeleton table.

"tha_peif_densityQ" is an example of a virtual variable (“VIRTUAL” = “TRUE”). The attributes for the virtual variable include “FUNCT”, “COMPONENT_0”, and “COMPONENT_1”, which give the function and arguments used to calculate the values of the virtual variable.

Note that the variable names in the skeleton table above begin with ‘tha_’. It is the THEMIS convention that CDF variables begin ‘th?_’ where ‘?’ is one of a-2, representing probes A-E. In the sections below variable names are listed for Probe A (with the exception, of course, of the ground based GMAG).

Coordinate systems in the following are abbreviated. GSE: Geocentric Solar Ecliptic, GSM: Geocentric Solar Magnetospheric, DSL: Despun Spacecraft, SSL: Spinning Spacecraft (see THEMIS Science Coordinate Systems Definition document for more details).

Descriptions of variables here are (for the most part) taken directly out of the master cdfs.

## ESA (Electrostatic Analyzer)

During L2 processing a data quality variable is created that indicates which data may have problems (see table below for more details). ESA L2 CDFs also contain a number of virtual variables, denoted with a ‘Q’, used by NASA SPDF to screen out data that may have problems. The data quality flag is used to fill these ‘Q’ variables (the values for virtual variables do not appear within the CDF, but are instead calculated by some external code from non-virtual variables). Note that the TDAS software makes use of the data quality flag but does not use the ‘Q’ virtual variables.

ESA L2 variables

Here ‘?’ takes the values ‘i’ for ion or ‘e’ for electron

‘*’ takes the values ‘f’ for full (high angular resolution, low (few min) time resolution), ‘r’ for reduced (low angular resolution, high (approx 3 sec) time resolution), and ‘b’ for burst (high time and angular resolution) mode.

For example, there exist variables tha_peif_data_quality, tha_peef_data_quality, tha_peir_data_quality, tha_peer_data_quality, tha_peib_data_quality, and tha_peeb_data_quality.

| tha_pe?*_data_quality | ESA Full/Reduced/Burst Mode Ion/Electron Moment Data Quality (0: Good data, non-zero: Data may not be suitable, see: http://themis.ssl.berkeley.edu/esa_flag.shtml.) |
| --- | --- |
| tha_pe?*_densityQ | (Virtual) ESA Full/Reduced/Burst Mode, Ion/Electron Density, good data only. |
| tha_pe?*_avgtempQ | (Virtual) Average temperature |
| tha_pe?*_vthermalQ | (Virtual) Thermal velocity |
| tha_pe?*_sc_potQ | (Virtual) Spacecraft potential |
| tha_pe?*_en_efluxQ | (Virtual) Energy flux spectrogram |
| tha_pe?*_t3Q | (Virtual) Diagonalized temperature |
| tha_pe?*_magt3Q | (Virtual) Temperature, field aligned |
| tha_pe?*_ptensQ | (Virtual) Pressure tensor |
| tha_pe?*_mftensQ | (Virtual) Momentum flux tensor |
| tha_pe?*_fluxQ | (Virtual) Particle flux vector |
| tha_pe?*_symmQ | (Virtual) Symmetry Vector (direction of pressure tensor symmetry (DSL)) |
| tha_pe?*_symm_angQ | (Virtual) Symmetry Angle (between symmetry direction and B) |
| tha_pe?*_magfQ | (Virtual) Magnetic Field Vector in DSL |
| tha_pe?*_velocity_dslQ | (Virtual) Velocity vector in DSL |
| tha_pe?*_velocity_gseQ | (Virtual) Velocity vector in GSE |
| tha_pe?*_velocity_gsmQ | (Virtual) Velocity vector in GSM |
| tha_pe?*_modeQ | (Virtual) Survey mode, controls angle and energy binning, and time resolution, values 0 to 4 (peer, peib, peeb only?) |
| tha_pe?*_density | (All qualities data) ESA full/reduced/burst mode, ion/electron density |
| tha_pe?*_avgtemp | Average temperature |
| tha_pe?*_vthermal | Thermal velocity |
| tha_pe?*_sc_pot | Spacecraft potential |
| tha_pe?*_en_eflux | Energy flux spectrogram |
| tha_pe?*_en_eflux_yaxis |  |
| tha_pe?*_t3 | Diagonalized temperature Notes on diagonalized temperature:.The first eigenvalue and eigenvector are the distinguisheable eigenvalue and the major (symmetry) axis, respectively. The "degenerate" eigenvalues are sorted such that the 2nd eigenvalue is smaller than third one. |
| tha_pe?*_t3_labl | (Metadata) Label Value = {“Tprp1_^ * ESA-A”, “Tprp2_^ * ESA-A”, “Tpar_^ * ESA-A”}, ^ = ion, elec, * = Full, Rdcd, Brst |
| tha_pe?*_t3_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?*_magt3 | Temperature, field aligned 3d temperatures around magnetic axis (Z) and normal axes (X,Y), where Y is Z direction crossed into Sun direction and X completes orthogonal system. |
| tha_pe?*_magt3_labl | (Metadata) Label Value = {“Tprp1_^ FA * ESA-A”, “Tprp2_^ FA * ESA-A”, “Tpar_^ FA ^ ESA-A”}, ^ = ion, elec, * = Full, Rdcd, Brst |
| tha_pe?*_magt3_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?*_ptens | Pressure tensor |
| tha_pe?*_ptens_labl | (Metadata) Label Value = {“Pxx_^ * ESA-A”, “Pyy_^ * ESA-A”, “Pzz_^ * ESA-A”, “Pxy_^ * ESA-A”, “Pxz_^ * ESA-A”, “Pyz_^ ( ESA-A”}, ^ = ion, elec, * = Full, Rdcd, Brst |
| tha_pe?*_ptens_compno | (Metadata) Component number Value = {1,2,3,4,5,6} |
| tha_pe?*_mftens | Momentum flux tensor |
| tha_pe?*_mftens_labl | (Metadata) Label Value = {“MFxx_^ * ESA-A”, “MFyy_^ * ESA-A”, “MFzz_^ * ESA-A”, “MFxy_^ *ESA-A”, “MFxz_^ * ESA-A”, “MFyz_^ * ESA-A”}, ^ = ion, elec, * = Full, Rdcd, Brst |
| tha_pe?*_mftens_compno | (Metadata) Component number Value = {1,2,3,4,5,6} |
| tha_pe?*_flux | Particle flux vector |
| tha_pe?*_flux_labl | (Metadata) Label Value = {“Fx_^ DSL * ESA-A”, “Fy_^ DSL * ESA-A”, “Fz_^ DSL * ESA-A”}, ^ = ion, elec * = Full, Rdcd, Brst |
| tha_pe?*_flux_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?*_symm | Symmetry Vector (direction of pressure tensor symmetry (DSL)) This is the direction vector of the principal axis of the pressure tensor in DSL coordinates. |
| tha_pe?*_symm_labl | (Metadata) Label Value = {“Symm_x^ * ESA-A”, “Symm_y^ * ESA-A”, “Symm_z^ * ESA-A”}, ^ = e, i, * = Full, Rdcd, Brst |
| tha_pe?*_symm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_pe?*_symm_ang | Symmetry Angle (between symmetry direction and B) |
| tha_pe?*_magf | Magnetic Field Vector in DSL |
| tha_pe?*_magf_labl | (Metadata) Label Value = {“Bx_^ DSL * ESA-A”, “By_^ DSL * ESA-A”, “Bz_^ DSL *t ESA-A”}, ^ = elec, ion, * = Full, Rdcd, Brst |
| tha_pe?*_magf_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_pe?*_velocity_dsl | Velocity vector in DSL |
| tha_pe?*_velocity_dsl_labl | (Metadata) Label Value = {“Vx_^ DSL * ESA-A”, “Vy_^ DSL * ESA-A”, “Vz_^ DSL * ESA-A”}, ^ = elec, ion, * = Full, Rdcd, Brst |
| tha_pe?*_velocity_dsl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_pe?*_velocity_gse | Velocity vector in GSE |
| tha_pe?*_velocity_gse_labl | (Metadata) Label Value = {“Vx_^ GSE * ESA-A”, “Vy_^ GSE * ESA-A”, “Vz_^ GSE * ESA-A”}, ^ = elec, ion, * = Full, Rdcd, Brst |
| tha_pe?*_velocity_gse_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_pe?*_velocity_gsm | Velocity vector in GSM |
| tha_pe?*_velocity_gsm_labl | (Metadata) Label Value = {“Vx_^ GSM * ESA-A”, “Vy_^ GSM * ESA-A”, “Vz_^ GSM * ESA-A”}, ^ = elec, ion, * = Full, Rdcd, Brst |
| tha_pe?*_velocity_gsm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_pe?*_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_pe?*_delta_time | Duration in seconds of sample |
| tha_pe?*_mode | Survey mode, controls angle and energy binning, and time resolution, values of 0 to 8 (ion) or 4 (electron) |
| tha_pe?*_mode_labl | (Metadata) Label Value = {“cfg1_^ * ESA-A”, “cfg2_^ * ESA-A”, “mode_^ * ESA-A}, ^ = elec, ion, * = Full, Rdcd, Brst |
| tha_pe?*_mode_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_pe?*_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_pe?*_epoch | (Virtual) |
| Rep_xyz_gse | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_dsl | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_gsm | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_nfa | (Metadata) Label representation (NFA: Nominally Field Aligned) Value = {“xx”, “yy”, “zz”} |
| sc_pot_source | Source of the potential field used to obtain particle moments. If None, then the potential was set to 0. Else the potential was calculated using EFI data. Value = None |
| tha_?esa_solarwind_flag | ESA electron/ion solar wind mode flag; 0: Not in Solar Wind mode, 1: in Solar Wind mode |
| tha_?esa_solarwind_flag_time | Unleaped seconds |
| tha_?esa_solarwind_flag_epoch | (Virtual) |
| tha_?esa_solarwind_flag_epoch0 | 01-Jan-1970 00:00:00.000 |
| range_epoch |  |

## SST (Solid State Telescope)

SST L2 variables

Here ‘?’ takes the values ‘i’ for ion or ‘e’ for electron.

| tha_ps?f_en_eflux | SST Ion/Electron energy spectrogram |
| --- | --- |
| tha_ps?f_en_eflux_yaxis |  |
| tha_ps?f_en_eflux_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_ps?f_en_eflux_delta_time | Duration in seconds of sample. |
| tha_ps?f_en_eflux_mode | SST survey mode |
| tha_ps?f_en_eflux_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_ps?f_en_eflux_epoch | (Virtual) |
| tha_?esa_solarwind_flag | ESA electron/ion solar wind mode flag; 0: Not in Solar Wind mode, 1: in Solar Wind mode |
| tha_?esa_solarwind_flag_time | Unleaped seconds |
| tha_?esa_solarwind_flag_epoch | (Virtual) |
| tha_?esa_solarwind_flag_epoch0 | 01-Jan-1970 00:00:00.000 |
| range_epoch |  |

## MOM (On board Moments)

Onboard moments are calculated from ESA and SST data. As with the ESA L2 cdfs, there is a data quality flag that indicates whether there are potential problems with the data. This data quality flag is used by NASA SPDF to fill the virtual ‘Q’ variables.

MOM L2 variables

Here ‘?’ takes the values ‘i’ for ion or ‘e’ for electron.

| tha_pe?m_data_quality | Ion/Electron Moment Data Quality (0: good data, nonzero: data may not be suitable. See http://themis.ssl.berkeley.edu/mom_flag.shtml) |
| --- | --- |
| tha_pe?m_densityQ | (Virtual) ESA On Board Moment Ion/Electron Density (good data only) |
| tha_pe?m_ptotQ | (Virtual) Ion/Electron total pressure |
| tha_pe?m_fluxQ | (Virtual) Ion/Electron particle flux vector |
| tha_pe?m_mftensQ | (Virtual) Ion/Electron momentum flux tensor |
| tha_pe?m_efluxQ | (Virtual) Ion/Electron energy flux vector |
| tha_pe?m_velocity_dslQ | (Virtual) Ion/Electron velocity vector in DSL |
| tha_pe?m_velocity_gseQ | (Virtual) Ion/Electron velocity vector in GSE |
| tha_pe?m_velocity_gsmQ | (Virtual) Ion/Electron velocity vector in GSM |
| tha_pe?m_ptensQ | (Virtual) Ion/Electron pressure tensor |
| tha_pe?m_magQ | (Virtual) Magnetic field vector (DSL) |
| tha_pe?m_velocity_magQ | (Virtual) Ion/Electron velocity vector, field aligned |
| tha_pe?m_t3_magQ | (Virtual) Ion/Electron temperature, field aligned |
| tha_pe?m_ptens_magQ | (Virtual) Ion/Electron pressure tensor, field aligned |
| tha_pe?m_density | ESA On Board Moment Ion/Electron Density |
| tha_pe?m_ptot | Ion/Electron total pressure |
| tha_pe?m_flux | Ion/Electron particle flux vector |
| tha_pe?m_flux_labl | (Metadata) Label Value = {“Fx_* MOM ESA-A”, “Fy_* MOM ESA-A”, “Fz_* MOM ESA-A”}, * = ion, elec |
| tha_pe?m_flux_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_mftens | Ion/Electron momentum flux tensor |
| tha_pe?m_mftens_labl | (Metadata) Label Value = {“Mfxx_* MOM ESA-A”, “Mfyy_* MOM ESA-A”, “Mfzz_* MOM ESA-A”, “Mfxy_* MOM ESA-A”, “Mfxz_* MOM ESA-A”, “Mfyz_* MOM ESA-A” }, * = ion, elec |
| tha_pe?m_mftens_compno | (Metadata) Component number Value = {1,2,3,4,5,6} |
| tha_pe?m_eflux | Ion/Electron energy flux vector |
| tha_pe?m_eflux_labl | (Metadata) Label Value = {“Efx_* MOM ESA-A”, “Efy_* MOM ESA-A”, “Efz_* MOM ESA-A”}, * = ion, elec |
| tha_pe?m_eflux_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_velocity_dsl | Ion/Electron velocity vector in DSL |
| tha_pe?m_velocity_dsl_labl | (Metadata) Label Value = {“ Vx_* DSL MOM ESA-A”, “Vy_* DSL MOM ESA-A”, “Vz_* DSL MOM ESA-A”}, * = ion, elec |
| tha_pe?m_velocity_dsl_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_velocity_gse | Ion/Electron velocity vector in GSE |
| tha_pe?m_velocity_gse_labl | (Metadata) Label Value = {“Vx_* GSE MOM ESA-A”, “Vy_* GSE MOM ESA-A”, “Vz_* GSE MOM ESA-A”}, * = ion, elec |
| tha_pe?m_velocity_gse_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_velocity_gsm | Ion/Electron velocity vector in GSM |
| tha_pe?m_velocity_gsm_labl | (Metadata) Label Value = {“Vx_* GSM MOM ESA-A”, “Vy_* GSM MOM ESA-A”, “Vz_* GSM MOM ESA-A”}, * = ion, elec |
| tha_pe?m_velocity_gsm_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_ptens | Ion/Electron pressure tensor |
| tha_pe?m_ptens_labl | (Metadata) Label Value = {“Pxx_* MOM ESA-A” , “Pyy_* MOM ESA-A”, “Pzz_* MOM ESA-A”, “Pxy_* MOM ESA-A”, “Pxz_* MOM ESA-A”, “Pyz_* MOM ESA-A”}, * = ion, elec |
| tha_pe?m_ptens_compno | (Metadata) Component number Value = {1,2,3,4,5,6} |
| tha_pe?m_mag | Magnetic field vector (DSL) |
| tha_pe?m_mag_labl | (Metadata) Label Value = { “Bx_* DSL MOM ESA-A”, “By_* DSL MOM ESA-A”, “Bz_* DSL MOM ESA-A”}, * = ion, elec |
| tha_pe?m_mag_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_velocity_mag | Ion/Electron velocity vector, field aligned |
| tha_pe?m_velocity_mag_labl | (Metadata) Label Value = {“Vx_* FA MOM ESA-A”, “Vy_* FA MOM ESA-A”, “Vz_* FA MOM ESA-A”}, * = ion, elec |
| tha_pe?m_velocity_mag_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_t3_mag | Ion/Electron temperature, field aligned 3d temperatures around magnetic axis (Z) and normal axes (X,Y), where Y is Z direction crossed into Sun direction, and X completes orthogonal system." |
| tha_pe?m_t3_mag_labl | (Metadata) Label Value = {“Tx_* FA MOM ESA-A”, “Ty_* FA MOM ESA-A”, “Tz_* FA MOM ESA-A”}, * = ion, elec |
| tha_pe?m_t3_mag_compno | (Metadata) Component number Value = {1,2,3} |
| tha_pe?m_ptens_mag | Ion/Electron pressure tensor, field aligned Pressure tensor around magnetic axis (Z) and normal axes (X,Y), where Y is direction crossed into Sun direction, and X completes orthogonal system. |
| tha_pe?m_ptens_mag_labl | (Metadata) Label Value = {“Pxx_* FA MOM ESA-A”, “Pyy_* FA MOM ESA-A”, “Pzz_* FA MOM ESA-A”, “Pxy_* FA MOM ESA-A”, “Pxz_* FA MOM ESA-A”, “Pyz_* FA MOM ESA-A”}, * = ion, elec |
| tha_pe?m_ptens_mag_compno | (Metadata) Component number Value = {1,2,3,4,5,6} |
| tha_pe?m_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_pe?m_epoch0 | 01-Jan-1970 00:00:00 |
| tha_pe?m_epoch | (Virtual) |
| tha_pxxm_pot | Spacecraft potential |
| tha_pxxm_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_pxxm_epoch0 | 01-Jan-1970 00:00:00 |
| tha_pxxm_epoch | (Virtual) |
| Rep_xyz_dsl | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_gse | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_gsm | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_nfa | (Metadata) Label representation Value = {“xx”, “yy”, “zz”} |
| tha_?esa_solarwind_flag | ESA electron/ion solar wind mode flag; 0: Not in Solar Wind mode, 1: in Solar Wind mode |
| tha_?esa_solarwind_flag_time | Unleaped seconds |
| tha_?esa_solarwind_flag_epoch | (Virtual) |
| tha_?esa_solarwind_flag_epoch0 | 01-Jan-1970 00:00:00 |
| range_epoch |  |

## EFI (Electric Field Instrument)

| tha_efs_dot0_epoch | (Virtual) |
| --- | --- |
| tha_efs_dot0_gse | EFS_DOT0 (spin-fit, using E dot B=0) electric field vector in GSE coordinates |
| tha_efs_dot0_gse_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_dot0_gse_labl | (Metadata) Label Value = {“Ex GSE EFS_dot0-A”, “Ey GSE EFS_dot0-A”, Ez GSE EFS_dot0-A”} |
| tha_efs_dot0_gsm | EFS_DOT0 (spin-fit, using E dot B=0) electric field vector in GSM coordinates |
| tha_efs_dot0_gsm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_dot0_gsm_labl | (Metadata) Label Value = {“Ex GSM EFS_dot0-A”, “Ey GSM EFS_dot0-A”, Ez GSM EFS_dot0-A”} |
| tha_efs_dot0_dsl | EFS_DOT0 (spin-fit, using E dot B=0) electric field vector in XYZ despun spacecraft coordinates (DSL) |
| tha_efs_dot0_dsl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_dot0_dsl_labl | (Metadata) Label Value = {“Ex DSL EFS_dot0-A”, “Ey DSL EFS_dot0-A”, Ez DSL EFS_dot0-A”} |
| tha_efs_dot0_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_efs_q_mag | EFS_Q_MAG (Data Quality Parameter: set to NaN for EFS, as there is no good measure of data quality.) |
| tha_efs_q_mag_time | UTC in seconds since 01-Jan_1970 00:00:00 |
| tha_efs_q_mag_epoch | (Virtual) |
| tha_efs_q_pha | EFS_Q_PHA (Data Quality Parameter: Set to NaN, as there is no good way to measure data quality for EFS data.) |
| tha_efs_q_pha_time | UTC in seconds since 01-Jan_1970 00:00:00 |
| tha_efs_q_pha_epoch | (Virtual) |
| tha_efs_dot0_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_eff_dot0_gse | EFF_DOT0 (fast-survey, 1/8 sec time resolution, using E dot B=0) electric field vector in GSE coordinates |
| tha_eff_dot0_gse_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_eff_dot0_gse_labl | (Metadata) Label Value = {“Ex GSE EFF_dot0-A”, “Ey GSE EFF_dot0-A”, Ez GSE EFF_dot0-A”} |
| tha_eff_dot0_gsm | EFF_DOT0 (fast-survey, 1/8 sec time resolution, using E dot B=0) electric field vector in GSM coordinates |
| tha_eff_dot0_gsm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_eff_dot0_gsm_labl | (Metadata) Label Value = {“Ex GSM EFF_dot0-A”, “Ey GSE EFF_dot0-A”, Ez GSM EFF_dot0-A”} |
| tha_eff_dot0_dsl | EFF_DOT0 (fast-survey, 1/8 sec time resolution, , using E dot B=0) electric field vector in XYZ despun spacecraft coordinates (DSL) |
| tha_eff_dot0_dsl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_eff_dot0_dsl_labl | (Metadata) Label Value = {“Ex DSL EFF_dot0-A”, “Ey DSL EFF_dot0-A”, Ez DSL EFF_dot0-A”} |
| tha_eff_dot0_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_eff_q_mag | EFF_Q_MAG (Data Quality Parameter: equal to the spin-fit E34 electric field magnitude divided by the spin-fit E12 electric field magnitude. Good values are near 1.0) |
| tha_eff_q_mag_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_eff_q_mag_epoch | (Virtual) |
| tha_eff_q_pha | EFF_Q_PHA (Data Quality Parameter: equal to the cosine of the angle between the spin-fit E34 electric field and the spin-fit E12 electric field. Good values are near 1.0) |
| tha_eff_q_pha_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_eff_q_pha_epoch | (Virtual) |
| tha_eff_e12_efs_epoch | (Virtual) |
| tha_eff_e12_efs | E12_EFS, Ground Spin-fit (using E12), spin plane electric field vector in XYZ despun spacecraft coordinates (DSL) |
| tha_eff_e12_efs_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_eff_e12_efs_labl | (Metadata) Label Value = {“Ex DSL EFF_E12_EFS-A”, “Ey DSL EFF_E12_EFS-A”, Ez DSL EFF_E12_EFS-A”} |
| tha_eff_e12_efs_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_eff_e34_efs_epoch | (Virtual) |
| tha_eff_e34_efs | E34_EFS, Ground Spin-fit (using E34), spin plane electric field vector in XYZ despun spacecraft coordinates (DSL) |
| tha_eff_e34_efs_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_eff_e34_efs_labl | (Metadata) Label Value = {“Ex DSL EFF_E34_EFS-A”, “Ey DSL EFF_E34_EFS-A”, Ez DSL EFF_E34_EFS-A”} |
| tha_eff_e34_efs_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_eff_dot0_epoch0 | 01-Jan-1970 00:00:00.000 |
| Rep_xyz_dsl | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_gse | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_gsm | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| range_epoch |  |

## FBK (Filter Bank Data)

| tha_fb_hff | High Frequency Filter peak and average values hf_peak and hf_avg are the peak and average values of the output of the High-Frequency Filter, a broadband filter covering the 100- to 400-kHz band used for AKR detection. |
| --- | --- |
| tha_fb_hff_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_hff_epoch | (Virtual) |
| tha_fb_hff_labl | (Metadata) Label Value = {“FBK-A HF Filter Peak Voltage”, “FBK-A HF Filter Average Voltage”} |
| tha_fb_hff_compno | (Metadata) Component number Value = {1, 2} |
| tha_fb_v1 | Spectrogram FBK Potential, Sensor 1 |
| tha_fb_v1_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_v1_epoch | (Virtual) |
| tha_fb_v2 | Spectrogram FBK Potential, Sensor 2 |
| tha_fb_v2_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_v2_epoch | (Virtual) |
| tha_fb_v3 | Spectrogram FBK Potential, Sensor 3 |
| tha_fb_v3_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_v3_epoch | (Virtual) |
| tha_fb_v4 | Spectrogram FBK Potential, Sensor 4 |
| tha_fb_v4_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_v4_epoch | (Virtual) |
| tha_fb_v5 | Spectrogram FBK Potential, Sensor 5 |
| tha_fb_v5_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_v5_epoch | (Virtual) |
| tha_fb_v6 | Spectrogram FBK Potential, Sensor 6 |
| tha_fb_v6_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_v6_epoch | (Virtual) |
| tha_fb_edc12 | Spectrogram FBK E Field DC Component, Sensors 1&2 (spin plane) |
| tha_fb_edc12_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_edc12_epoch | (Virtual) |
| tha_fb_edc34 | Spectrogram FBK E Field DC Component, Sensors 3&4 (spin plane) |
| tha_fb_edc34_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_edc34_epoch | (Virtual) |
| tha_fb_edc56 | Spectrogram FBK E Field DC Component, Sensors 5&6 (axial) |
| tha_fb_edc56_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_edc56_epoch | (Virtual) |
| tha_fb_scm1 | Spectrogram FBK Search Coil Magnetometer (SCM) Axis 1 |
| tha_fb_scm1_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_scm1_epoch | (Virtual) |
| tha_fb_scm2 | Spectrogram FBK Search Coil Magnetometer (SCM) Axis 2 |
| tha_fb_scm2_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_scm2_epoch | (Virtual) |
| tha_fb_scm3 | Spectrogram FBK Search Coil Magnetometer (SCM) Axis 3 |
| tha_fb_scm3_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_scm3_epoch | (Virtual) |
| tha_fb_eac12 | Spectrogram FBK E Field AC Component, Sensors 1&2 (spin plane) |
| tha_fb_eac12_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_eac12_epoch | (Virtual) |
| tha_fb_eac34 | Spectrogram FBK E Field AC Component, Sensors 3&4 (spin plane) |
| tha_fb_eac34_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_eac34_epoch | (Virtual) |
| tha_fb_eac56 | Spectrogram FBK E Field AC Component, Sensors 5&6 (axial) |
| tha_fb_eac56_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fb_eac56_epoch | (Virtual) |
| tha_fb_yaxis | Value = {2.689e+03, 5.720e+02, 1.442e+02, 3.620e+01, 9.050e+00, 2.260e+00} |
| tha_fbk_labl | (Metadata) Label Value = {“2-kHz”, “512-Hz”, “128-Hz”, “32-Hz”, “8-Hz”, “2-Hz”} |
| tha_fbk_fcenter | center frequency (geometric mean) Value = {2.689e+03, 5.720e+02, 1.442e+02, 3.620e+01, 9.050e+00, 2.260e+00} |
| tha_fbk_fband | frequency bandwidths Value = {4.604e+03, 5.880e+02, 1.472e+02, 3.690e+01, 9.220e+00, 2.310e+00} |
| tha_fbk_freqno | (Metadata) Frequency Number Value = {1, 2, 3, 4, 5, 6} |
| tha_fbk_epoch0 | 01-Jan-1970 00:00:00.000 |
| range_epoch |  |

## FFT (On Board Fast Fourier Transform)

On Board Fast Fourier Transform (FFT) power spectra of Electric (EFI) and Magnetic (SCM) field, for particle and wave burst survey modes.

Here ‘?’ can take the value ‘f’ for Fast Survey, ‘p’ for Particle Burst, ‘w’ for Wave Burst.

| tha_ff?_16_dbpara | FFT Power Spectrum, 16 frequencies for SCM delta-B (parallel to B) |
| --- | --- |
| tha_ff?_16_dbperp | FFT Power Spectrum, 16 frequencies for SCM delta-B (perpendicular to B) |
| tha_ff?_16_eac12 | FFT Power Spectrum, 16 frequencies for E Field AC Component, Sensors 1&2 (spin plane) |
| tha_ff?_16_eac34 | FFT Power Spectrum, 16 frequencies for E Field AC Component, Sensors 3&4 (spin plane) |
| tha_ff?_16_eac56 | FFT Power Spectrum, 16 frequencies for E Field AC Component, Sensors 5&6 (axial) |
| tha_ff?_16_edc12 | FFT Power Spectrum, 16 frequencies for E Field DC Component, Sensors 1&2 (spin plane) |
| tha_ff?_16_edc34 | FFT Power Spectrum, 16 frequencies for E Field DC Component, Sensors 3&4 (spin plane) |
| tha_ff?_16_edc56 | FFT Power Spectrum, 16 frequencies for E Field DC Component, Sensors 5&6 (axial) |
| tha_ff?_16_epara | FFT Power Spectrum, 16 frequencies for EFI E (parallel to B) |
| tha_ff?_16_eperp | FFT Power Spectrum, 16 frequencies for EFI E (perp to B) |
| tha_ff?_16_scm1 | FFT Power Spectrum, 16 frequencies for SCM, Axis 1 |
| tha_ff?_16_scm2 | FFT Power Spectrum, 16 frequencies for SCM, Axis 2 |
| tha_ff?_16_scm3 | FFT Power Spectrum, 16 frequencies for SCM, Axis 3 |
| tha_ff?_16_v1 | FFT Power Spectrum , 16 frequencies for EFI Potential, Sensor 1 |
| tha_ff?_16_v2 | FFT Power Spectrum , 16 frequencies for EFI Potential, Sensor 2 |
| tha_ff?_16_v3 | FFT Power Spectrum , 16 frequencies for EFI Potential, Sensor 3 |
| tha_ff?_16_v4 | FFT Power Spectrum , 16 frequencies for EFI Potential, Sensor 4 |
| tha_ff?_16_v5 | FFT Power Spectrum , 16 frequencies for EFI Potential, Sensor 5 |
| tha_ff?_16_v6 | FFT Power Spectrum , 16 frequencies for EFI Potential, Sensor 6 |
| tha_ff?_16_yaxis | no values |
| tha_ff?_16_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_ff?_16_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_ff?_16_epoch | (Virtual) |
| tha_ff?_32_dbpara | FFT Power Spectrum, 32 frequencies for SCM delta-B (parallel to B) |
| tha_ff?_32_dbperp | FFT Power Spectrum, 32 frequencies for SCM delta-B (perpendicular to B) |
| tha_ff?_32_eac12 | FFT Power Spectrum, 32 frequencies for E Field AC Component, Sensors 1&2 (spin plane) |
| tha_ff?_32_eac34 | FFT Power Spectrum, 32 frequencies for E Field AC Component, Sensors 3&4 (spin plane) |
| tha_ff?_32_eac56 | FFT Power Spectrum, 32 frequencies for E Field AC Component, Sensors 5&6 (axial) |
| tha_ff?_32_edc12 | FFT Power Spectrum, 32 frequencies for E Field DC Component, Sensors 1&2 (spin plane) |
| tha_ff?_32_edc34 | FFT Power Spectrum, 32 frequencies for E Field DC Component, Sensors 3&4 (spin plane) |
| tha_ff?_32_edc56 | FFT Power Spectrum, 32 frequencies for E Field DC Component, Sensors 5&6 (axial) |
| tha_ff?_32_epara | FFT Power Spectrum, 32 frequencies for EFI E (parallel to B) |
| tha_ff?_32_eperp | FFT Power Spectrum, 32 frequencies for EFI E (perp to B) |
| tha_ff?_32_scm1 | FFT Power Spectrum, 32 frequencies for SCM, Axis 1 |
| tha_ff?_32_scm2 | FFT Power Spectrum, 32 frequencies for SCM, Axis 2 |
| tha_ff?_32_scm3 | FFT Power Spectrum, 32 frequencies for SCM, Axis 3 |
| tha_ff?_32_v1 | FFT Power Spectrum , 32 frequencies for EFI Potential, Sensor 1 |
| tha_ff?_32_v2 | FFT Power Spectrum , 32 frequencies for EFI Potential, Sensor 2 |
| tha_ff?_32_v3 | FFT Power Spectrum , 32 frequencies for EFI Potential, Sensor 3 |
| tha_ff?_32_v4 | FFT Power Spectrum , 32 frequencies for EFI Potential, Sensor 4 |
| tha_ff?_32_v5 | FFT Power Spectrum , 32 frequencies for EFI Potential, Sensor 5 |
| tha_ff?_32_v6 | FFT Power Spectrum , 32 frequencies for EFI Potential, Sensor 6 |
| tha_ff?_32_yaxis | no values |
| tha_ff?_32_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_ff?_32_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_ff?_32_epoch | (Virtual) |
| tha_ff?_64_dbpara | FFT Power Spectrum, 64 frequencies for SCM delta-B (parallel to B) |
| tha_ff?_64_dbperp | FFT Power Spectrum, 64 frequencies for SCM delta-B (perpendicular to B) |
| tha_ff?_64_eac12 | FFT Power Spectrum, 64 frequencies for E Field AC Component, Sensors 1&2 (spin plane) |
| tha_ff?_64_eac34 | FFT Power Spectrum, 64 frequencies for E Field AC Component, Sensors 3&4 (spin plane) |
| tha_ff?_64_eac56 | FFT Power Spectrum, 64 frequencies for E Field AC Component, Sensors 5&6 (axial) |
| tha_ff?_64_edc12 | FFT Power Spectrum, 64 frequencies for E Field DC Component, Sensors 1&2 (spin plane) |
| tha_ff?_64_edc34 | FFT Power Spectrum, 64 frequencies for E Field DC Component, Sensors 3&4 (spin plane) |
| tha_ff?_64_edc56 | FFT Power Spectrum, 64 frequencies for E Field DC Component, Sensors 5&6 (axial) |
| tha_ff?_64_epara | FFT Power Spectrum, 64 frequencies for EFI E (parallel to B) |
| tha_ff?_64_eperp | FFT Power Spectrum, 64 frequencies for EFI E (perp to B) |
| tha_ff?_64_scm1 | FFT Power Spectrum, 64 frequencies for SCM, Axis 1 |
| tha_ff?_64_scm2 | FFT Power Spectrum, 64 frequencies for SCM, Axis 2 |
| tha_ff?_64_scm3 | FFT Power Spectrum, 64 frequencies for SCM, Axis 3 |
| tha_ff?_64_v1 | FFT Power Spectrum , 64 frequencies for EFI Potential, Sensor 1 |
| tha_ff?_64_v2 | FFT Power Spectrum , 64 frequencies for EFI Potential, Sensor 2 |
| tha_ff?_64_v3 | FFT Power Spectrum , 64 frequencies for EFI Potential, Sensor 3 |
| tha_ff?_64_v4 | FFT Power Spectrum , 64 frequencies for EFI Potential, Sensor 4 |
| tha_ff?_64_v5 | FFT Power Spectrum , 64 frequencies for EFI Potential, Sensor 5 |
| tha_ff?_64_v6 | FFT Power Spectrum , 64 frequencies for EFI Potential, Sensor 6 |
| tha_ff?_64_yaxis | no values |
| tha_ff?_64_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_ff?_64_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_ff?_64_epoch | (Virtual) |
| range_epoch |  |

## FGM (Fluxgate Magnetometer)

| tha_fgs_btotal | Spin resolution (FGS) magnetic field magnitude |
| --- | --- |
| tha_fgs_gse | FGS (spin-resolution/~3 sec) magnetic field in GSE coordinates |
| tha_fgs_gsm | FGS magnetic field in GSM coordinates |
| tha_fgs_dsl | FGS magnetic field in DSL coordinates |
| tha_fgs_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_fgs_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fgs_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_fgs_epoch | (Virtual) |
| tha_fgs_labl | (Metadata) Label Value = {“Bx FGS-A”, “By FGS-A”, “Bz FGS-A”} |
| tha_fgl_btotal | Low time resolution/~0.25sec (FGL) magnetic field magnitude |
| tha_fgl_gse | FGL magnetic field in GSE coordinates |
| tha_fgl_gsm | FGL magnetic field in GSM coordinates |
| tha_fgl_dsl | FGL magnetic field in DSL coordinates |
| tha_fgl_ssl | FGL magnetic field in SSL coordinates |
| tha_fgl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_fgl_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fgl_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_fgl_epoch16 | (Virtual) |
| tha_fgl_labl | (Metadata) Label Value = {“Bx FGL-A”, “By FGL-A”, “Bz FGL-A”} |
| tha_fgh_btotal | High time resolution/~0.008 sec (FGH) magnetic field magnitude |
| tha_fgh_gse | FGH magnetic field in GSE coordinates |
| tha_fgh_gsm | FGH magnetic field in GSM coordinates |
| tha_fgh_dsl | FGH magnetic field in DSL coordinates |
| tha_fgh_ssl | FGH magnetic field in SSL coordinates |
| tha_fgh_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_fgh_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fgh_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_fgh_epoch16 | (Virtual) |
| tha_fgh_labl | (Metadata) Label Value = {“Bx FGH-A”, “By FGH-A”, “Bz FGH-A”} |
| tha_fge_btotal | Engineering mode (FGE) magnetic field magnitude |
| tha_fge_gse | FGE magnetic field in GSE coordinates |
| tha_fge_gsm | FGE magnetic field in GSM coordinates |
| tha_fge_dsl | FGE magnetic field in DSL coordinates |
| tha_fge_ssl | FGE magnetic field in SSL coordinates |
| tha_fge_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_fge_labl | (Metadata) Label Value = {“Bx FGE-A”, “By FGE-A”, “Bz FGE-A”} |
| tha_fge_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fge_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_fge_epoch16 | (Virtual) |
| Rep_xyz | (Metadata) Representation for xyz vector/tensor dimension Value = {“x”, “y”, “z”} |
| range_epoch |  |

## FIT (On Board Spin-Fit Electric and Magnetic Field Data)

| tha_fgs_sigma | Standard deviation of the onboard magnetic field spin-fit (FGS) |
| --- | --- |
| tha_fgs_dsl | FGS magnetic field vector in DSL coordinates |
| tha_fgs_dsl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_fgs_dsl_labl | (Metadata) Label Value = {“Bx DSL FGS-A”, “By DSL FGS-A”, “Bz DSL FGS-A”} |
| tha_fgs_gse | FGS magnetic field vector in GSE coordinates |
| tha_fgs_gse_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_fgs_gse_labl | (Metadata) Label Value = {“Bx GSE FGS-A”, “By GSE FGS-A”, “Bz GSE FGS-A”} |
| tha_fgs_gsm | FGS magnetic field vector in GSM coordinates |
| tha_fgs_gsm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_fgs_gsm_labl | (Metadata) Label Value = {“Bx GSM FGS-A”, “By GSM FGS-A”, “Bz GSM FGS-A”} |
| tha_fgs_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fgs_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_fgs_epoch | (Virtual) |
| tha_efs_sigma | Standard deviation of the onboard electric field spin-fit (EFS) |
| tha_efs_dsl | EFS electric field vector in DSL coordinates |
| tha_efs_dsl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_dsl_labl | (Metadata) Label Value = {“Bx DSL EFS-A”, “By DSL EFS-A”, “Bz DSL EFS-A”} |
| tha_efs_0_dsl | EFS_0 (spin-fit, using E_z=0) electric field in DSL coordinates |
| tha_efs_0_dsl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_0_dsl_labl | (Metadata) Label Value = {“Ex DSL EFS_0-A”, “Ey DSL EFS_0-A”, “Ez DSL EFS_0-A”} |
| tha_efs_dot0_dsl | EFS_DOT0 (spin-fit, using E dot B = 0) electric field vector in DSL coordinates |
| tha_efs_dot0_dsl_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_dot0_dsl_labl | (Metadata) Label Value = {“Ex DSL EFS_dot0-A”, “Ey DSL EFS_dot0-A”, “Ez DSL EFS_d0t0-A”} |
| tha_efs_gse | EFS electric field vector in GSE coordinates |
| tha_efs_gse_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_gse_labl | (Metadata) Label Value = {“Ex GSE EFS-A”, “Ey GSE EFS-A”, “Ez GSE EFS-A”} |
| tha_efs_0_gse | EFS_0 (spin-fit, using E_z=0) electric field in GSE coordinates |
| tha_efs_0_gse_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_0_gse_labl | (Metadata) Label Value = {“Ex GSE EFS_0-A”, “Ey GSE EFS_0-A”, “Ez GSE EFS_0-A”} |
| tha_efs_dot0_gse | EFS_DOT0 (spin-fit, using E dot B = 0) electric field vector in GSE coordinates |
| tha_efs_dot0_gse_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_dot0_gse_labl | (Metadata) Label Value = {“Ex GSE EFS_dot0-A”, “Ey GSE EFS_dot0-A”, “Ez GSE EFS_dot0-A”} |
| tha_efs_gsm | EFS electric field vector in GSM coordinates |
| tha_efs_gsm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_gsm_labl | (Metadata) Label Value = {“Ex GSM EFS-A”, “Ey GSM EFS-A”, “Ez GSM EFS-A”} |
| tha_efs_0_gsm | EFS_0 (spin-fit, using E_z=0) electric field in GSM coordinates |
| tha_efs_0_gsm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_0_gsm_labl | (Metadata) Label Value = {“Ex GSM EFS_0-A”, “Ey GSM EFS_0-A”, “Ez GSM EFS_0-A”} |
| tha_efs_dot0_gsm | EFS_DOT0 (spin-fit, using E dot B = 0) electric field vector in GSM coordinates |
| tha_efs_dot0_gsm_compno | (Metadata) Component number Value = {1, 2, 3} |
| tha_efs_dot0_gsm_labl | (Metadata) Label Value = {“Ex GSM EFS_dot0-A”, “Ey GSM EFS_dot0-A”, “Ez GSM EFS_dot0-A”} |
| tha_efs_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_efs_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_efs_epoch | (Virtual) |
| tha_fit_bfit | FIT_BFIT spin-fit calibrated model data A, B, C, sigma, avg. (DSL) |
| tha_fit_bfit_compno | (Metadata) Component number Value = {1, 2, 3, 4, 5} |
| tha_fit_bfit_labl | (Metadata) Label Value = {“A FIT_BFIT FGM-A”, “B FIT_BFIT FGM-A”, “C FIT_BFIT FGM-A”, “Sigma FIT_BFIT FGM-A”, “Avg. FIT_BFIT FGM-A”} |
| tha_fit_bfit_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fit_bfit_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_fit_bfit_epoch | (Virtual) |
| tha_fit_efit | FIT_EFIT spin-fit calibrated model data A, B, C, sigma, avg. (DSL) |
| tha_fit_efit_compno | (Metadata) Component number Value = {1, 2, 3,4 ,5} |
| tha_fit_efit_labl | (Metadata) Label Value = {“A FIT_EFIT FGM-A”, “B FIT_EFIT FGM-A”, “ C FIT_EFIT FGM-A”, “Sigma FIT_EFIT FGM-A”, “Avg. FIT_EFIT FGM-A”} |
| tha_fit_efit_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_fit_efit_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_fit_efit_epoch | (Virtual) |
| Rep_xyz_dsl | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_gse | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| Rep_xyz_gsm | (Metadata) Label representation Value = {“x”, “y”, “z”} |
| range_epoch |  |

## GMAG (Ground Magnetometer)

For additional information on the L2 GMAG CDFs see the Ground Magnetometer L2 Data Files Variable Name Definition document.

Data from external sites (that is not THEMIS GBO or EPO) are processed to conform to the same file definitions.

The L2 GMAG CDFs contain the following variables (here ???? represents the four (or three) letter code for the GMAG site):

| thg_mag_???? | Magnetic field B in HDZ vector components |
| --- | --- |
| thg_mag_????_unit | (Metadata) Magnetic field units Value = {“nT”, “nT”, “nT”} |
| thg_mag_????_labl | (Metadata) Label Value = {“Magnetic North, local”, “Magnetic East, local”, “Vertical Down, local”} |
| thg_mag_????_compno | (Metadata) HDZ component number Value = {1, 2, 3} |
| thg_mag_????_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| thg_mag_????_epoch | (Virtual) |
| thg_mag_????_epoch0 | 01-Jan-1970 00:00:00.000 |
| range_epoch |  |

## SCM (Search Coil Magnetometer)

| tha_scf_epoch | (Virtual) |
| --- | --- |
| tha_scf_btotal | Search Coil Fast-survey, 1/8 sec time resolution, magnetic field B magnitude |
| tha_scf_gse | SCF magnetic field in XYZ GSE coordinates |
| tha_scf_gsm | SCF magnetic field in XYZ GSM Coordinates |
| tha_scf_dsl | SCF magnetic field in XYZ DSL Coordinates |
| tha_scf_compno | (Metadata) XYZ component number Value = {1, 2, 3} |
| tha_scf_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_scf_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_scf_labl | (Metadata) Label Value = {“Bx SCF-A”, “By SCF-A”, “Bz SCF-A”} |
| tha_scp_epoch16 | (Virtual) Search Coil Particle-burst epoch variable |
| tha_scp_btotal | SCP (Particle burst, 1/128 sec time resolution) magnetic field magnitude |
| tha_scp_gse | SCP magnetic field in XYZ GSE coordinates |
| tha_scp_gsm | SCP magnetic field in XYZ GSM Coordinates |
| tha_scp_dsl | SCP magnetic field in XYZ DSL Coordinates |
| tha_scp_compno | (Metadata) XYZ component number Value = {1, 2, 3} |
| tha_scp_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_scp_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_scp_labl | (Metadata) Label Value = {“Bx SCP-A”, “By SCP-A”, “Bz SCP-A”} |
| tha_scw_epoch16 | (Virtual) Search Coil Wave-burst epoch variable |
| tha_scw_btotal | SCW (Wave burst, 1/8192 sec time resolution) magnetic field magnitude |
| tha_scw_gse | SCW magnetic field in XYZ GSE coordinates |
| tha_scw_gsm | SCW magnetic field in XYZ GSM Coordinates |
| tha_scw_dsl | SCW magnetic field in XYZ DSL Coordinates |
| tha_scw_compno | (Metadata) XYZ component number Value = {1, 2, 3} |
| tha_scw_time | UTC in seconds since 01-Jan-1970 00:00:00 |
| tha_scw_epoch0 | 01-Jan-1970 00:00:00.000 |
| tha_scw_labl | (Metadata) Label Value = {“Bx SCW-A”, “By SCW-A”, “Bz SCW-A”} |
| Rep_xyz | (Metadata) Representation for xyz vector/tensor dimension Value = {“x”, “y”, “z”} |
| range_epoch |  |