## Slide 1
QUESTION 4A: Six previous missions are cited as FSW heritage. Identify the software baseline against which the reuse percentages in Table F-12 were calculated.
Answer:The CSR page 56 Table F-12 that contained the reuse percentages by module has been upgraded to more clearly identify the software baseline used as shown in the Question/Answer Appendix
Starting with the SAMPEX mission, the flight software for successive missions (FAST, SWAS, TRACE and WIRE) was utilized as the basis for continued mission support. Functions were enhanced and improved for each successive mission as the same basic functionality is required for successive missions. The same is true for THEMIS
Due to the similarity in both the C&DH and simple ACS functions of the FAST spacecraft, we intend on utilizing the FAST flight software as well as the most recent SMEX mission (WIRE) to baseline the THEMIS flight software system
For attitude control support, the math functions used for the EO-1 flight software were selected. Utilizing the math components and the design architecture for failure detection and correction from the EO-1 mission also supports our approach of using existing/tested flight software components to develop the THEMIS flight software.