## Slide 1
Question # 8: Why do you have confidence that the reliability approach will meet the mission life requirement? Present your assumptions and initial conditions for the analysis. What is the single-probe reliability, and how does it correlate to the overall mission reliability?
Answer:
Since either P3 or P4 can replace any other Probe, should a block failure occur, mission resilience results with a variety of paths to achieve science objectives
  Constellation architecture is analogous to an on-orbit “satellite in storage” eliminating single point failures within the mission architecture
Probes also have graceful performance degradation if individual elements fail
  I.e dual axial and tangential thrusters, gyro’s and magnetometer (backup the sun sensor), N+1 redundancy in memory blocks, solar array string or battery cell failure reduce capacity
  Individual instrument failure is decoupled from operation of the rest of that probe’s instruments representing a minor loss of mission science data collection capability
Our reliability analyses and FMEA’s characterize our system design providing insight into key operational functions
Our Mission Success Confidence results from our time-tested design practices, selection of heritage components, in-process statistical production feedback, qualified manufacturing processes, and a rigorous and comprehensive component, subsystem, and system level test program

## Slide 2
Question # 8, Cont’d:
Main Mission Mode reliability analysis used extensive industry & prior Swales (EO-1) component databases convolved into board/element configurations for each function to derive MTBF’s & associated reliabilities for both two year (design life) and one year (minimum life) timeframes
“k of n” approach (binomial series expansion) used to calculate Mission Reliability of the Constellation
Resulting individual Probe reliability and Constellation reliability are appropriate for a MIDEX