## Slide 1
Question # 6:
GSFC Spec 311-INST-1A [CSR, Page 100] applies only to instruments, and calls for Grade 3 parts only for non-essential instruments with lifetimes less than one year. Please explain your decision to use Grade 3 parts (with some up-screens to Grade 2) for key parts in critical subsystems for the entire spacecraft.
Answer:
  GSFC-410-MIDEX-003 Rev A section 5.2 states that “In general all parts should be selected and processed in accordance with GSFC 311-INST-001 for Grade 3 quality level”. The THEMIS EEE parts program has established as a minimum Grade 3 quality level for both instruments and probe EEE parts.
  Satellite probes critical components such as the BAU, Miniature Spinning Sun Sensor and Transponder have established a Grade 2 or better parts program.
  For inexpensive/short lead parts such as diodes, resistors, capacitors, small transistors etc. we have specified Grade 1 parts.
  The IDPU will institute, in general, a Grade 2 or better parts program.
  The instruments will institute Grade 3 or better upgrades will be considered if the schedule and cost impacts are within the baseline program.