## Slide 1: SI: Themis Boom Systems mission design supplement
Detailed Appendage Deployment Process
Spin to 10 RPM (15 max), to release Mag Booms (10 to 8.6 RPM momentum despin)
Spin to 30 RPM to prepare for Wire Boom Deployment, then release door caging
  Deploy AB pair to 5m radius, then CD pair to 5m (30 to 11 RPM momentum despin)
  Deploy AB pair to 10m, then CD pair to 10m (11 to 3.5 RPM despin)
  Spin to 26 RPM to unfurl all Sphere Reels
  Deploy AB pair to 12m, then CD pair to 12m (26 to 18 RPM despin)
  Spin to 24 RPM, deploy AB pair to 14m, then CD pair to 14m (24 to 17 RPM despin)
  Spin to 22 RPM, deploy AB pair to 16m, then CD pair to 16m (22 to 17 RPM despin)
  Spin to 20 RPM, deploy AB pair to 18m, then CD pair to 18m (20 to 16 RPM despin)
  Spin to 20 RPM, deploy AB pair to 20m, then CD pair to 20m (20 to 16 RPM despin)
  NOTES: All sequences may be interrupted by ‘Safe Hold’ without risk to a probe
    IDPU controlled deploy logic stops longer boom if difference is > 0.1m
    Deployment can be verified by spin changes, spin flutter & nutation frequencies
Release Axial booms (as pair or individually)
  Trim final operational spin rate to 20 RPM