## Slide 1
QUESTION 5: The Master Equipment List shows several components (e.g., gyros, thermostats, valves, transducers, RCS heaters) at zero power required. How are these accounted for in the power analysis?
Answer: The Master Equipment List has average power dissipations for the nominal science mode as the probes spend the vast majority of their lifetimes operating in that mode. The components in question all dissipate 0 watts during science operations except for the RCS heaters that were accounted for under the thermal subsystem as shown in the QA appendix
Power analysis accounted for thruster operations but that level of detail was omitted from the CSR due to page limitations
  Thruster operations power analysis is based on mature power numbers and includes the following; probe bus, all instruments on, one pair of cat bed heaters on for 30 minutes, one pair of thrusters on 100% duty cycle, transmitter on 100%, EOL solar array performance, and worst case sun angles
  Longest planned burn time of 60 minutes yields a 21% battery DOD
  Limiting battery DOD to 50% yields a maximum burn time of approximately 2.5 hours, far beyond that needed to satisfy our maneuver profile
  Additional power margin can be achieved by powering down the instruments as we don’t acquire valid science data during thruster operations