## Slide 1
Question # 2: Present the maneuver operations plan for both the large delta-v maneuvers and the side thrusting maneuvers including hardware configurations, commanding, and dynamic stability concerns?
Answer:
For all deployment and failure modes, Probes have positive passive spin-stability margin resulting in no concerns for dynamic stability (also see answers to Questions # 1, 3, and 9 for additional detailed backup information)
Side and axial thrusting have convergent wire boom damping and do not excite unfavorable oscillations
  Demonstrated on POLAR for fully deployed satellite with precession to burn attitude and back
All maneuvers use a stored time command firing sequence of a subset of the four thrusters (generated by the GMAN ops. Tool)
  All maneuvers occur while Probe is in ground contact; Perigee maneuvers monitored via TDRSS two-way link (also see answer to Question # 12)
  Complete maneuver sequence table for P1 injection phase (largest number of individual maneuvers) is shown for completeness and in the Appendix handout
All maneuvers follow a common procedure (illustrated in the following flowchart) planned for a typical single maneuver event

## Slide 2
Question # 2, Cont’d:

## Slide 3
Question # 2, Cont’d:
Flight Operations Functions
Maneuver Operations (Typical) Sequence
Ground Operations Functions
“Look Ahead” Orbit Propagation Indicates Upcoming Maintenance Maneuver is Desired
Current/Desired Orbit/Attitude used in GMAN
Specific Maneuver Events, Attitudes, and Durations Formulated
Discrete Thruster Profile and Pulse Sequence Formed
Discrete Stored Command Sequence Generated via MPS
Upload TLM Table, Firing Sequence, & Downlink Rate Selection
Offline Validation of Entire Stored Command Sequence Performed on Probe Hi-Fidelity Test-bed
Power-up Gyro’s, Catalyst Bed Heaters (Pre-Heat)
Downlink On-Board CMD Buffer
Compare Flight to Ground Reference Image to Verify Proper Sequence Load
Verify CMD & TLM link via GN, TDRSS, USN, or DSN
Verify Current Attitude via Sun Sensor Data
Verify Gyro Performance, Catalyst Bed Heater Functionality, Propellant Tank Pressure, Valve/Fuel Line Temperatures & States, and Pre-Maneuver Attitude
Power-off Catalyst Bed Heaters
Execute Burn Sequence
Periodic Long-Term Calibration of Pulse Timing and Thruster Performance
Monitor Key Temperatures, Attitude, and State Vector
On-Board Failure Detection/Correction (FDC) Logic (gyro rates, sun-sensor attitude limits, etc) Aborts Sequence if Anomaly is Detected
Power Down Gyros
Verify Tank Pressure, General Probe Health & Safety, 2-Way Ranging
Turn Off Transmitter
Determine New Orbit and New Attitude