## Slide 1: THEMIS Operations
Manfred Bester
Mission Operations Manager
Space Experience: 15 years
Projects: STS-55, FAST, IMAGE, RHESSI, CHIPSAT, ST-5, MMS
Disciplines: Analog and Digital Electronics, RF and Microwave Engineering, Cryogenic Systems, Physical Optics, Real-time Control Systems, Astrodynamics Software Development, Satellite Orbit Analysis, Satellite Communications, Ground Station and Ground Data System Design and Integration, Spacecraft Design and Integration, Mission Operations, Scientific Data Analysis, Project Management
RHESSI
IMAGE
FAST
BGS

## Slide 2: Overview
Mission Operations Concept
Mission Orbits
Data Storage Requirements
Ground Systems
Mission Profile
L&EO & Maneuver Operations
Normal & Contingency Operations
Science Operations
Network Plan & IT Security
Staffing, Costs and Schedule
Risk Mitigation
Summary
Backup Charts

## Slide 3: Mission Operations Concept
Space Segment
  5 Spinning Probes in High Earth Orbits
  Simultaneous Release from LV
  Initial Orbits Close to Final Mission Orbits of Probes 3,4,5
  Probes 1 and 2 Move to Their Final Mission Orbits After Check-out
  Store and Forward Strategy for Science Data Recovery
  All Probes Share Same Frequency − Contact One Probe at a Time
Ground Stations
  Berkeley Ground Station as Prime Facility
  Universal Space Network as Secondary
  TDRSS (SSA), Wallops GN and DSN for Ascent, Maneuver and Contingency Support
Operations Centers
  Mission and Science Operations Centers Co-located at U.C. Berkeley

## Slide 4: THEMIS Mission Orbits
PCA | 12.103 x 1. 100 Re at 9.0°
Orbits at L + 46 5 Re / div
Probe | Orbital Period | Orbit at L + 46 | Orbit at WD – 24
1 | 4 d | 30.943 x 1.500 Re at 23.0° | 31.645 x 1.500 Re at 7.0°
2 | 2 d | 19.756 x 1.168 Re at 15.0° | 19.770 x 1.168 Re at 7.0°
3 | 1 d | 12.127 x 1.118 Re at 9.0° | 12.127 x 1.118 Re at 9.0°
4 | 1 d | 12.103 x 1.118 Re at 9.0° | 12.103 x 1.118 Re at 9.0°
5 | 1 d | 12.250 x 1.118 Re at 4.0° | 12.250 x 1.118 Re at 4.0°

## Slide 5: Answer to Q7: Data Storage
Question # 7: Please specify the worst-case data storage requirement for each probe. Clarify the average data volume of 750 Mbits − Is it per day or per orbit? If per day: (a) Is the data storage sufficient to store 4 days of data plus a missed contact for Probe 1; and (b) How are overlaps in coverage of the probes handled at the ground station?
Answer:
Each probe accumulates 750 Mbits of science and engineering data per orbit. The science instruments are turned on only near apogee, where the conjunctions occur.
Lossless data compression by a factor of 2.0 is applied onboard, meaning that 375 Mbits of data have to be stored for each orbit.
The onboard memory has a capacity of 256 Mbytes, allowing data storage for > 5 orbits.
When data are transmitted to the ground, an overhead of 12% for CCSDS frame formatting and 14% for Reed-Solomon code symbols is applied. This amounts to a telemetry volume of approximately 480 Mbits per orbit per Probe, or 1.44 − 2.4 Gbits per day for all 5 Probes.
Nominal downlink time is 20 min at a data rate of 400 kbps at ranges < 20,000 km. Available downlink time at BGS and USN−AU has 60−100% margin for each ground station, allowing resolution of scheduling conflicts and playback of data from lost passes (see Appendix).

## Slide 6: Overview of Missions Supported
Mission | FAST | RHESSI | THEMIS
Launch | 21 Aug 1996 * | 05 Feb 2002 | Aug 2006
Duration | 3 Years | 3 Years | 2 Years
Orbit | 350 x 3,900 km, 83° | 580 x 607 km, 38° | HEO, Low Inclination
BGS Passes | 1 / Week ** | 6 / Day | 5 / Day ***
Support Type | TLM / CMD | TLM / CMD | TLM / CMD
Max Data Rate | 2,250 kbps | 4,000 kbps | 400 kbps
Data Volume | 20 Gbits / Day | 11 Gbits / Day | 1.44 − 2.4 Gbits / Day ****
* FAST mission operations transferred from GSFC to UCB in Oct. 1999.
** FAST science and engineering data recovered at Poker Flat, Wallops Island and McMurdo Base with typically 11 passes / day. BGS is back-up ground station.
*** Each THEMIS probe contacted at least once per day for SOH monitoring and Doppler tracking.
**** See Answer to Question # 7: Data Storage Requirement for Each Probe

## Slide 7: THEMIS Operations Org Chart
All Aspects of THEMIS Operations Are Performed at UCB / SSL
NASA / GSFC GNCD Provides Support in Form of Consulting
Software Tools: GTDS, GMAN, MSASS, SatTrack, ITOS, MPS, SERS
Implement Data Base to Track Probe Configuration, Status & Anomalies

## Slide 8: UCB Mission Operations Center
BGS Antenna, Equipment Racks and FOT Workstations at the UCB Mission Operations Center

## Slide 9: Berkeley Ground Station
Technical Highlights
Antenna
Model 300 Pedestal (L-3 Com, EMP Systems)
11-m Parabolic Reflector with Prime Focus Feed
Three Axis Drive System:
Azimuth / Elevation / Cross-Elevation
Autotracking with Conical Scan System
RF Systems
S-Band Telemetry and Command Capabilities
Receive Polarization Diversity
Figure of Merit (G/T) > 24.5 dB/K at 5 º Elevation
Current Transmit Power 100 W, EIRP > 63 dBW
Upgrade to 200 W, EIRP > 66 dBW
Install and Certify Apogee Labs Carrier Doppler Measurement System
Data Processing
Dual CCSDS Frontend Processors
Telemetry Data Routing by Virtual Channel IDs
Command Forwarding

## Slide 10: THEMIS Mission Profile

## Slide 11: L&EO Operations
Launch & Early Orbit Operations
  End-to-End Data Flow Tests Including All Ground Stations and TDRSS
  Extensive Rehearsals and Detailed Mission Simulations
  Delta II Launch Sequence with Release of Probes
  Round Robin State-of-Health Monitoring
  Attitude and Orbit Determination
  Uplink of First Set of Command Loads to Each Probe
  Deployment of Magnetometer Booms
  Systematic Instrument Power-up and Check-out
  Decision of Probe Placement
  Spin Up to 30 r.p.m. with Calibration of Tangential Thrusters as Byproduct
  Discrete Pairs of Apogee and Perigee Maneuvers for Placement into Final Mission Orbits (Reorientation – Continuous Burn – Reorientation Sequence)
  Maneuvers Performed While in Contact with Ground Stations and/or TDRSS

## Slide 12: Answer to Q2: Maneuver Operations
Question # 2: Present the maneuver operations plan for both the large delta-v maneuvers and the side thrusting maneuvers including hardware configurations, commanding and dynamic stability concerns.
Answer:
For all deployment and failure modes, Probes have positive passive spin-stability margin resulting in no concerns for dynamic stability (also see Answers to Questions # 1, 3, and 9 for additional detailed backup information).
Side and axial thrusting have convergent wire boom damping and do not excite unfavorable oscillations.
  Demonstrated on POLAR for fully deployed satellite with precession to burn attitude and back
All maneuvers use a stored time command firing sequence of a subset of the four thrusters, generated by the GMAN maneuver planning tool.
  All maneuvers occur while Probe is in ground contact. Perigee maneuvers are monitored via a TDRSS two-way link (also see Answer to Question # 12).
  Complete maneuver sequence table for the P1 injection phase with the largest number of individual maneuvers) is shown for completeness and in the Appendix handout.
All maneuvers follow a common procedure, as is illustrated in the following flowchart for a typical single maneuver event.

## Slide 13: Answer to Q2 (Continued)
Flight Operations Functions
Maneuver Operations (Typical) Sequence
Ground Operations Functions
“Look Ahead” Orbit Propagation Indicates Upcoming Maintenance Maneuver is Desired
Current/Desired Orbit/Attitude used in GMAN
Specific Maneuver Events, Attitudes, and Durations Formulated
Discrete Thruster Profile and Pulse Sequence Formed
Discrete Stored Command Sequence Generated via MPS
Upload TLM Table, Firing Sequence, & Downlink Rate Selection
Offline Validation of Entire Stored Command Sequence Performed on Probe Hi-Fidelity Test-bed
Power-up Gyro’s, Catalyst Bed Heaters (Pre-Heat)
Downlink On-Board CMD Buffer
Compare Flight to Ground Reference Image to Verify Proper Sequence Load
Verify CMD & TLM link via GN, TDRSS, USN, or DSN
Verify Current Attitude via Sun Sensor Data
Verify Gyro Performance, Catalyst Bed Heater Functionality, Propellant Tank Pressure, Valve/Fuel Line Temperatures & States, and Pre-Maneuver Attitude
Power-off Catalyst Bed Heaters
Execute Burn Sequence
Periodic Long-Term Calibration of Pulse Timing and Thruster Performance
Monitor Key Temperatures, Attitude, and State Vector
On-Board Failure Detection/Correction (FDC) Logic (gyro rates, sun-sensor attitude limits, etc) Aborts Sequence if Anomaly is Detected
Power Down Gyros
Verify Tank Pressure, General Probe Health & Safety, 2-Way Ranging
Turn Off Transmitter
Determine New Orbit and New Attitude

## Slide 14: Maneuver Summary
THEMIS Maneuver Summary |  |  | 
Probe | Maneuver ID | Purpose of Maneuver | Maneuvers
1 | P1-1 − P1-4 P1-5 − P1-11 P1-12 | Initial Mission Orbit Insertion Fine Tuning for Optimization of Conjunction Science De-orbit | 7 7 1
2 | P2-1 − P2-4 P2-5 − P2-11 P2-12 | Initial Mission Orbit Insertion Fine Tuning for Optimization of Conjunction Science De-orbit | 6 7 1
3 | P3-1 − P3-2 P3-3 P3-4 − P3-5 | Initial Mission Orbit Insertion Fine Tuning for Optimization of Conjunction Science De-orbit | 2 1 2
4 | P4-1 − P4-2 P4-3 P4-4 − P4-5 | Initial Mission Orbit Insertion Fine Tuning for Optimization of Conjunction Science De-orbit | 2 1 2
5 | P5-1 P5-2 − P5-6 P5-7 − P5-8 | Initial Mission Orbit Insertion Fine Tuning for Optimization of Conjunction Science De-orbit | 1 5 2
Total |  |  | 47

## Slide 15: Answer to Q12: TDRSS and DSN
Question # 12: Describe the use of TDRSS during early mission operations and quantify the dependency that THEMIS has on the TDRSS and DSN-Madrid networks. Have you confirmed that these resources are available?
Answer:
TDRSS H / I / J support is required during launch and ascent to orbit.
TDRSS contacts provide initial SOH checks as soon as fairing opens, and allow monitoring Probe release from the PCA.
TDRSS support is also required to ensure continuous two-way communications during maneuvers near perigee.
TDRSS support requirements are rather basic:
  Standard S-Band Single Access (SSA) forward and return service.
  THEMIS uses a TDRSS compatible transponder that has FUSE and EO-1 heritage.
  Telemetry uplink / downlink via TDRSS at 1 kbps.
  No tracking requirements − Doppler tracking performed at ground stations.
Flexibility with scheduling TDRSS support for perigee maneuvers − Probes are in stable orbits.
TDRSS H / I / J anticipated to be operational in 2006 − 2008.
THEMIS team is in contact with CSOC representative to draft a PSLA.

## Slide 16: Answer to Q12 (Continued)
DSN Madrid support is optional and for contingencies only.
CSOC has a new contract in place with Hartebeesthoek, providing an alternate GN option that is easier to implement from the THEMIS project’s point of view and less costly than DSN. Berkeley FOT already interacts with White Sands Scheduling on a routine basis for FAST, RHESSI and CHIPSAT projects.
TDRSS Support Summary |  | 
PCA | Probe Monitoring During Ascent Phase | 6.0 h
Probe 1 | 4 Apogee Raise Maneuvers Performed Near Perigee @ 1.25 h Each | 5.0 h
Probe 2 | 3 Apogee Raise Maneuvers Performed Near Perigee @ 1.0 h Each | 3.0 h
Probe 3 | 1 Apogee Trim Performed Near Perigee @ 1.0 h Each | 1.0 h
Probe 4 | 1 Apogee Trim Performed Near Perigee @ 1.0 h Each | 1.0 h
Probe 5 | 4 Period Change Maneuvers Performed Near Perigee @ 0.7 – 1.7 h Each | 5.0 h
Total Support | Entire Mission Duration | 21.0 h

## Slide 17: Normal Operations
Mission Planning During Normal Operations
  Preparation of the Conjunction Season
  Ground Station Contact Schedules
Probe Command and Control
  Probe Health and Safety Monitoring
  Recovery of Science and Engineering Data
  Command Load Uplink Twice Per Week
  Instrument Configuration and Data Trending
Attitude & Orbit Determination
  Routinely Performed Multiple Times per Week
Maneuver Planning and Execution
  Orbits of Probes 1,2,5 Adjusted Few Times Per Year to Optimize Conjunctions
  Orbits of Probes 1 & 2 Adjusted Annually to Counteract Lunar Perturbations

## Slide 18: Pass Scheduling
Required Pass Coverage for Science Data Recovery
  Telemetry Data Volume 480 Mbits / Orbit / Probe (1.44 − 2.4 Gbits / Day Total)
  Requires One 20 min Pass / Orbit / Probe at Data Rate 400 kbps
  BGS as Primary Ground Station with 1030 Passes / Year
  USN−AU (Universal Space Network, Perth) as Secondary with 340 Passes / Year
  Additional BGS Doppler Tracking Passes Scheduled for Orbit Determination
  Contingency Passes Available (60 − 100 % Margin at Each BGS and USN−AU)
Autonomous Pass Scheduling
  Based on Prediction of Dynamic Link Margin Rather Than Pure Line-of-Sight
  Employed Very Successfully with RHESSI Mission
  Ground Station Self-tests Inserted Automatically into Gaps in Tracking Schedule
  Autonomous Scheduling Functions Currently Developed for ST-5 Mission
  Scheme Optimizes Utilization of Ground Assets, Maximizes Downlink Time, Minimizes Data Loss and Cost

## Slide 19: Typical Pass Schedule

## Slide 20: Contingency Operations
Contingency Operations
  Assessment of Plausible Failure Modes Performed During Mission Design Phase
  Results Taken into Account in Probe Design
  Fault Tree Software Tool Will Allow FOT to Perform Quick Data Base Search
  Consultation with Bus and Instrument Engineering Support Team
  Corrective Actions Carefully Planned and Subsequently Executed
  Green Cards Used in Mission and Launch Simulations
Safe Mode
  Probes Are Spin Stabilized Normal to the Ecliptic Plane
  Power Positive in 4π sr
  Communications at Low Rate (TLM 5 kbps, CMD 1 kbps) Out to Farthest Apogee

## Slide 21: Science Operations
Data Processing Pipeline for Probe Data
  Archive Raw Telemetry Data with Annotation Header (Level 0)
  Split Level 0 Data into Individual Files for Each Instrument (24 h) (Level 1)
  Convert Level 1 Instrument Data to Physical Units (Level 2)
  Archive Level 0-2 Products on CD-ROMs, Distribute to CO-Is and NSSDC
  Local Archive at SSL on Linux Based RAID System (Same as RHESSI)
Science Data Analysis
  Merge Probe Data with ASI and GMAG Data Received from Canada
  Data Validated by Scientist Responsible for Daily Checks
  Identification and Tabulation of Geophysical Events
  Adapt Science Data Tool (SDT) Developed at SSL for Analysis of FAST, WIND, CLUSTER & POLAR Data

## Slide 22: Network Plan & IT Security
NASA Network Security Requirements Driven by NPG 2810.1,
“Security of Information Technology”
  GSFC IT Security Outlined in Document 290-004, “IONet Access Protection Policy and Requirements”
  Establishes IT Network Systems Security Measures and Controls for Access to Critical NASA Resources
Documentation Requirements
  IONet Security Plan, Risk Analysis and Contingency Plan
Closed IONet Security Compliance
  Dedicated, Isolated Network and Workstations for TDRSS Access
  Configuration Control by System Administrator
  Network Certification and Scanning
  Personnel Screening

## Slide 23: MOC Staffing
MOC Staffing During Launch & Early Orbit Operations
  UCB Flight Operations Team
  24 Hour Staffing with Prime and Secondary Shifts
  Critical Commanding During Prime Shift Only
  Swales and UCB Engineering Team on Console During Prime Shift
  Instrument Scientists During Instrument Commissioning
MOC Staffing During Normal Operations
  THEMIS Follows FAST / RHESSI / CHIPSAT Model
  Normal Operations Run with 8 x 5 Staffing
  Lights-out Operations During Off-hours Successfully Demonstrated
  Transition to Autonomous Operations After L+ 71 Days
  Attitude & Orbit Maneuvers Always Treated as Special Operations

## Slide 24: UCB Operations Team
Operations Team Functions
  Flight Operations
  Flight Dynamics
  Mission Planning
  Pass Scheduling
  Ground Station Operations
  Science Data Processing
Strong Team Heritage
  EUVE
  POLAR, IMAGE
  FAST, RHESSI, CHIPSAT
  TDRSS Communications

## Slide 25: Costs and Schedule
Operations Costs
  Cost Effective Approach Based on Successful FAST / RHESSI Model
  Mission Operations, Ground Station and Flight Dynamics Integrated Into One Coherent Facility
  Phase-in Operations Team Gradually
  Required Trade Study Will Be Performed in Phase B
Operations Schedule
  THEMIS MOC Configuration During Phase C / D
  Development of Detailed Operations Plans and Procedures
  Flight Dynamics Software Configuration and Verification with GNCD Support
  FOT Training in Classroom and During Mission I&T
  End-to-end Data Flow Testing with USN, TDRSS, Wallops GN and DSN
  Peak Activities In Phase D, Taper Down During Phase E

## Slide 26: Risk Mitigation
Provide Operational Redundancy
  Dual Strings in Equipment Where Practical, Back-up Power
  Multiple Workstations for Telemetry and Command Support
Conduct Interface Tests at Various Stages
  RF and Data Compatibility and End-to-end Data Flow Tests
Begin Operations Team Training Early in the Program
  Participation as Test Conductors During I&T
  Extensive Probe Simulator and Classroom Training
  Flight Dynamics Training and Certification by NASA / GSFC GNCD
  Team Member Certification for Operational Readiness
Collaborate Closely with Swales and Hammers
  TLM / CMD Data Base, ITOS Page and Procedure Development & Testing
  Remote Probe Monitoring
Take Advantage of Lessons Learned Data Base

## Slide 27: Summary
THEMIS Operations Follow Proven FAST and RHESSI Model
  UCB Team Implemented Multi-Mission Operations Center
  Scalable Ground System Architecture Proven Very Successful
  Demonstrated Reliable Lights-out Operations for FAST and RHESSI
  High Degree of Automation Results in Low Operations Costs
  3+ Years of Ground Station Operations
  3+ Years of FAST Mission Operations
  6+ Years of FAST Science Operations
  1 Year of RHESSI Mission and Science Operations
  THEMIS Operations Concept Based on Solid Heritage
THEMIS Operations Support
  UCB Team Will Be Well Trained and Prepared to Operate THEMIS
  NASA / GSFC GNCD Maneuver Support Enlisted on Consulting Basis

## Slide 28
Backup Charts

## Slide 29: UCB Mission Operations Center
Secure 600 ft2 Facility at SSL