## Slide 1
THEMIS determines where and how substorms are triggered.
Science Overview
SEC Roadmap: “Understand energy, mass and flux transport in Geospace”
SEC Roadmap: “How does solar variability affect society?”
NRC, National Academy: A strategic question in space physics (1995).
Substorms are…
…important to NASA:
Aurora
Current disruption
Reconnection
Auroral eruptions are recurrent (~3-6hrs)
Magnetospheric substorms are responsible for auroral eruptions.
Fundamental mode of magnetospheric circulation
Important for geo-storms have societal implications.
Rich in new types of basic space plasma physics.

## Slide 2
Clearly identified the mission elements to distinguish between substorm models
Current Disruption Model of Onset |  | 
Order | Time | Event
1 | t = 0s | Current Disruption
2 | t = 30s | Auroral Eruption
3 | t = 60s | Reconnection
Near Earth Reconnection Model of Onset |  | 
Order | Time | Event
1 | t = 0s | Reconnection
2 | t = 90s | Current Disruption
3 | t = 120s | Auroral Eruption
Ground Based Observatories (GBOs) determine auroral breakup within 1-3s …
… while THEMIS’s probes (five) with orbit periods 1:2:4 days align once per 4 days over North America and determine onset of Current Disruption (“CD” at ~10RE) and Reconnection (“Rx” at ~25RE) each within <10s.
?

## Slide 3
Science Objectives
THEMIS HAS FOCUSED MINIMUM (TO BASELINE) OBJECTIVES:
Time History of Events…
  Auroral breakup (on the ground)
  Current Disruption [CD] (2 probes at ~10RE)
  Reconnection [Rx] (2 probes at ~20-30RE)
… and Macroscale Interactions during >5 (>10) Substorms (Primary):
  Current Disruption and Reconnection coupling
    Outward motion (1600km/s) of rarefaction wave
    Inward motion of flows (1000km/s) and Poynting flux.
  Ionospheric coupling
    Cross-tail current reduction (P5u/P4) vs flows
    Field aligned current generation by flow vorticity, pressure gradients (P/dz, P/dx).
  Cross-scale coupling to local modes
    Field line resonances (10RE, 5 min)
    Ballooning modes, KH waves (1RE, 1min)
    Weibel instability, cross-field current instability, kinetic Alfven waves (0.1RE, 6Hz)
Production of storm time MeV electrons (Secondary)
Control of solar wind-magnetosphere coupling by the bow-shock, magnetosheath and magnetopause (Tertiary)

## Slide 4
Probe conjunctions well understood
BASELINE: >10 substorms achieved w/ 5 probes in 2 yrs & 50% margin.
MINIMUM: >5 substorms achieved in 1yr w/ 4 probes.
computations include lunar, solar, drag, J2 terms
YP1/2/3/4/5<±2RE; ZP3,4,5/NS<±2RE; ZP1,2/NS<±5RE
Ascent design is optimal for science
maximizes conjunctions, minimizes shadows
… immune to launch insertion errors
small, piece-wise Vs increase placement fidelity
… and immune to probe insertion errors.
Can withstand insertion error of V=80cm/s on any probe
Actual conjunction times in 1st year

## Slide 5
SST
ESA
EFIa
EFIs
FGM
SCM
Heritage instruments exceed science requirements
Instruments easy to assemble and test
Fluxgate Magnetometer (FGM)
ElectroStatic Analyzer (ESA)
Solid State Telescope (SST) [Composed of 2 heads (SSTh)]
Search Coil Magnetometer (SCM)
Electric Field Instrument (EFI) [2axial (EFIa), 4spin-plane (EFIs) booms].
…place clear and simple requirements on probes
Spin period (Tspin=3s) accommodates cadence (<10s)
Attitude control (5.6o), knowledge (1o), short-term stability (0.1o) from <10% error in V, ExB, B, J
EMC, ESC, thermal requirements/verification as on FAST, POLAR, WIND, LP, etc.
Instrument Rqmts: | Mass | Power
Predict | 21.0 kg | 12.1 W
Reserve | 12.8% | 21.6%
Max expected | 23.7 kg | 14.7 W
Margin | 40.5% | 41.9%

## Slide 6
Number of instruments exceed measurement requirements
Identical instrumentation provides high science margins and fault tolerance
Instruments required to achieve Primary Mission Objective |  |  |  |  |  | 
 | Measurement goals | P1 | P2 | P3 | P4 | P5
Time History of Events | P3,4&5 monitor CD P1,2 bracket Rx tres<30s, Y<±2RE | FGM 2SSTh 2EFIs | FGM ESA 2SSTh 2EFIs | FGM ESA 1SSTh | FGM ESA 1SSTh | FGM ESA 1SSTh
Macroscale Interactions | Track rarefaction wave, inward flows, Poynting with B<1nT, V/V~10% |  | FGM ESA | FGM ESA | FGM ESA | FGM ESA
 | Radial/cross-sheet pressure, velocity and current gradients require P/P~ V/V ~ B/B ~10%, non-MHD |  | FGM ESA | FGM ESA 2EFIs | FGM ESA 2EFIs | FGM ESA 2EFIs
 | Cross-tail pairs measure FLRs, KH, ballooning on B, V, P @ 10s and fast modes on Bxyz and Exy @ 6Hz |  | FGM ESA SCM | FGM ESA SCM 4EFIs 2EFIa | FGM ESA 2EFIs | FGM ESA SCM 4EFIs 2EFIa
Instrument redundancy:
  SST-ESA energy overlap
  FGM-SCM frequency overlap
  P1/P2 redundant instrumentation (only directional flux needed in one of two).
Each probe has:
    FGM
    ESA
    2SSTh (2heads)
    SCM
    2EFIa (2axials)
    4EFIs (4spin plane)

## Slide 7
Mission elements are simple
USN
THEMIS OPS
Msn Ops
Flight Dyn
Sci. Ops
BGS Ops
BGS
FGM
IDPU
SCM
EFI
ESA
SST
BAU
P1
P2
P3
P4
P5
Sci.
Analysis
GBO
GMAG, ASI
DSN
TDRSS
NORAD
Backup
Primary
Secondary
NSSDC
Inst-I&T
UCB
Msn I&T
Swales
D2925-10
@ CCAS
Encapsulation
& launch

## Slide 8
Mission profile is robust
Pre-Launch (6hrs) | Launch (25min) |  | Check-out & ascend (60days) | Science ops (2yrs) | Re-entry
Checkout Countdown | 2nd stage burn Spin-up 3rd stage burn Spin-down | Probe dispense | Bus check-out Dply mags/check instr. Orbit place. Total of: - 6 side thrustings - 6 reor/fire/reor sequences Deploy EFI | Minor ctrl ops (all): 22 side-thrustings 2 inclination changes | Minor ctrl ops (Side-thrusts, finish by EOM+9mo) - 8 side-thrustings Passive re-entry thereafter (1-10yrs)
 |  |  | Fuel consumption, maneuvers and contacts during ascend: validated with GMAN. |  | 

## Slide 9
Question # 1: Please describe the mission profiles for each probe and for scenarios in which one probe replaces another in the constellation. Include detailed delta-v profiles for each scenario including pertinent orbital parameters. What is the operational sequence of events for moving an already-operating probe to replace a failed one?
Answer:
HIGH LEVEL NOMINAL MISSION PROFILE:
  The Probes, during all mission phases, are shown on the Mission Profile Table Poster and in your Appendix handouts (Expansion of CSR Figure F-1A) and demonstrate that THEMIS Mission Modes are well defined
  This Profile is understood across all elements of the team enabling the optimization and operational simplicity achieved during the Phase A study
  Detailed Delta-V profiles/orbit parameters for all probe scenarios shown in Appendix handout
DELTA-V PROFILE -- PROBE REPLACEMENT SCENARIO DETAILED MANEUVER AND OPERATIONAL SEQUENCE:
  The detailed Delta-V Table that follows illustrates P3 and P4; This represents the worst case energy/propellant usage scenario (i.e. replacing P1 by either P3 or P4)
  Assumes all Probes fully deployed at nominal mission orbits before P3 or P4 are “called into duty” to replace P1 (worst case operational assumption)
  Even after full replacement operations are completed, positive fuel margin still exists on the replacement probe (P3 or P4); These operations include end of mission maneuver to fully satisfy orbital debris requirements
  Operational sequence for Probe Replacement Scenario is identical to operations for other maneuvers (See answer to Question 2 that also addresses this part of Question 1)
Ans. to Q#1a. Mission & V profiles

## Slide 10
Continued:
  This table is similar to all of the Probe detailed Delta-V and orbit maneuver profiles; This replacement scenario envelopes P3 and P1’s core maneuvers as well as demonstrating the sequence of maneuvers for the Probe replacement scenario
Ans. to Q#1a. Mission & V profiles

## Slide 11
Mission design meets requirements
Mission profile
  Two year mission design easily met in this high Earth orbit
  Launch: D2925 from CCAS (40min window any day) permits 40% lift margin
  Probe carrier (3rd stage fixture) w/ flight proven release exceeds load rqmts
  Science & routine ops and multi-object tracking has ample heritage at UCB
  GN&C benefits from: simple RCS, heritage sfw, ground-cmd, GSFC support
Probe design
  Simple, passive thermal design w/ backup heaters
  Survival at all attitudes under worst shadows (thermal constant > max shadow)
  Simple data flow / automated routine science ops minimize cost and risk
    Store/Forward 375Mbit/orbit (256Mbyte capability permits multi-orbit storage)
  Orbit control & knowledge exceed rqmts by factor of 10
  Attitude control & knowledge exceed rqmts by >40%
  Early EMC/ESC mitigation as per heritage practices (e.g. FAST, POLAR)

## Slide 12
No science changes since Step 1
Detailed implementation studies during Phase A have increased margins and reduced mission risk relative to step 1.
Tail observation season centered closer to equinox (can still launch any day of yr):
  Improved substorm event yields (recurrence) by 50% resulted in:
  …minimum mission achievable with 1 yr of operations (lowered mission risk)
Orbit apogees/periods optimized (reduced risk of substorm event loss)
Prg. altitudes closer to each other and lower than step-1 (improved fuel margin)
GBO locations in Alaska/Canada optimized (local infrastructure reduced risk)
Boom design and ion ESA design optimized (heritage items reduced risk)
Commitments secured from all international institutes providing flight hardware

## Slide 13
Integrated scientist-engineer team
This is evidenced by Phase A activities:
Direct inject with passive PCA reduces schedule and ops risks
PCA dispense simplified: improves clearances, reduces risk
Increased fuel tank capacity
  Ensures P3P1 replacement even at maximum expected dry mass
  Increased fuel margin (43% for limit case: P1)
Added solar panels at bottom face
  Power positive on all attitudes
  Eliminates autonomous safe-mode reor maneuver, reducing risk
ACS solution simplified with micro-gyros replacing accelerometers
RCS propulsion pods connected:
  Passive fuel management streamlines flight operations
  Simplifies I&T, fueling ops and manufacturing process
THEMIS has a highly integrated team of scientists and engineers interacting efficiently to optimize the mission design and resources, reducing risk and ensuring mission success.

## Slide 14
Simple, robust and fault tolerant system design
+
Subsystem and institutional flight heritage
+
Emphasis on manufacturability and ease of testing
=
High probability of mission success within resources
In Summary…

## Slide 15
BACKUP SLIDES

## Slide 16
De-orbit requirements are met
Re-entry maneuver at End of Mission (EOM) is in V budget
  Re-entry of P1 after contingency replacement (by P3/4) is also in V budget.
Depletion of on-board energy sources at EOM
Exclusion zones at GEO and LEO are met
Lifetime and orbital debris analysis:
  Launch perigee ensures PC + 3rd stage re-entry
    Lifetime: 1.7-4.5yrs (depending on: DAS/GTDS, atmos. model, definitive RAP)
    Total PC + 3rd stage casualty area: 1.04 m2
  P3,4,5 probe perigees ensure short lifetime after EOM re-entry V.
    Lifetimes: 1.6-3.6 yrs (depending on: DAS/GTDS, atmos. model, EOM RAP)
    Total probe casualty area: 2.68 m2 (tanks + battery)
  P1, 2 lunar phasing (V for “ma change” at EOM) ensures re-entry
    Lifetime: 2.5-10 yrs (depending on actual lunar phase and probe).

## Slide 17
Continued: P1 ascend scenario.
Ans. to Q#1a. P1 Mission & V profile
  Calculations assume tank depletion and compute margin available
  Separate computation of ACS thrusting for reor and attitude accounted for separately
  Total margin (including ACS) is 43% (P1 is worst case of all)
  L&EO computations verified by GMAN
  Final apogee raise occurs in 2 steps (duration ~60min)
  Long duration burns occur with axial thrusting (reor/fire/reor). Short ones with side thrusting
  From P1-4 to P1-5 inclination drops to target inclination (7o) due to lunar perturbations

## Slide 18
Continued: P2 ascend scenario.
Ans. to Q#1a. P2 Mission & V profile
  Calculations assume tank depletion and compute margin available
  Separate computation of ACS thrusting for reor and attitude accounted for separately
  Total margin (including ACS) is 133%
  L&EO computations verified by GMAN
  Long duration burns occur with axial thrusting (reor/fire/reor). Short ones with side thrusting
  From P2-4 to P2-5 inclination drops to target inclination (7o) due to lunar perturbations

## Slide 19
Continued: P3 ascend scenario.
Ans. to Q#1a. P3 Mission & V profile
  Calculations assume tank depletion and compute margin available
  Separate computation of ACS thrusting for reor and attitude accounted for separately
  Total margin (including ACS) is 1000%
  L&EO computations verified by GMAN
  Inclination change occurs with axial thrusting (reor/fire/reor). Others with side thrusting

## Slide 20
Continued: P4 ascend scenario.
Ans. to Q#1a. P4 Mission & V profile
  Calculations assume tank depletion and compute margin available
  Separate computation of ACS thrusting for reor and attitude accounted for separately
  Total margin (including ACS) is 1004%
  L&EO computations verified by GMAN
  Inclination change occurs with axial thrusting (reor/fire/reor). Others with side thrusting

## Slide 21
Continued: P5 ascend scenario.
Ans. to Q#1a. P5 Mission & V profile
  Calculations assume tank depletion and compute margin available
  Separate computation of ACS thrusting for reor and attitude accounted for separately
  Total margin (including ACS) is 73%
  L&EO computations verified by GMAN
  Inclination change occurs with axial thrusting (reor/fire/reor). Others with side thrusting

## Slide 22
Continued:
  This table is similar to all of the Probe detailed Delta-V and orbit maneuver profiles; This replacement scenario envelopes P3 and P1’s core maneuvers as well as demonstrating the sequence of maneuvers for the Probe replacement scenario
Ans. to Q#1a. P3->P1 replacement

## Slide 23: THEMIS’s instruments, constellation strategy and operation plans have inherent redundancies that ensure mission success
Science requirements accommodated with robust mission design
Instrument capability overlap and identical probes permit graceful probe degradation with no effect on science closure.
MPF of 4 probes in 1 year with robust replacement capability of P1/2/3 by P3/4 ensures high reliability.
Fail-safe nature of probes and mission ops bestow THEMIS resilience:
  Ground-operated with on-board watchdog timeouts
  Control center “disaster” backup plans and multiple backup stations
  In an emergency, autonomous routine ops & multi-orbit storage:
    Permit attention to be focused on anomaly resolution
    Reduce risk of operator overload
    Guarantee science data recovery while anomaly is being resolved
No mission single point failure after D2925 orbit insertion (see fault tree diagram in CSR)
THEMIS fault-tree diagram (see CSR)