THEMIS

PARTICLES L1 Data files Variable Name Definition

THM-SOC-106

September 18, 2006

Timothy Quinn, THEMIS Science Operations

Dr. Davin Larson, THEMIS SST

Dr. James McFadden, THEMIS ESA

Dr. Charles Carlson, THEMIS ESA

Michael Ludlam, Instrument Manager

Peter Harvey, THEMIS Project Manager

Vassilis Angelopoulos, THEMIS Principal Investigator

# Document Revision Record

| Rev. | Date | Description of Change | Approved By |
| --- | --- | --- | --- |
| 1 | 2006-09-12 | Draft | - |
| 2 | 2006/09/18 | Signature Version | Signatories |
|  |  | Added Ludlam in signature list; Added ESA Modes Table |  |

# Distribution List

| Name | Email |
| --- | --- |
| Jim Lewis, U.C. Berkeley | jwl@ssl.berkeley.edu |
| Dr. Tai Phan, U.C. Berkeley | phan@ssl.berkeley.edu |
| Dr. Robert Lin, UCB | boblin@ssl.berkeley.edu |
| Dr. Manfred Bester, UCB | Manfred@ssl.berkeley.edu |
| Dr. Davin Larson, UCB | davin@ssl.berkeley.edu |
| Dr. Ellen Taylor, UCB | ertaylor@ssl.berkeley.edu |
| Dr. Dave Sibeck, NASA GSFC | david.g.sibeck@nasa.gov |

# TBD List

| Identifier | Description |
| --- | --- |

Table of Contents

Document Revision Record	2

Distribution List	2

TBD List	2

1.	Introduction	4

1.1	Purpose and Scope.	4

1.2	Applicable Documents.	5

2.	General L1DAT File Variable Naming Conventions	5

2.1	Construct of PARTICLES VARNAMES: TH[A-E]_XYZ_nnnn	5

2.2	Packet HEADERs: TH[A-E]_XYZ_HED; TH[A-E]_XYZ_nnnn_HED	5

3.	Specific PARTICLES Quantities	6

3.1	Distribution Functions (APIDs 453-45F): TH[A-E]_XYZ_nnnn	6

3.2	Moments (APID 453)	6

3.3	SST Engineering data (APID 452)	6

# Introduction

## Purpose and Scope.

THEMIS data are transmitted to the ground as Virtual Channel (VC), APplication  Identifier (APID) packets, each containing packets of a specific instrument data type from a specific IDPU instrument APID. Time-ordering of individual APID packet files, time-tagging, decompression of the IDPU post-recording compression, a small re-arrangement of quantities and possible trivial processing of raw quantities results in L0 file data. These files (herein termed APID_L0DAT.pkt) contain APID data in daily files. The APIDs are described in: thm_fsw_003_ctm_v4.013.xls (and previous versions), and are also listed below:

THEMIS Level 1 probe data (herein termed L1DAT.cdf), shall be CDF files containing the above L0 data, in principle as close to their L0 format as feasible, but with addition of metadata and time stamps that facilitate interpretation and access by the scientific community. It is anticipated that L1 files will originally contain data stemming from their individual APID files, but will eventually be merged into a single daily multi-instrument file, containing all the science APIDs for a single probe.

Generation of physical quantities from such L1DAT.cdf files shall proceed, in principle, by use of two additional files and a piece of code: A calibration file (herein termed CAL.cdf), a probe STATE file (herein termed STATE.cdf) and a piece of IDL code that reads the three files, calibrates and transforms the data into the proper coordinate system and produces physical quantities.

The purpose of this document is to define the EFI, SCM and FGM instrument L1 data file quantities and names. The overarching principle is to create short and unique mnemonics that facilitate easy understanding of the data quantities they carry, while preserving, if possible, the efficiency (and compactness) of the L0 and APID data representation.

## Applicable Documents.

- THM_SYS_012_PDMP				THEMIS Project Data Management Plan

- THM_SOC_101_TIME				THEMIS TIME Definition

- THM_SOC_105_FIELDS_L1_VARNAMES	THEMIS FIELDS Variable Name Def’s

- THM_SOC_108_GMAG_L1_VARNAMES		THEMIS GMAG Variable Name Def’s

- THM_SOC_109_ASI_L1_VARNAMES		THEMIS ASI Variable Name Definitions

- THM_SOC_110_COORDINATES			THEMIS Coordinate Systems Definitions

- THM_SOC_111_SUNSENSPROC			THEMIS SUN SENSOR Science Processing

- THM_SOC_112_ATTPAIPROC			THEMIS Science ATT & Inertia Determ.

- THM_SOC_113_FGM_CALPROC		THEMIS FGM CAL File and Processing

- THM_SOC_114_SCM_CALPROC			THEMIS SCM CAL File and Processing

- THM_SOC_115_EFI_CALPROC			THEMIS EFI CAL File and Processing

- THM_SOC_116_ESA_CALPROC			THEMIS ESA CAL File and Processing

- THM_SOC_117_SST_CALPROC			THEMIS SST CAL File and Processing

# General L1DAT File Variable Naming Conventions

## Construct of PARTICLES VARNAMES: TH[A-E]_XYZ_nnnn

Following an overall principle of naming THEMIS variables using more general to less general descriptors, separated by  the underscore character “_”, the ESA and SST variables shall be named:  TH[A-E]_ XYZ, where:  A-E is the probe letter – identifier, and “XYZ” is a descriptive ESA or SST distribution quantity identifier.

This construct works well with data products from most distribution functions and when further specificity is required in order to ensure optimal file size, such as in the number of spectral angle-energy quantities, additional descriptors _nnnn are utilized. Those unique indentifiers can be letters of numbers.

## Packet HEADERs: TH[A-E]_XYZ_HED; TH[A-E]_XYZ_nnnn_HED

Packet header information and packet time (but not packet data) shall be included in the L1 files. Such headers shall be named by appending the 3 letters “HED” to the variable name. When multiple variables were extracted from the same L0 packets, a more generic name for the packet variable shall be used, e.g., TH[A-E]_MOM_HED would describe headers for all ESA and SST moments.

# Specific PARTICLES Quantities

## Distribution Functions (APIDs 454-45F): TH[A-E]_XYZ_nnnn

ESA and SST distribution functions are transmitted in various angle-energy combinations depending on mode (survey, burst) and region (magnetospheric, shocked solar wind, and pristine solar wind). The naming convention shall be: TH[A-E]_XYZ_nnnn, where:

X({E, S} for ESA or SST

Y({I, E} for Ions or Electrons

Z ({F,R,B} for Full, Reduced or Burst distributions

nnnn is a unique identifier of the angle-energy ranges for the SST and ESA shown in Tables 1 and 2.

## Moments (APID 453)

ESA and SST moments are transmitted together in APID 453, along with the spacecraft potential. The spacecraft potential is used in the ESA moment computation for removing electron contamination.

The variable representing the moment data products shall be named: TH[A-E]_MOM and shall be a 4x13 array where:

_MOM.dat(0,*) shall be the ion ESA moments

_MOM.dat(1,*) shall be the electron ESA moments

_MOM.dat(2,*) shall be the ion SST moments and

_MOM.dat(3,*) shall be the electron SST moments.

The variable representing the spacecraft potential that was used for the moment computation shall be in variable: _MOM_POT, a time-varying quantity of type R*4

The variable representing the status shall be _MOM_QF, a 1 dimension, 2 BYTE array, representing the  SST data valid (_MOM_QF.dat(0); bit=1) and ESA data valid (_MOM_QF.dat(0); bit=0).

## SST Engineering data (APID 452)

Data shall be contained in a variable named: _SST_ENG which will represent a time varying, 1 dimensional, 256 BYTE array. Header information shall be contained in _SST_ENG_HED and header time shall be in _SST_ENG_HED_TIME